## Slide 1
Puneet Jain
SA2 Chairman, Intel
SA2 Moderated Email
Discussion Agreements

## Slide 2: ATSSS Open Issues
Moderator Summary and Proposed Way Forward are available here [Link]
Working Agreements
  During the UE registration, the serving AMF shall inform the UE with network indication for the support of ATSSS, if supported.
  AMF shall always notify the UE for the ATSSS Network Capability whenever the UE switches RA.
  During the N2 mobility handover or idle mode mobility for MA PDU session, when network detects that the destination network no longer supports ATSSS, the MA PDU session shall be released by the AMF.

## Slide 3: eNA Open Issues
Moderator Summary and Proposed Way Forward are available here [Link]
Working Agreements
  Abnormal behavior related network data analytics for target of analytics reporting being “any UE” will be supported.
  Solution on how to alleviate heavy load caused by a request for abnormal behavior analytics for “any UE” to be further discussed.
  Comment from Chairman: Can all of above supported with enough time for stage-3 work before Rel-16 freeze in June 2020?

## Slide 4: Vertical_LAN Open Issues (1/2)
Moderator Summary and Proposed Way Forward are available here [Link]
Working Agreements
  Support for PSFP based Hold and Forward Buffering rule
    Given no clear majority this functionality will not be is not supported in Rel-16.
  VLAN ID configuration for bridge management
    Option #2 (OA&M configuration of allowed versus forbidden VLAN IDs across all TSN bridges – NW-TT, DS-TT, IEEE TSN network) shall be supported.
    Should option #1 (dynamic exchange of forbidden VLAN IDs or allowed VLAN IDs) also be supported as an option?
  Assumptions on the number of ports per NW-TT within the UPF
    Option A (There is only one NW-TT per UPF. Each NW-TT can have one or more ports) shall be supported.
  System Configuration that is not PDU Session specific
    NEF procedure for invoking system configuration that is not PDU Session specific will not be introduced in Rel-16.

## Slide 5: Vertical_LAN Open Issues (2/2)
Moderator Summary and Proposed Way Forward are available here [Link]
Working Agreements
  Support for CAG specific Access control
    SA2 should not respond to question directed to SA1.
    Response to Question 1.1 in LS (S2-2002656): No, the UE cannot camp in manually selected CAG ID if it is not present in Allowed CAG list after registration.
    Response to Question 1.2 in LS (S2-2002656): No need to support any prioritization of CAG IDs.

## Slide 6: MT-EDT Open Issues
Moderator Summary and Proposed Way Forward are available here [Link]
Working Agreements
  Send LS to SA and relevant working groups (CT1, RAN2, RAN3, SA3) informing that there is no consensus in SA2 on specifying any solution for MT-EDT support in 5GC (in Rel-16). Provide high level summary of discussions in the LS as appropriate.

## Slide 7: FS_5G_ProSe Open Issues
Moderator Summary and Proposed Way Forward are available here [Link]
Agreements
  Service continuity for UE-to-Network Relay is in scope of FS_5G_ProSe SID and time will be allocated to discuss solutions to KI#3 in the TR 23.752.

## Slide 8: ETSUN Open Issues
Moderator Summary and Proposed Way Forward are available here [Link]
Working Agreements
  In this release of the specification, deployments topologies with specific SMF Service Areas applies only for 3GPP access
  In this release of the specification, ATSSS assumes SMFs Service Areas covering the whole PLMN

## Slide 9: eSBA Open Issues
Moderator Summary and Proposed Way Forward are available here [Link]
Working Agreements
  Specify HTTP/2 request message routing between multiple SCPs.
  SEPP aspects should not be specified in this release of the specification.
  Instance selection shall be performed either at NF service consumer or at last SCP in the path.
  Dynamic information about SCP availability should be supported.
  only address discovery of next-hop SCP to be supported.
  NF should not be aware that multiple SCPs are deployed.
  Comment from Chairman: Can all of above supported with enough time for stage-3 work before Rel-16 freeze in June 2020?