## Slide 1: MUSIM Way Forward
MediaTek Inc.
3GPP TSG SA2#140E S2-2005504
August 19 – September 2, 2020 Agenda Item 8.10

## Slide 2: MUSIM Way Forward MediaTek recommendations
General:
  Simple solutions with no unnecessary flexibility
  No specification of solutions relying on non-3GPP access
  No specification of solutions requiring an additional network node not otherwise required for 3GPP access (as of Rel-15); no unnecessary feature dependency
Key Issue #1 – Handling of MT Service (paging during ongoing service)
  Solution #1 allowing introduction of new Paging Cause (applicable in RRC Inactive, RRC Idle). Paging Response subject to UE implementation.
  No new AS gaps necessary. This is a RANx discussion i.e. no SA2 request on this matter.
  No need identified for “busy indication” (can be discussed in RAN) or for paging response timer
  Paging filtering solution#10 is incomplete and not suitable for decision right now (what the paging filter is is very unclear)
Key Issue #2 – Enabling paging reception (paging collisions)
  Solution #19 as an implementation option (no standardization necessary)
  Solution #20. Also open to UE ID recommendation from the UE to the network in MRU if deemed necessary.
  No paging-specific ID (5GS). No change to PO calculations (AS impact)
  EPS: IMSI offset can be considered due to the use of a permanent identity
  No “notification” for paging (i.e. via ePDG, N3IWF, external paging server, SMS)
Key Issue #3 – Coordinated leaving & resumption
  Solution #22 as the simplest and most efficient approach to serve as baseline i.e. systematic AS-triggered leaving in 5GS – the same solution could be applied in E-UTRA if acceptable in RAN
  LS to RAN2 to request considering RRC-based approach in E-UTRA

## Slide 3: Key Issue #1 Handling of MT service
Solutions | Comments
Solution #1 Paging Cause | Identification of the reason for paging without RRC conn. establishment thus resolving a key issue on the field today No user interaction at paging
Solution #2 Short absence | AS-centric solution RAN to investigate (contribution driven). No request from SA2
Solution #3 Busy indication | Avoids further paging a temporarily busy UE Requires “busy state” and means to leave the busy state (timer/explicit signaling) Temporary only i.e. requires repeated transactions Requires responding to paging that may simply not be possible (e.g. during ongoing voice call) thus not resolving the problem on the field today
Solution #7 Push notification via Paging Server | Tackles the key issue Requires introduction of a paging server and rather substantial complexity for issuing PLMN A pages over PLMN B’s Uu interface and handling either a specific always-on connection in PLMN B or repeated “paging registration” PLMN A Paging gets charged (billed) in PLMN B to the user
Solution #8 Push notification via N3IWF | Similar to solution 7 in terms of impact/complexity Requires N3IWF deployment that is not otherwise required except for untrusted N3GPP access or indirect SNPN access
Solutions | Comments
Solution #9 Preferred number list | Builds on top of Solution #1 adding black/white list of MSISDNs or SIP URIs – and corresponding handling at DSCP (i.e. different values depending whether the number is preferred or not) Requires user interaction not otherwise required today and related “education” (i.e. only applicable with one SIM in connected mode)
Solution #10 Paging filter | The solution is way too high level right now i.e. unsuitable No definition of: paging filter granularity and rules Requires user interaction not otherwise required today and related “education” wrt meaning/applicability of the filter
Solution #11 Paging response T | Forces a paging response, which inherent to the key issue, may not be possible (e.g. during ongoing voice call)
Solution #12 Paging notification via SMS | SMS is clearly not suited for “real-time” transactions Potential security issue: rogue UE1 indicating MSISDN of a target UE2 making e.g. UE2 unavailable
Solution #13 Paging notification via ePDG/N3IWF | Similar to solutions 7&8 in terms of impact/complexity

## Slide 4: Key Issue #2 Enabling paging reception (Paging Collisions)
Solutions | Comments
Solution #7 Push notification via Paging Server | Tackles the key issue See previous slide
Solution #12 Paging notification via SMS | Tackles the key issue See previous slide
Solution #14 Changing NAS parameters (requests 5G GUTI) | Prevents collisions Changes to Registration Complete to request a new GUTI are unnecessary. Changes to UCU are unnecessary. Registration Request with indication for non-colliding 5G-GUTI is sufficient.
Solution #15 Alternative UE ID for paging | Prevents collision Requires allocation of some additional Paging ID and corresponding changes to PO calculations – this is not deemed necessary in 5GS (except for EPS given PO is based on IMSI which is permanent)
Solution #16 EPS IMSI offset | Prevents collision (EPS only scenario) Not necessary when one SIM is on 5GS
Solutions | Comments
Solution #17 MUSIM Assistance | Similar to Solution #15 Alternative UE ID only for paging is unnecessary in 5GS Changes to Service Request not deemed necessary
Solution #18 Consecutive POs | AS-centric solution RAN to investigate (contribution driven) No request from SA2
Solution #19 MRU | Tackles the key issue by preserving paging success rate Relies fully on UE implementation to alternate paging reception between USIMs – no specification work needed (other than e.g. a NOTE to reflect it can occur in the field)
Solution #20 MRU Trigger | Prevents collisions Relies on MRU security principles to reassign 5G-GUTI Indication in Registration Request may be necessary (stats)
Solution #21 Scheduling gap | AS-centric solution RAN to investigate (contribution driven) No request from SA2

## Slide 5: Key Issue #3 Coordinated leaving and resumption
Solutions | Comments
Solution #4 NAS-triggered leave with local release | Tackles the key issue Similar principle in 5GS and EPS Brings the UE to idle mode Solution #4 was extended to include RAN/UE negotiation of local AS release which was not in the original proposal (i.e. suspend or local release) – this is not deemed necessary. The extension includes flexibility that is not addressed i.e. decision criteria for the UE to trigger NAS or AS release
Solution #5 NAS and AS release depending on long/short leave | Tackles the key issue Two-level flexibility adds substantial complexity with no clear benefit i.e. AS vs NAS mechanism and short vs long leave Criteria for short/long leave are not deterministic (i.e. only best guess) Simplified approach recommended in Solution #22
Solution #6 AS release with suspend/release | Tackles the key issue Unclear what the distinction is vs other proposals. Data handling unclear
Solution #22 AS leaving | Tackles the key issue – simplest proposal Systematic UE-triggered AS-triggered release allowing transition to idle/inactive under network control. Timer-based allowing UE leaving without explicit NW order. Gradual release of all resources Applicability to E-UTRA can be discussed in RAN
In EPS unless E-UTRA changes are possible (currently excluded in the RAN MUSIM WI), only a NAS solution is possible
MediaTek preference is for a systematic mechanism always triggered at RRC by the UE i.e. no flexibility to trigger the release at AS or NAS, as shown in solution #22
  OK to consider the same proposal for E-UTRA (LS to RAN2 necessary given RAN WI scope)
  Simplest proposal