## Slide 1
Hold and Forward Buffering in R17 TSC
Nokia, Nokia Shanghai Bell
S2-2007749

## Slide 2
Status with Hold and Forward Buffering
23.700-20 Key Issue #3A and Solution #5
Key issue #3A says
  Ability for AF to request absolute delay and jitter requirements, and mechanisms to enable the PCF to determine the 5GS QoS parameters based on the requirements received from AF.
  How to enable an application and 5GS to agree on a TSC configuration that addresses the applications needs and can be supported by 5GS.
Solution #5 proposes jitter elimination by Hold and Forward (H&F) Buffering
  H&F is implemented in UE for DL traffic and UPF for UL traffic
  Applicable for periodic traffic for which AF provides Burst Arrival Time and asks for guaranteed absolute delay
  Comparable to Rel 16 TSN DS-TT and NW-TT buffering but generalized for non-TSN cases
Two editor’s notes are present in Solution #5 related to H&F buffering
  Editor's note: Whether and how to apply Hold and forward buffers for IP PDU Sessions and Ethernet PDU sessions if CNC is not present is FFS.
  Editor's note: How the parameters for H&F buffering are created and sent to the UE and UPF is FFS.

## Slide 3
Addressing EN on whether and how to apply H&F
Use cases for Hold and Forward Buffering
Making current and legacy industrial applications wireless with 5G using Ethernet or IP
  Many current and legacy industrial applications are completely intolerant to jitter as they are used to operating over jitter free networking such as various field buses or specialized Ethernet based networks (EtherCAT, etc.)
  5G can support them ”indirectly” via IEEE TSN integration but this may be a heavy path for many deployments, particularly for those cases where IEEE TSN networking is not otherwise required
  H&F as part of 5GS natively would allow support for such applications also over non-TSN Ethernet and IP based connectivity, providing a potentially easier upgrade path to 5G based wireless connectivity
Providing low or controlled jitter for demanding modern applications
  Most modern IP based applications (VIAPA, AR, VR, gaming) have their own jitter elimination capabilities at the receiving endpoints, but they also benefit if the network can guarantee zero or low jitter, as they can tune their buffer sizes with that knowledge
  Special 5G integrated devices could even totally ”offload” jitter management to the 5G module within the device
  The 5GS can introduce jitter that far exceeds the wired network because favourable scheduling opportunities enable packet delivery in a fraction of the PDB.
UE-UE communication with 5GS based optimized forwarding
  H&F at UPF for uplink traffic may be needed to provide reasonably accurate BAT/TSCAI for the downlink

## Slide 4
Consequences of Not Supporting HnF Buffering
In the absence of an IEEE TSN DN (supporting 802.1Qbv, Qci, Qcc, etc.) deployed with the Fully Centralized Model, the 5GS will be incapable of efficiently supporting applications where limits on 5GS jitter are required.
  The 5GS can introduce jitter up to the AN-PDB, which far exceeds jitter introduced by a non-TSN wired network. Simpler network solutions to support deterministic applications that do not require upgrading the DN to support IEEE TSN are precluded, hindering 5GS deployment for IIoT and other applications that cannot tolerate the jitter introduced by the 5GS.
Support for non-Ethernet applications that require deterministic networking is precluded.
To achieve limits on jitter in the 5GS, the AN-PDB for an application must set to the jitter requirement, wasting RAN resources.
  Unrealistic for the jitter requirements of many applications.
  Example - if required 5GS delay is 10 msec and jitter must be limited to 0.5 msec, AN-PDB must be set to ~0.5 msec since a "favorable" RAN scheduling opportunity can result in packet delivery much faster than the AN-PDB.

## Slide 5
When IEEE TSN is not needed
HnF Buffers to Support Deterministic Applications
5GS (especially AN) introduces jitter orders of magnitude greater than a non-TSN DN
Only option to limit jitter is the 5GS TSN bridge, which requires an IEEE TSN DN with fully centralized configuration.
Precludes supporting applications that require deterministic networking but not IEEE TSN.
Non-TSN wired network jitter on the order of microseconds (eg: GigE 802.1Q)
Uu Jitter up to the AN-PDB is introduced
DN / Bridges / Routers
End-station
End-station
UE/DS-TT
UPF/NW-TT
RAN
DN / Bridges / Routers
End-station
End-station
UE/DS-TT
UPF/NW-TT
RAN
AF/NEF
Why HnF Buffers?
HnF Buffer Configuration
HnF Buffers can be Configured by the AF using the PMIC
But Rel. 16 PMIC for HnF buffer configuration is provided by CNC using IEEE TSN managed objects that are only available with fully centralized IEEE TSN
Instead AF/NEF can send include the TSC Assistance Container in the PMIC
  Contains BAT, PDB and Burst Spread which the DS/TT or NW-TT can use to determine HnF Buffer timing
PMIC
PMIC

## Slide 6
Addressing EN on how H&F parameters are sent to UE and UPF
How to Configure Hold and Forward Buffering
Option 1: H&F buffers are configured using the Traffic Pattern parameters (Burst Arrival Time (referenced to the 5GS ingress as in Rel. 16), the flow Periodicity and flow direction) TSC Assistance Container, as was proposed in SA2 #140E S2-2005738.
The UE/DS-TT or UPF/NW-TT may calculate Hold and Buffer parameters using the PMIC provided information and QoS flow parameters.
    HnF_Open_Time = BAT + PDB + UE Residence Time + n*Periodicity + Burst_Spread
    HnF_Close_Time =HnF_Open_Time + Window
Option 2: H&F buffers are configured according to R16 IEEE Qbv parameters, possibly only for Ethernet PDU Sessions. Since there is no CNC, it is the responsibility of the AF/NEF to construct the 802.1Qbv managed objects which are transferred in the PMIC as in Rel. 16.
Gate Control Parameters in PMIC
Notes: Table 5.28.3.1-1, and are reproduced below.
Table 6.5.2.1-1: Gate Control Parameters in PMIC

## Slide 7
Way forward proposal
Include H&F capability at both UE (for DL) and UPF (for UL) for both Ethernet and IP PDU sessions.
Preferred way forward will be Option 1 to avoid imposing the need to convert to Qbv Parameters;
However if this is not agreeable, Option 2 should be supported at the minimum for all ETH PDU sessions.