## Slide 1: FS_MUSIM teleconference
Samsung
(September 24th 2020)

## Slide 2: Agenda
  MUSIM Assistance Information (content and whether/how/when it is used), paging filtering (content and whether/how/when it is used)
  Notification type of solutions (7, 8, 12, 13, 27)
  Various add-ons (different Paging Cause (9), upper bound timer (11))
  Optimizations for “on the same network” (24, 26) or in presence of non-3GPP access (23, 25)
  Other

## Slide 3: Paging filtering (content and whether/how/when it is used)
  When used(examples):
  IDLE mode*(UE_1) + IDLE mode(UE_2): We don’t see a need for paging filtering nor leaving procedure, UE is expected to be open to receive all services.
  Connected mode(UE_1) + IDLE mode(UE_2): If UE wants to switch the service from UE_1 to UE_2, UE_1 is expected to execute leaving procedure for example sol#5. i.e. to inform the network in connected mode that its not available to receive downlink data further.
  IDLE mode(UE_1) + IDLE mode(UE_2): If UE_2 wants to start the service, UE_1 can indicate to network that its not reachable following principles of Paging filtering(sol#10) over 3GPPA or N3GPPA to save network_1 resources.
  *Idle mode above also includes the case of INACTIVE state.
  Content:
  MUSIM AI is common between leaving procedure(e.g. sol#5) and Paging filtering(sol#10)

## Slide 4
MUSIM Assistance Information (content and whether/how/when it is used)
MUSIM AI
PDU session ID(s)
Paging causes
N3GPPA paging
Timer
MUSIM AI is provided by UE when it is leaving the network over 3GPPA either in IDLE mode (following principles of sol#10) or in connected mode (e.g. sol#5). i.e. whenever UE is not reachable over 3GPPA for some or all the services to save network resources. If MUSIM AI is not included all the services are blocked when leaving procedure is executed, network will wait for resume procedure for resumption of services.
PDU session ID(s) : The list of PDU session ID(s) for which UE will respond to paging message. If not included UE will not respond for paging of any downlink data packet.
Paging causes: List of paging causes UE shall respond to paging. If not included UE will not respond for any paging cause.
N3GPPA paging: If registered on same PLMN for both 3GPPA and N3GPPA, UE guides network to page(i.e. send NOTIFICATION message) the UE only on N3GPPA taking into account other MUSIM AI.
Timer : Indicates the duration UE will not be able to receive the paging message taking into account other MUSIM AI. After its expiry services are automatically resumed. In worst case:
  If UE is able to receive the service before timer expires , due to change in conditions of the UE, UE will execute resume procedure.
  If UE is not able to receive the service after timer expires too, due to change in conditions of the UE, UE will re-execute the leaving procedure following principles of sol#10.
  If timer is not included then network is mandated to wait for resume procedure from the UE to resume the operations.

## Slide 5: Agenda 1: Notification type of solutions (7, 8, 12, 13, 27)
  Samsung supports solution#8 mainly because it utilizes existing architecture.
Agenda 3: Various add-ons (different Paging Cause (9), upper bound timer (11))
Paging causes: We think we have spent good amount of time and understood different company positions. Thus prefer to not spend more time in this call. Our position is same from last meeting for different paging causes.
Upper bound timer(solution #11): We support the motivation of the solution but we think this should be discussed directly in CT1 because it’s a protocol issue and not architecture issue.
Agenda 4: Optimizations for “on the same network” (24, 26) or in presence of non-3GPP access (23, 25)
Samsung supports solution 24,26. Mainly because just by enhancing the knowledge of the network that both USIMs belongs to same UE and minimal changes, it can solve both KI#1 and KI#2. Working offline to explore possibility of merging solution 24 and 26.
Solutions 25: Discussed as part of MUSIM AI in slide 2 called as “N3GPPA paging”

## Slide 6: Agenda 5: Others
  Questions on conclusion pCRs for upcoming meeting(s):
  Should we again(similar to last meeting) aim for merging of all conclusion papers in single tdoc and work on revisions during the meeting –or- we should aim to have separate conclusion papers?
  Samsung view:
    What we did in last meeting was fine for interim conclusions and evaluations. But if we follow same thing in future meetings for final conclusions, our concern is, we may end up having different branches of revisions of same tdoc, based on different company positions. This different branches may never get stabilized.
    We think we should work on separate conclusion papers depending on positions. So that at the end we have stable conclusion pCRs. Which in worst case can go for show of hands and conclude a given KI#.

## Slide 7: Thank You !!