## Slide 1: FS_IIoT Show of hands questions
Nokia (Rapporteur)

## Slide 2: Key Issue #1 Uplink Time Synchronization
Background
  There are 4 methods documented as part of solution #1 to support BMCA for Time Synchronization. Need to pick one Method as way forward.
  Method 1 – TSN AF determines the port role, announce message is forwarded over CP (C-plane based).
  Method 2 – NW-TT determines port roles; DS-TT forwards all announce messages, U-plane.
  Method 3 – NW-TT determines port roles; If message Priority Vector is better than the current Port Priority Vector, DS-TT forwards announce, U-plane
  Method 4 - NW-TT determines port roles; NW-TT forwards announce message on behalf of DS-TT, U-plane.
Way forward: <>

## Slide 3: Key Issue #2 UE-UE TSC Communication
Background
  Item 1: Varying views on support for UE-UE communication for IEEE TSN bridge with or without any pre-configuration.
Questions:
  Options for item 1:
    Option 1: Allow UE-UE communication, 5GS acting as IEEE TSN bridge supported only if they are configured as part of 5G VN group.
    Option 2: Allow UE-UE communication considering AF request for QoS, as long as they are within the same 5GS acting as IEEE TSN Bridge for ETH PDU Sessions.
    Option 3: Allow both options – option 1 & 2.
  Way forward: < >

## Slide 4: Key Issue #2 UE-UE TSC Communication
Background
  Item 2: Varying views on how the local switching within UPF should be controlled.
Questions:
  Options for Item 2:
    Option 1: Local switching within UPF is autonomously determined based on MAC learning and IP routing* knowledge. When local switching is performed, QoS updated considering AF request for listeners and talkers.
    Option 2: Local switching within UPF is controlled via N4 (FAR/PDR) rules. When local switching is performed, QoS updated considering AF request for listeners and talkers.
    Option 3: Allow both options
    Way forward: < >
* in case of IP@, it is about knowing target UE’s IP prefix for routing

## Slide 5: Key Issue #3A Support for deterministic services
Background
  Support for H&F for ETH (non-IEEE TSN) PDU Sessions.
  Support for H&F for IP PDU Sessions.
Questions:
  Should we support H&F for ETH (non-IEEE TSN) PDU Sessions? (YES/NO)
  Options to support H&F for ETH (non-IEEE TSN):
    Option 1: With Rel-16 Qbv parameters
    Option 2: With TSCAI parameters
    Option 3: Option 1 or Option 2 is fine.
  Should we support H&F for IP (non-IEEE TSN) PDU Sessions? (YES/NO)
  Options to support H&F for IP (non-IEEE TSN):
    Option 1: With Rel-16 Qbv parameters
    Option 2: With TSCAI parameters
    Option 3: Option 1 or Option 2
  Way forward: < >

## Slide 6: Key Issue #3B Exposure of TSC services Exposure of Time Synchronization
Background
  Conclusion has the following:
  Editor's note: whether there is a need to include validity time for AF time sync request is FFS. Also, how to support validity time is FFS.
  Options
  Option 1: AF assumed to activate and deactivate requests (thus maintain validity period accordingly).
  Option 2: AF provides validity period for the request, 5GS maintains the validity period (i.e. deactivates the request when the validity period expires).