## Slide 1: Study on Architecture Enhancement to support Ranging-based Positioning and Services
S2-2100979
Xiaomi

## Slide 2: Definition of Ranging
Ranging refers to the determination of the distance between two UEs and/or the direction of one UE, i.e. target UE, from the other one, i.e. observer UE, via direct communication connection.
  Relative positioning between 2 UEs can be derived based on ranging
The observer UE has a zenith and a reference direction, and its reference plane is the plane orthogonal to the zenith.
The direction of the target UE to the observer UE is represented by the Azimuth direction and the Elevation direction.
  Azimuth direction: the angle formed between a reference direction and a line from the observer UE to target UE projected on the reference plane of the observer UE.
  Elevation direction: the angle above the reference plane of the observer UE.
Source: TR 22.855

## Slide 3: Use case 1 Smart Home TV control
Both UE and smart TV have ranging capability
Ranging of UE to the TV reference point
  Distance: d
  Azimuth direction: a1
  Elevation direction: e1
Ranging of TV reference point to the UE
  Distance: d
  Azimuth direction: a2
  Elevation direction: e2
With (a1, e1), (a2, e2), and d, the smart TV can calculate to derive where to place the curser on the screen and can determine which content the user selects
Sports
News
Movies
Education
Game
Shopping
TV reference point

## Slide 4: Use case 2 Remote Access Right authorization
CICI’s door, Alice’s UE and Bob’s UE are all ranging capable
Alice is a visitor of CICI building, who has no access right of the door.
Bob, who is a CICI stuff, triggers ranging service to monitor ranging of Alice’s UE to the door.
When Alice’s UE is in 10cm distance to CICI’s door, Alice is authorized the access right.

## Slide 5: Use case 3 Museum Tour
Under each painting in the museum, there’s an IoT device which is ranging capable
The Museum Tour Server monitors ranging of the IoT device of each painting to the UE.
When UE moves close (<5m), points to “The Starry Night” and triggers ranging service, Museum Tour Server knows the ranging result and plays the introduction of “The Starry Night” to the UE, because the Azimuth direction < 10 degree, and the Distance < 5m.
UE reference direction
Azimuth direction < 10 degree
Distance < 5m
5GS
Museum Tour Server

## Slide 6: Use case 4 Pets positioning based on energy efficient ranging
Jerry (Tom’s pet dog), wearing a smart dog collar, was lost in a place far away from Tom. The smart dog collar is a ranging capable IoT device powered by a coin battery
Tom couldn’t get Jerry’s location using LCS service, which is not supported by the smart dog collar, and there’s no network coverage.
Jerry was discovered by Tom’s Drone, which is ranging capable and is under the network coverage.
The Drone reported to Tom’s smart phone (Drone controller) its location (based on Location Service) and Ranging result of Jerry’s smart ranging capable IoT device.
Tom’s smart phone derived the location of Jerry based on Drone’s location and Jerry’s ranging result to the Drone, and then Tom found Jerry.

## Slide 7: Use case 5 Immersive sound based on coordinated ranging
Speaker A/B/C and Tom’s cell phone are ranging capable. No-LoS paths are between Speaker B & Tom’s cellphone and between Speaker B and Speaker A.
Speaker A determines the relative position of speaker B through coordinated ranging with speaker C, i.e. Speaker A uses the ranging result of Speaker A to Speaker C, and the ranging result of Speaker B to Speaker C to calculate/calibrate/corroborate the ranging result of Speaker A to Speaker B.
Speaker B also determines relative position of Tom using the same mechanism.
The speakers adjust the sound field to provide an immersive audio experience to Tom.

## Slide 8: Scenario
Ranging-based positioning and services can be supported with or without 5G coverage.
If licensed band is used, it shall be fully under operator control.
Source: TR 22.855

## Slide 9: Related study in SA1
The SA1 SID Ranging (SP-200575) has reached 80% completion up to SA#90e.
  Functional requirements and Performance requirements that have architecture impact are identified
TS 22.186 (Enhancement of 3GPP support for V2X scenarios) has required that “The 3GPP system shall support relative lateral position accuracy of 0.1 m between UEs supporting V2X application.
  This is a R16 requirement, however, it has not been realized in R17.

## Slide 10: Authorization, Provisioning and Privacy
The 5G system shall be able to support ranging service authorization for a UE or a group of UE.
The 5G system shall be able to support ranging service policy/parameter provisioning for ranging device discovery and service execution.
The 5G system shall be able to protect privacy of a UE and its user, ensuring that no identifiable information can be tracked by undesired entities during Ranging.
The 5G system shall be able to ensure that user privacy is not violated during Ranging service, e.g., based on regulatory requirements.

## Slide 11: Ranging device discovery and service execution
The 5G system shall be able to support for a UE to discover other UEs supporting Ranging.
The 5G system shall be able to enable or disable the Ranging service based on e.g. UE presence in a specific area required by the ranging service.
The 5G system shall support mutual ranging, i.e. the two UE’s involved shall be able to range each other.

## Slide 12: Coordinated ranging among multiple UEs
The 5G system shall support coordinated ranging among multiple UEs, e.g., UE 1 can determine the distance and angle to UE 2 with no LOS path with the help of UE 3, which has LOS with both UE 1 and UE 2.
The 5G system shall support a UE initiating discovery of one or multiple UE(s) to assist with coordinated ranging of a target UE.
The 5G system shall provide a mechanism for UE to identify UEs who can assist with ranging a target UE.
The 5G system shall support transferring sufficient information from UEs participating in coordinated ranging so that the UEs can calibrate ranging measurements.

## Slide 13: QoS Handling
The 5G system shall be able to handle QoS requirements for different use case scenarios (i.e. ranging accuracy, availability, latency, effective ranging distance, coverage, NLOS/LOS, relative UE velocity, ranging interval, number of concurrent ranging operation for a UE, number of concurrent ranging operation in an area) based on stage 1 performance requirements.

## Slide 14: Ranging service exposure
The 5G system shall be able to support one UE initiates ranging service to the other UE.
The 5G system shall allow ranging service between 2 UEs triggered by and exposed to a third UE.
The 5G system shall be able to support ranging service exposure to the 3rd party application server.

## Slide 15: Energy efficiency
Since the ranging measurement at the UE consumes power, for low power consumption ranging UEs, the 5G system shall support energy efficient UE ranging services and operation.

## Slide 16: Roaming and Interworking
The 5G system shall be able to provide ranging service to roaming UEs.
The 5G system shall be able to support ranging service between UEs which subscribe to different operators.

## Slide 17: Operator control, management and charging
The 5G system shall be able to ensure that the use of ranging, if in licensed spectrum, is only permitted in network coverage under the full control of the operator who provides the coverage.
The 5G system shall be able to support charging for the usage of ranging service in licensed spectrum.

## Slide 18: Related Study in RAN2
FS_NR_pos_cov (RP-201518, Study on scenarios and requirements of in-coverage, partial coverage, and out-of-coverage NR positioning use cases) R18 SID approved to study on positioning use cases, requirements and scenarios for V2X and public safety UE in in-coverage, partial coverage, and out-of-coverage
Similar architecture enhancement to 5GC as that of supporting Ranging-based Positioning and Services is foreseen.
It is proposed to develop a common architectural enhancements to 5GC for V2X and public safety UE use cases as well to avoid potential divergence or overlapped work.

## Slide 19: Conclusions
A SID is needed in SA2 to enable Ranging-based positioning and services over sidelink for commercial, V2X and public safety use cases in in-coverage, partial coverage, and out-of-coverage of 5G network, with the following architectural considerations:
  Overall architecture reference model
  Service authorization and policy/parameter provisioning for a UE or a group of UE
  Assurance of UE Ranging privacy;
  Ranging device discovery and service execution between 2 UEs and coordinated ranging among multiple UEs to enable ranging between UEs with no LOS path;
  QoS handling for different use case scenarios based on stage 1 performance requirements, in terms of ranging accuracy, availability, latency, effective ranging distance, coverage, NLOS/LOS, relative UE velocity, ranging interval, number of concurrent ranging operation for a UE, number of concurrent ranging operation in an area;
  Ranging service request initiation and service exposure;
  Energy efficient UE ranging services and operation for low power consumption UEs;
  Enabling ranging service between UEs subscribed to different operators and for roaming users;
  Operator management, control and charging for the usage of ranging service in licensed spectrum
Time schedule: TBD, to follow SA2 guidance.