## Slide 1: 5MBS: Way Forward proposals

## Slide 2: Summary of the Way Forward proposal
Topic | WF Proposal
UP Join | Remove UP join alternative in Conclusion.
MB-SMF discovery | NRF based mechanism is selected. May be revisited in normative phase if NRF is not found suitable for fast-changing information about multicast sessions. Need for addition database to hold data about multicast session to be evaluated in normative phase.
Roaming, ETSUN and National content delivery | Will not be addressed in R17.
MBS traffic over N6/N9 | Using GTP based, N9-like interface between MB-UPF and PSA-UPF as the basis. To be determined in normative phase whether PSA-UPF could optionally support N6-like towards MBSTF
Establish/Update the associated PDU session | When UE joins MBS, associated PDU session is updated with the associated QoS flow info.
UE notifie 5GC via NAS signalling | UE always notify 5GC via NAS signalling regardless of the RRC state when UE joins or leaves.
NG-RAN notify session activation to UEs | Confirm beneficial of group level session activation notification to RRC Idle UEs for 5MBS-capable RAN. SA2 normative work will be pending RAN2 confirmation and conclusion.