## Slide 1
Shared delivery establishment and subsequent signalling - For discussion

## Slide 2: Related TDOCs
Tdoc number | Title | Source | Affected clauses |  |  |  | Note | WF proposal
 |  |  | 7.2.1.3 | 7.2.1.x (shared path establishment) | 7.2.1.y path release | 7.2.1.z (deactivation) |  | 
S2-2102291 | 23.247: Update [7.2.1.3] MBS join and Session establishment procedure | Ericsson |  |  |  |  |  | Should be merged into one
S2-2102387 | 23.247: MBS Session Join and Establishment | Huawei |  (7.2.1 a few) |  |  |  |  | 
S2-2102434 | 23.247: MBS Join and Session Establishment Procedure | Tencent |  |  |  |  |  | 
S2-2102438 | 23.247: Multicast session join procedure | CATT |  |  |  |  |  | 
S2-2102675 | 23.247: [7.2.1]-UE requested session join | vivo |  |  |  |  |  | 
S2-2102797 | 23.247: Modification to MBS session join procedure | ZTE |  |  |  |  |  | 
S2-2102941 | 23.247: Shared delivery establishment and support of subsequent signalling from MB-SMF | Nokia |  |  |  |  | 7.2.1.x/y/z: should consider together with related docs. | 
Tdoc number | Title | Source | Affected clauses |  |  |  |  | Note | WF proposal
 |  |  | 7.2.3.1 | 7.2.3.2 | 7.2.3.3 | 7.2.3.4 | 4.2.x |  | 
S2-2102290 | Signaling efficiency for Shared Delivery and others | Ericsson |  |  |  |  |  | Discussion paper, (update of the docs submitted to CC#1) | 
S2-2102393 | Discussion on Signalling Efficiency for MBS solutions | Huawei |  |  |  |  |  | Discussion paper (update of the docs submitted to CC#1) | 
S2-2102356 | 23.247: Multicast session start/stop/update&activation/de-activation/modification procedures | Samsung |  |  |  |  |  | Basic procedure: activation involve SMF. | Should be merged into one
S2-2102772 | 23.247: MBS Session Activation and Deactivation | Huawei |  |  |  |  |  | Basic procedure. | 
S2-2102942 | 23.247: MBS session activation. | Nokia |  |  |  |  |  | Session activation based on option 2 of 1017: SMF provides UE list to AMF | 

## Slide 3
Shared delivery establishment
Slide added by Ericsson
We would have expected an overall discussion on the scenarios from previous meetings, e.g. how to activate a session for joined UEs in IDLE and CONNECTED, UEs joining active and inactive in sessions.
The scenario picked for comparison in this part is activation of resources for a UE joining an already ongoing (i.e. active or inactive) MBS session, which is only one aspect among many to be looked at, therefore we have major concern to take this as basis for decision.

## Slide 4: Different proposed options
Option 1: Shared delivery establishment triggered by RAN, no RAN nodes and SMFs stored in MB-SMF (Huawei)
All subsequent signalling from MB-SAMF related to multicast session (e.g. for activation and deactivation) would need to go via SMF, as MB-SMF is not aware of AMFs and NG-RAN nodes in multicast session.
Separate procedure triggered by PDU Session Modification
RAN or AMF split resource update procedures for shared delivery and PDU session during Xn/N2 HO

## Slide 5: Different proposed options
Option 2: Shared delivery establishment triggered by RAN, MB-SMF stores RAN node IDs (Nokia)
signalling from MB-SMF for activation via AMF to enable that radio areas for UEs are taken into consideration
Separate procedure triggered by PDU Session Modification
RAN or AMF split resource update procedures for shared delivery and PDU session during Xn/N2 HO

## Slide 6: Different proposed options
Option 3: Shared delivery establishment triggered by RAN, AMF stores RAN node IDs
In a variant of Option 2, AMF also stores GTP Tunnel endpoint for multicast transport and avoids signalling to MB-SMF if multicast transport is used and additional RAN nodes request shared delivery for that multicast session.
signalling from MB-SMF for activation via AMF to enable that radio areas for UEs are taken into consideration
Separate procedure triggered by PDU Session Modification
RAN or AMF split resource update procedures for shared delivery and PDU session during Xn/N2 HO

## Slide 7: Different proposed options
Option 4: AMF centric approach: AMF triggers establishment of shared delivery and stores UEs and RAN nodes in multicast session
(Ericsson)
signalling from MB-SMF for activation also via AMF
Insert SMF, AMF, MB-SMF interaction during PDU Session Modification, and use separate procedure for handling RAN response.
AMF centric for Xn/N2 HO?

## Slide 8: Different proposed options
Option 5: Signalling Piggybacked in PDU session signalling (Vivo)
All subsequent signalling from MB-SMF related to multicast session (e.g. for activation, deactivation) would need to go via SMF, as MB-SMF is not aware of AMFs and NG-RAN nodes in multicast session.
Signalling piggybacked in Xn/N2 HO

## Slide 9: Comparison of Options
 | Option 1 | Option 2 | Option 3 | Option 4 | Option 5
State about multicast session in AMF | Not required | Not required | RAN nodes | RAN nodes, UEs, MB-SMF | Not required
State about multicast session in MB-SMF | SMFs, RAN node addresses | SMFs, AMFs RAN nodes, RAN node adresses, UEs | SMFs, AMFs, RAN node addresses, UEs | SMFs, AMFs, RAN node addresses | SMFs, RAN node addresses
State about multicast session in SMF | MB-SMF, UEs, RAN nodes | MB-SMF, UEs | MB-SMF, UEs | Not required | MB-SMF, UEs, RAN nodes
subsequent direct signalling for multicast session (e.g. deactivation) from MB-SMF to RAN nodes possible | yes | Yes | Yes | Yes | yes
activation for multicast session from MB-SMF to RAN nodes | Via SMF and AMF | Via SMF and AMF | Via SMF and AMF | Via AMF | Via SMF and AMF
deactivation for multicast session from MB-SMF to RAN nodes | Via SMF and AMF | Via AMF | Via AMF | Via AMF | Via SMF and AMF
Possibility of dublicated signalling from different AMFs for same MBS session at RAN node | Only session activation | Only session activation | Only session activation | Yes (Ericson: handling straightforward) | Only session activation
Reliable exchange of unicast transport address via acknowledged messages | yes | yes | yes | no (Ericson: why not reliable?) | yes
AMF involved in session management of multicast session | no Ericsson: yes (AMF has to do this cumbersome processing of UE lists) | no Ericsson: yes (AMF has to do this cumbersome processing of UE lists) | no Ericsson: yes (AMF has to do this cumbersome processing of UE lists) | Yes (Ericsson: at session activation the AMF is relieved from UE list processing. So, this is a big advantage and along decent engineering principles. And, currently, AMF already has PDU Session info, EBI etc) | no
Same solution for shared delivery establishment when first UE is handed over to RAN node | yes | yes | yes | yes | yes
Ericsson: UE joined state in AMF can avoid UE list sent by SMF during activation and solves the scaling issues in case of large UE lists.
Ericsson: The cost is that AMF needs to be always contacted to calculate paging areas from a potentially large UE list. This is rather cumbersome design
Ericsson: The decisive comparison aspect is not how to establish finally resources but how to get into this situation
Ericsson: This was identified in the first RAN3 MBS meeting and is a stage 3 issue
Ericsson: This is a bit far-fetched aspect with some very arbitrary grounding
Eric: RAN talking to different entities !!!
Eric: RAN talking to different entities !!!
Eric: RAN talks to same entity for act and de-act

## Slide 10
subsequent signalling and other aspects
Slide added by Ericsson
In the following slides:
Option-SMF refers to SMF handling MBS Session
Option-AMF refers to AMF handling MBS Session

## Slide 11: MBS Session Activation
Option-SMF (Nokia S2-2102942)
Slide added by Ericsson
Option-AMF: MB-SMF -> AMF -> RAN (see red rectangle below)
UE
NG-RAN
AMF
SMF
MB-SMF
UE Join
MB Session Info (Join, MB-SMF ID)
NRF
Discover MB-SMF
Discovery could be done by AMF
MBS Session Establishment Request/Response
RAN resource setup
MBS Session Deactivation Request/Response
MBS Session Deactivation
MBS Session Activation Request/Response
MBS Session Activation (list of CONNECTED UEs)
Establishment
Deactivation
Activation
Group paging (MBS Session ID)
Q1: If joined UEs does not have UP in SMF, but in CONNECTED state for other reason, how would such UE be added in MBS Session in RAN?
Q2: If all joined UEs in SMF have UP activated, does it mean that no MBS Session activation message will be sent to the NG-RAN? If so, how to bring the “inactive” MBS Session in RAN to Active again?

## Slide 12: MBS Session Deactivation
Option-SMF (from S2-2101017)
Slide added by Ericsson
Option-AMF: (see red rectangle below)
Option 2
AMF
UE
SMF
MB-SMF
MBS deactivate
NG-RAN
MBS contexts and N3 may be kept for connected and inactive UEs
Variant 2c
DeActivate (MBS session id, list of NG-RAN nodes)
UE
NG-RAN
AMF
SMF
MB-SMF
UE Join
MB Session Info (Join, MB-SMF ID)
NRF
Discover MB-SMF
Discovery could be done by AMF
MBS Session Establishment Request/Response
RAN resource setup
MBS Session Deactivation Request/Response
MBS Session Deactivation
MBS Session Activation Request/Response
MBS Session Activation (list of CONNECTED UEs)
Establishment
Deactivation
Activation
Group paging (MBS Session ID)

## Slide 13: MBS Session Update (adding/deleting/modifying MBS QoS Flow)
Option-SMF: Which path to follow ?
  Path: MBS Session Activation, or
  Path: MBS Session Deactivation?
Slide added by Ericsson
Option-AMF: same path as for MBS Start/Activate/Deactivate
UE
NG-RAN
AMF
SMF
MB-SMF
NRF
MBS Session Update Request/Response
MBS Session Update
Update

## Slide 14: Other aspects
Alignment/misalignment between handling of PDU Session and handling of MBS Session ?
  SMF and MB-SMF discovery
    AMF discovers SMF for PDU Session (based on DNN, S-NSSAI, location…), while Option-SMF discovers MB-SMF for MBS Session => misalignment?
      Not future proof for ETSUN scenario, as SMF is not aware of other SMF service areas (although it’s moved out of Rel-17)
  NG-RAN info in CN
    SMF is only aware of NG-RAN tunnel entity for PDU Session, while in Option-SMF, MB-SMF will have knowledge of NG-RAN node (in addition to NG-RAN’s tunnel info) => misalignment?
  SM/MM split but AMF is already aware of session info, e.g.
    AMF handles EBI associated with QoS Flow (which is SM info),
    In NB-IoT case, AMF needs to know whether PDU Session’s UP has been established to limit the max no. of radio bearers
Slide added by Ericsson

## Slide 15: Comparison of Options considering subsequent signalling and other aspects
 | Option-SMF | Option-AMF | Comment
Consistent logic of different procedures (involved entities, failure handling possibilities etc) | No, every procedure is different, unless signaling efficiency is not considered | Consistent and signaling efficient | 
Potential issues with MBS Session activation | Yes, see Q1 and Q2 in slide “MBS Session Activation” | Not identified so far | 
UE join with only TMGI allocated | How UE can be associated with MBS Session when it’s started/estalbished is not clarified | Supported | 
Complexity to support foreseen future scenarios (e.g., ETSUN scenarios, roaming) | Expected to be very complicated unless AMF is involved | AMF selecting MB-SMF follows the same logic as for I-SMF selection | 
Slide added by Ericsson

## Slide 16
Thank You!