## Slide 1: AIS, TSCAI and TSC Assistance Container
Chunshan Xiong
chunshxiong@tencent.com

## Slide 2: TSC Assistance Container (PTP Time Domain)
Time Domain
Flow Direction
Periodicity
Burst Arrival time (Optional)
Survival Time (Optional)
TSCAI
(5GS Time)
Flow Direction
Periodicity
Burst Arrival time (Optional)
Survival Time (Optional)
BAT in TSCAI is determined based on BAT in TSC-A-C with the time drift/rateRatio, CN-PDB and UE-DS-TT Resident Time
Survival Time in TSCAI is also determined based on Survival Time in TSC-A-C with the rateRatio.
Periodicity in TSCAI = Periodicity in TSC-A-C
SMF
Observation 1: AF can directly create/generate the TSC Assistance Container and the SMF can determine the TSCAI based on TSC-A-C (both in the AFPCF and AFNEFPCF cases).
Observation 2: NEF does NOT need to create/generate the TSC Assistance Container.
Observation 3: The TS23.501/2/3 needs to be updated based on above observations.

## Slide 3: 1.AF TSC QoS
Requested 5GS delay,
Requested GFBR,
Requested MFBR,
2.NEF TSC QoS
Requested PDB,
Requested GFBR,
Requested MFBR,
3.PCF TSC QoS Rules
Requested PDB,
Requested GFBR,
Requested MFBR,
GFBR(1) = GFBR(2) = GFBR(3)
MFBR(1) = MFBR(2) = MFBR(3)
PDB(2) = PDB (3)
5GS delay(1) – (UE-DS-TT Resident Time) = PDB (2 or 3)
NEF (Untrusted AF) or PCF (Trusted AF)
Observation 4: PDB determination is NOT related with time domain(or time synchronization) but with the architecture ( with UE-DS-TT).
Observation 5: If the PCF receives the direct TSC QOS request from the AF, the PCF can determine the requested PDB based on the Requested 5GS delay and UE-DS-TT Resident Time. If there is no UE-DS-TT information, the PCF copies the PDB from the 5GS delay;  New CR
Observation 6: If the PCF receives the TSC QOS request from the NEF, the PCF copy the PDB from the NEF TSC QoS Request ;
Observation 7: For the AIS, normally, there is no UE-DS-TT is used for the cloud gaming/AR/VR, in such case, UE-DS-TT Resident Time=0, and the PCF can also copy the PDB from the direct AF TSC QoS Request.

## Slide 4: AIS and TSC and Time Synchronization
Cloud Gaming service are widely used from 4G and cloud gaming user are greater than several hundred Million user in global.
All these mobile CG users are connected to 4G and 5G without DS-TT and without time synchronization requirements.
The basic assumption for the AIS is no time synchronization is required and no DS-TT is used and Trusted AF can directly provide TSC Assistance container and QoS Requirements to the PCF with the 5GS delay = PDB.
It is allowed that the AIS can be provided in the time synchronized 5G network, e.g. the industrial AR/VR may need time synchronization. In such case, the Trusted AF can directly provide TSC Assistance container and QoS Requirements to the PCF and the PCF can determine the PDB = 5GS Delay – ( UE-DS-TT Resident Time ).
The WID of AIS focuses on the QoS-related standards.
Observation 8: The basic assumption for the AIS is no time synchronization is required and no DS-TT is used.
Observation 9: For the AIS, the Trusted AF can directly provide TSC Assistance container and QoS Requirements to the PCF with the 5GS Delay = PDB;
Observation 10: The industrial AR/VR may need time synchronization, in such case, the Trusted AF can directly provide TSC Assistance container and QoS Requirements to the PCF and the PCF can determine the PDB = 5GS Delay – ( UE-DS-TT Resident Time ).