## Slide 1
PCF authorizing MBS Session policy - For discussion

## Slide 2: Central issues
How to bring MBS service description for an MBS session from NEF/MBSF/AF to PCF?
How to handle associated QoS flows for individual fallback in policy control?

## Slide 3
How to bring MBS service description for an MBS session from NEF/MBSF/AF to PCF?

## Slide 4
Conclusions in TR 23.757
Figure 8.2.3-2: Initial Multicast group configuration via NEF
Only flow for initial configuration,
uses Service information in UDR
uses BSF to support session binding. This enables NEF to discover MB-PCF for subsequent interactions
Ericsson comment: Not yet adopted in TS
Ericsson comment: what is the subsequent interaction?

## Slide 5: Status in TS 23.247
In Clause 7.1.1.1 Initial MBS session configuration:
  It is still unclear how information for policy authorization is conveyed from NEF to PCF.
  PCF used BSF and thus performs some binding
    7. AF of content provider may provide contents for an MBS session (possibly providing information for a previously allocated TMGI; e.g. service type of either multicast service or broadcast service) to NEF. If step 1-4 has not been executed before, the AF may provide a source specific multicast address or it may request that the network allocates an identifier for the MBS session (i.e., TMGI) and its service type of either multicast service or broadcast service. MBS information may further include QoS requirements, UE authorization information (e.g. a GPSI or an External Group Id or a UE ID to identify UEs authorized to join the multicast service), MBS service area (see step 6 for detail) identifying the service scope.
    …
    9. NEF/MBSF requests MB-SMF to reserve ingress resources for a MBS distribution session and provides MBS Session ID or request allocation, and indicate its service type (either multicast service or broadcast service). It also indicates if the allocation of an ingress transport address is requested.
    The MBS service area is provided by NEF/MBSF to the MB-SMF if provided by the AF in step 7.
    10. MB-SMF updates NF profile to NRF with the serving MBS Session ID.
    11. [Optional] The MB-SMF sends SM MBS Policy Association Request to MB-PCF with the MBS Session ID, AF Identifier, and the QoS requirements.
    12. [Optional] The MB-PCF registers at the BSF that it handles the multicast session. It provides an identifier that the policy association is for multicast and the MBS Session ID, it own PCF ID and optionally its PCF set ID.
In Clause 7.3.1 MBS Session Establishment for Broadcast
  There was a desire to have common procedures for multicast and broadcast, but this is not yet implemented
  There is a direct service request from NEF to PCF
    If dynamic PCC is deployed, the steps 7a,7b, 9a and 9b are executed.
    7a. … The NEF/MBSF sends an MBS Session Start (TMGI, Service Requirement, MBS service area) message to the PCF.
    7b. The PCF responses to the NEF/MBSF.
    8. ... NEF/MBSF sends an MBS Session Start (TMGI, PCF ID) message to the MB-SMF.
    9a. [Optional] MB-SMF sends the TMGI for the MBS Session and the Service Requirement to the MB-PCF.
    9b. [Optional] The MB-PCF returns the PCC rule for the MBS Session, which the MB-SMF uses as the 5G Authorized QoS Profile for the MBS Session. If multiple MBS service requirements are received, then MB-PCF will provide multiple 5G Authorized QoS Profiles.

## Slide 6: Related TDOCs at SA2#144E
Tdoc number | Title | Source | Affected clauses |  |  |  |  |  | Note | WF proposal
 |  |  | Annex A | 9.X (General description) | 9.Y (PCF service with SMF) | 9.Z (PCF service with NEF) | 7.1.1 | 6.6 |  | 
S2-2102726 | 23.247: MBS Application and Service Configuration Options | Tencent |  |  |  |  |  |  | AF-->PCF-->MB-SMF | 
S2-2102439 | 23.247: Policy control for Multicast and Broadcast services | CATT |  |  |  |  |  |  | General description | 
S2-2102946 | 23.247: PCF service for Interactions between MB-SMF and PCF. | Nokia |  |  |  |  |  |  | Interaction between MB-SMF and PCF | Separate one
S2-2102724 | 23.247: Requested MBS QoS and Dynamic PCC | Tencent |  |  |  |  |  |  | AF-->PCF-->MB-SMF | 
S2-2102725 | 23.247: MBS Session-AMBR | Tencent |  |  |  |  |  |  | Session AMBR for MBS should be considered for individual delivery | Separate one
S2-2102947 | 23.247: NEF PCF interactions. | Nokia |  |  |  |  |  |  | Interaction between NEF and PCF | 
Tdoc number | Title | Source | Affected clauses |  |  |  | Note | WF proposal
 |  |  | 7.3.1 | 7.3.2 | 7.3.3 | 7.3.x |  | 
S2-2102728 | 23.247: Update MBS Session Establishment for Broadcast procedure | Tencent |  |  |  |  | AF-->PCF-->MB-SMF | 
S2-2102729 | 23.247: Update MBS Session Update for Broadcast procedure | Tencent |  |  |  |  | AF-->PCF-->MB-SMF | 
S2-2102730 | 23.247: Update MBS Session Release for Broadcast procedure | Tencent |  |  |  |  | AF-->PCF-->MB-SMF | 
Tdoc number | Title | Source | Affected clauses |  |  |  |  | Note | WF proposal
 |  |  | 7.1.1 | 7.1.2 | 7.1.1.x de-configuration | 7.1.1.y configuration update | 7.2.1.3 |  | 
S2-2102354 | 23.247: Update on common procedures for multicast and broadcast services | Samsung |  |  |  |  |  | Adding de-configuration and configuration update procedure | Should be merged into one
S2-2102392 | 23.247: Updates for MBS session configuration | Huawei |  |  |  |  |  | Timing of establishing N6 connection | 
S2-2102437 | 23.247: Procedures of configuration for MBS | CATT |  |  |  |  |  |  | 
S2-2102673 | 23.247: [7.1.1]-Update to configuration procedures | vivo |  |  |  |  |  | Separate the “big” configuration procedure. | 
S2-2102727 | 23.247: Update the MBS Session Configuration Procedure | Tencent |  |  |  |  |  | AF-->PCF-->MB-SMF | 
S2-2102338 | 23.247: Clause 7.1.1: Clarification on MBS service area | LG Electronics |  |  |  |  |  |  | 
Figure 8.2.3-2: Initial Multicast group configuration via NEF

## Slide 7: Different proposed options
Option 1 (currently concluded in TR 23.757 Ericsson proposal, no CR)
  Service requirements are included in message from NEF to MB-SMF and then forwarded to PCF
PCF
MB-SMF
NEF/MBSF
AF
MB Session Start (service requirement)
MBS Policy Association Req/Resp
Ericsson comment :
As commented during SA2#144E, PCF interaction illustrated here is also proposed in Nokia Sol#3 in TR23.757 and included in conclusion (clause 8.2.3)
Ericsson comment: Don’t understand why Nokia keeps describing things ignoring the fact that the flow in this slide is concluded in TR and currently adopted in 23.247.

## Slide 8: Different proposed options
Option 2 (Tencent, was withdrawn during last meeting)
  If PCF is used, it triggers establishment of MBS context at MBS

## Slide 9: Different proposed options
Option 3 (2947r01 (Nokia, Tencent), 2673(Vivo)?, 2439 (Intel, Lenovo, Tencent, Motorola Mobility)?)
  Similar to existing PCC
  Session binding based on MBS session context at PCF
  For initial configuration , NEF establishes PCC authorization session
  For updates, direct interaction between NEF and PCF
  PCF retrieves stored configured session information from database (Nokia: UDR, Vivo: UDR)
  BSF used to discover PCF with MBS session context

## Slide 10: Comparison of Options
Option 1
  Unclear how policy authorization requests can be rejected => [Ericsson] PCF provides authorized QoS
  Large containers might be required for service decription => [Ericsson] Do we expect many service descriptions? For MBS Sesison with 2 MBS QoS Flows, then 2 sets of packet filters would be sufficient? Besides, is the size of container an issue with SBI?
  MB-SMF would be affected for service informnation updates even if PCF does not updated authorized QoS => [Ericsson] Do we expect any scenario that a new service data flow is to be added without changing the QoS? What is the difference if AF send the request to the PCF ?
  Unclear how PCF can use preconfigurede input for policy decisions (without database access) => [Ericsson] What is the difference from AF interacting with PCF directly? Policy decision can be provisioned by AF -> NEF -> UDR, and then PCF can subscribe to policy change
Option 2 (already withdrawn) => [Ericsson] does not seem to work.
  Substantial change of MB-SMF PCF interactions compared to existing PCF_SmPolicyControl (might become an MB-SMF service)
  Unclear how PCF can use preconfigurede input for policy decisions (without database access)
Option 3
  Aims for alignment with and maximum reuse of existing PCC procedures to ease implementations =>[Ericsson] What is the alignement? In PDU Session establishment, SMF create SM policy association with PCF before AF requested resoruce allocation.
  Provides farmework for extensions (e.g. event notification when service is activated, when PCF decides to downgrade QoS …)
    [Ericsson] With the MB-SMF – PCF interaction in 23.247 v0.2.0, PCF can also downgrade QoS. Do you have example of event notification? It would be helpful if we discuss the use case for MBS Session policy control.

## Slide 11
How to handle associated QoS flows for individual fallback in policy control?

## Slide 12
At the time when the UE joins, QoS flows associated to the multicast session will be added by the SMF to the unicast PDU session and marked as being associated with the multicast session in preparation to a fallback to individual delivery.
The SMF obtains the information about the QoS flows for multicast from the MB-SMF.
Other QoS flows are determined by the SMF based on Policy Rules supplied by the PCF
QoS flows contain QoS rules with Packet filters and priorities and QFIs that need to be harmonized and decided upon based on policies. Associated QoS flows should be kept separate from QoS flows where radio resources are always reserved. Thus, special 5QIs not used for the PDU session may need to be allocated. This conflicts with existing QoS flow binding procedures in TS 23.503.
Total available bandwidth also needs to be considered
Policy control should be able decide which services the user can obtain simultaneously
Problem

## Slide 13
SMF informs PCF that UE joined a multicast session and provides QoS flows obtained from MB-SMF for that multicast session
The PCF determines Policy Rules from the QoS flow information for the multicast session and selects 5QIs and priorities taking into account other installed PCC rules.
PCF provides Policy rules for associated QoS flows that contain an indication that those rules are for QoS flows associated with a multicast session
Proposal

## Slide 14
Thank You!