## Slide 1: eNPN Status Report
Peter Hedman
Ericsson (Rapporteur)

## Slide 2: eNPN status after SA2#146E (1/3)
General
  5 LSes sent from SA2#146e (one NPN related TEI17 reply to CT1)
  CRs agreed addressing most of the items from the Exception request, see SP-210539, with items related to KI#1, KI#2, KI#3 and KI#4, but issues left are dependent on SA3 and CT1 and will be addressed by SA2 alignment (Cat F) CRs i.e.
    how to provide UE capabilities to UDM for extending UPU with additional parameters (CT1 to resolve)
    Completion of architecture with DCS (including whether DCS can include AUSF/UDM) based on SA3 feedback
    Whether/how credentials for NSSAA and secondary authentication can be sent from PVS to the UDM (SA3 dependent)
    Whether to provide Allowed NSSAI to the UE (CT1 dependent)
Related to Key Issue 1 (Enhancements to Support SNPN along with credentials owned by an entity separate from the SNPN):
  No agreement for how to provide UE capabilities to UDM for extending UPU with additional parameters, instead an LS asking CT1 to take the lead and progress the work (SA2 will align based on the outcome)
  CRs agreed to enable update of CH controlled prioritized lists of preferred SNPNs and GINs using SoR (also LS sent)
  CRs agreed related to CH selection when SUPI type is IMSI
  8 CRs to 23.501 and 4 CRs to 23.502 agreed
  Next Steps: maintenance
Related to Key Issue 2 (NPN support for Video, Imaging and Audio for Professional Applications (VIAPA))
  1 CR to 23.501 agreed related to guidelines for usage of QoS related exposure capabilities to leverage between underlay network and overlay network
  Next Steps: maintenance
WI Code | Work Item Title | WP | Target Date | WID#
eNPN | Enhanced support of Non-Public Networks | 85% > 95% | Sept, 21 | SP-200980

## Slide 3: eNPN status after SA2#146E (2/3)
Related to Key Issue 3 (Support of IMS voice and emergency services for SNPN)
  1 CR agreed to 23.228 addressing whether SNPN can support IMS services from more than one independent IMS provider
  1 CR agreed to 23.501 on SNPN support for emergency
  1 CR agreed to 23.228 on IMS Support for SNPN
  Next Steps: maintenance
Related to Key Issue 4 (UE Onboarding and remote provisioning)
  1 CR agreed to 23.502 on provision/update the UE with credentials for NSSAA and/or secondary authentication
  1 CR to 23.501 and 1 CR agreed to 23.502 clarifying that AMF re-allocation is supported and how the AMF implementation specific timer for onboarding is handled in this case
  1 CR agreed to 23.501 and 1 CR agreed to 23.502 on Dynamically providing PVS addresses from DCS to ONN for restricting UP and provide PVS addresses to the UE
  1 CR agreed to 23.501 related to completion of architecture with DCS. As dependent on SA3, SA2 alignment will be needed once SA3 concluded their work.
  No agreement for how to provide UE capabilities to UDM for extending UPU with additional parameters, instead an LS asking CT1 to take the lead and progress the work (SA2 will align based on the outcome)
  No agreement on how credentials for NSSAA and/or secondary authentication can be sent from a PVS to UDM i.e. dependent on SA3 and SA2 alignment will be needed once SA3 concluded their work.
  1 CR agreed to 23.502 on details of Registration procedure for onboarding, but some details left and dependent on SA3 and also CT1 whether Allowed NSSAI is to be sent to the UE
  Additionally, 6 CRs to 23.501 agreed
  Next Steps: maintenance
WI Code | Work Item Title | WP | Target Date | WID#
eNPN | Enhanced support of Non-Public Networks | 85% > 95% | Sept, 21 | SP-200980

## Slide 4: eNPN status after SA2#145E (3/3)
  RAN impacts and dependencies:
  As per agreed CRs the RAN impacts are SIB related for changes related to Key issues 1, 3 and 4; new RRC indication for solutions related to Key issues 4
SA3 dependencies
  SA3 dependencies identified functionality related to support of Credentials Holder, support of IMS voice and emergency, and support for UE onboarding.
  SA3 feedback expected on e.g. Onboarding architrecture related to DCS and CP provisioning of credentials for NSSAA and/or secondary authentication
Contentious Issue:
  -
Focus for the Next Meeting (SA2#147E):
  Maintenance including changes required to support input from other WGs
Overall Plan:
  Maintenance
Risks:
  Completion of the work dependent on progress in SA3 (KI#4)

## Slide 5: eNPN Status at SA#93e
Progress since SA#92-e:
  5 LSes sent from SA2#146e (one NPN related TEI17 reply to CT1)
  CRs agreed addressing most of the items from the Exception request, see SP-210539, with items related to KI#1, KI#2, KI#3 and KI#4, but issues left are dependent on SA3 and CT1 and will be addressed by SA2 alignment (Cat F) CRs
    how to provide UE capabilities to UDM for extending UPU with additional parameters (CT1 to resolve with SA3 input)
    Completion of architecture with DCS (including whether DCS can include AUSF/UDM) based on SA3 feedback
    Whether/how credentials for NSSAA and secondary authentication can be sent from PVS to the UDM (SA3 dependent)
    Whether to provide Allowed NSSAI to the UE (CT1 dependent)
  8 CRs to 23.501 and 4 CRs to 23.502 agreed related to KI#1
  1 CR agreed to TS 23.501 related to KI#2
  1 CR agreed to TS 23.501, 2 CRs agreed to TS 23.228 related to KI#3
  9 CRs agreed to TS 23.501, 4 CRs agreed to TS 23.502 related to KI#4
  RAN impacts and dependencies:
  RAN impacts as per agreed CRs:
    Impacts are SIB related for changes related to Key issues 1, 3 and 4; new RRC indication for solutions related to Key issues 4
Next steps:
  Corrections, and questions and alignments with other WGs
WI Code | Work Item Title | WP | Target Date | WID#
eNPN | Enhanced support of Non-Public Networks | 85% > 95% | Sept, 21 | SP-200980