## Slide 1: MPS for 5GC LBO Authorization Gap
Discussion Paper for 3GPP SA2#151-e, May 16-20, 2022
S2-2203859
Robert C. Streijl, Peraton Labs

## Slide 2: Introduction
There is a gap in 5G LBO for MPS.
The V-PCF cannot authorize a Service User with an MPS subscription.
A proposal is provided in this discussion paper.
CRs for TS 23.501, TS 23.502, and TS 23.503 are also submitted based on this proposal
This Discussion Paper and 3 CRs are supported by a new TEI-18 work item.

## Slide 3: PCF Authorization 5GC LBO Roaming - Problem
2) vPCF cannot use N24 to obtain MPS subscription from HPLMN, because N24 does not have authorization features and only supports UE policy.
Data
Network
UE
LTE-Uu
NR
eNB
gNB
eNB
gNB
Xn
5G-RAN
V-PCF
N6
N5
AF
N14
AMF
UPF
N3
N2
N9
N8
HPLMN
VPLMN
N10
N24
UDM
H-PCF
UDR
N35
N36
N7
N4
I-SMF
N11
N15
N38
SMF
N16a
1) AF (e.g., MPS for Data Transport Service server) sends authorization request and invocation request to vPCF.

## Slide 4: Proposed Solution
Goal
  V-PCF must learn if the roaming UE has an MPS subscription
Existing/design principles
  V-AMF receives the MPS priority indication from UDM over N8
  No change desired over the roaming interfaces (N8, N10, N24), because IP-NNI agreements are complex to change.
Solution
  V-AMF passes an MPS priority indicator to V-SMF(s) and the V-SMF(s) passes it to the V-PCF(s).
    MPS priority indicator indicates whether the UE has an MPS subscription, or not.
  V-PCF store the MPS priority indication such that V-PCF can later use it to authorize dynamic AF initiated MPS requests (e.g., MPS for Data Transport Service).

## Slide 5: PCF Authorization 5GC LBO Roaming - Solution
Data
Network
UE
LTE-Uu
NR
eNB
gNB
eNB
gNB
Xn
5G-RAN
V-PCF
N6
N5
AF
N14
AMF
UPF
N3
N2
N9
N8
HPLMN
VPLMN
N10
N24
UDM
H-PCF
UDR
N35
N36
N7
N4
I-SMF
N11
N15
N38
SMF
N16a
Existing: N8 is the only roaming interface where the MPS priority indicator is passed.
Proposal: Make use of this indication received at the AMF on N8 to inform vPCF about MPS subscription.
Solution: Use N11 and N7 (and N16a in the case of I-SMF)

## Slide 6: Proposed Solution
Proposal: Add MPS priority indication to the following service operations:
AMF
I-SMF
SMF
PCF
Create SM Context
Update SM Context
Create SM Context
Update SM Context
PDU Session Update
SM Policy Control Create
SM Policy Control Update
N11
N16a
N7
N11
VPLMN

## Slide 7: Solution (1-2)
PDU Session Establishment
  At UE registration, the V-AMF receives an indication whether the UE has an MPS subscription from the UDM in the HPLMN. The V-AMF sends an MPS priority indication to the SMF and PCF as follows:
      V-AMF -> V-SMF: Nsmf_PDUSession_CreateSMContext
      V-SMF -> V-PCF: Npcf_SMPolicyControl_Create
      V-PCF -> V-SMF: Npcf_SMPolicyControl_Create Response
      V-SMF -> V-AMF: Nsmf_PDUSession_CreateSMContext response
  V-PCF sends a newly specified Policy Control Request Trigger (PCRT) for MPS priority indication change to V-SMF in step 3 above. This allows the V-SMF to report in the future in case of an MPS subscription change using Npcf_SMPolicyControl_Update.
  When adding an I-SMF, the V-SMF already has MPS subscription: No change required.
  This is required for roaming UEs with LBO only

## Slide 8: Solution (2-2)
PDU Session Modification
  MPS priority/subscription modification in UDM in HPLMN. V-AMF learns via Nudm_SDM_Notification.
  Two cases:
    V-AMF did not have an MPS subscription, but now has an MPS subscription (“MPS priority” is present)
    V-AMF had an MPS subscription, but no longer has the MPS priority (“MPS priority” is absent)
  Without I-SMF:
      V-AMF -> V-SMF: Nsmf_PDUSession_UpdateSMContext
      V-SMF -> V-PCF: Npcf_SMPolicyControl_Update
      V-PCF -> V-SMF: Npcf_SMPolicyControl_Update Response
      V-SMF -> V-AMF: Nsmf_PDUSession_UpdateSMContext response
  With an I-SMF:
      V-AMF -> I-SMF: Nsmf_PDUSession_UpdateSMContext
      I-SMF -> V-SMF: Nsmf_PDUSession_Update
      V-SMF -> V-PCF: Npcf_SMPolicyControl_Update
      V-PCF -> V-SMF: Npcf_SMPolicyControl_Update response
      V-SMF -> I-SMF: Nsmf_PDUSession_Update response
      I-SMF -> V-AMF: Nsmf_PDUSession_UpdateSMContext response
  Note: When V-PCF receives an MPS subscription, the existing 3GPP procedure could use step 3 (no I-SMF) or steps 4 + 5 (with I-SMF) to potentially send back a change in PCC rule for the PDU session. This is left to the operator.

## Slide 9: Impacted TSs and Clauses
TS 23.501
  § 5.6.3 Roaming
  § 5.22.2 Subscription-related Priority Mechanisms
TS 23.502
  § 4.3.2.2.1 Non-Roaming and Roaming with Local Breakout (step 3 and 7b)
  § 4.3.3.2 UE or network requested PDU Session Modification (non-roaming and roaming with local breakout) (step 1h and 2)
  § 4.16.4 SM Policy Association Establishment (step 1)
  § 4.23.5.3 PDU Session modification procedure
  § 5.2.5.4.2 Npcf_SMPolicyControl_Create service operation
  § 5.2.8.2.3 Nsmf_PDUSession_Update service operation
  § 5.2.8.2.5 Nsmf_PDUSession_CreateSMContext service operation
  § 5.2.8.2.6 Nsmf_PDUSession_UpdateSMContext service operation
TS 23.503
  § 5.2.2 Roaming architecture
  § 6.1.3.5 Policy Control Request Triggers relevant for SMF
  § 6.1.3.11 Multimedia Priority Service support
  § 6.2.1.2 Input for PCC decisions

## Slide 10: Proposal
The proposal is to adopt the solution outlined in this discussion paper.
Contributions/Draft CRs:
  S2-2203860, 23501 Draft CR on MPS for 5GC LBO
  S2-2203861, 23502 Draft CR on MPS for 5GC LBO
  S2-2203862, 23503 Draft CR on MPS for 5GC LBO