## Slide 1: FS_AMP pre-SA2#152 CC
ZHUOYI CHEN
Rapporteur, China Telecom

## Slide 2: Status of FS_AMP
TR23.700-89, 80% finished
1 KI and 10 Solutions documented
Target for SA2#152E (last planned meeting for study phase)
  Clean up ENs in Solution#3, #6 and #9
  Finish solution evaluation
  Reach conclusion
  Submit WID proposal

## Slide 3: KI#1 Candidate Solutions Overview
 | N26-based Solution | Without N26 Interface Solution |  | 
1. Input path to MME | PCF-AMF-MME #1, #3, #6, #10 | PCF-AMF-HSS+UDM-MME #2, #4, #5, #7 | MME Locally #8 | PCF-HSS+UDM-MME #9
2. Local/Preconfig. timer | #10 | - | #2, #8 | -
3. One-time timer from PCF | #3 | #4, #5 | - | -
4. AM Policy Asso. Maint. | #1, #6 | #7 | - | #9

## Slide 4: KI#1 Candidate Solutions Overview
How does MME interact with 5GC for necessary inputs?
  MME local policy
    Sol. #8, if MME awares a UE from 5G, set the RFSP Index in use as “4G prioritized”
  From 5GC
    Sol. #1, #3, #6, #10, N26-based scenario, directly from AMF
    Sol. #2, #4, #5, #7, #9, without N26 interface scenario, from HSS+UDM
      Sol. #2, #4, #5, #7, (PCF->) AMF-> HSS+UDM -> MME
      Sol. #9, PCF -> HSS + UDM -> MME
How does MME re-select RFSP Index in use?
  When validity timer expires, MME may be able to select the RFSP Index
    Sol. #2, #8, #10, the timer is preconfigured timer in MME
    Sol. #3, #4, #5, when PCF generate a RFSP Index to “4G”, it provides the timer along.
  PCF provides updated authorized RFSP Index
    Sol. #1, #6, #7 and #9, when UE in 4G, the PCF needs to keep the AM association to the UE.

## Slide 5: Papers Submitted for CC
Solution Update
  Sol#3, Ericsson
  Sol#6, Samsung
  Sol#7, Samsung
Evaluation
  Ericsson
  CT
Conclusion
  Ericsson
  CT
WID

## Slide 6: KI#1 Way Forward Proposal
For without N26 interworking:  or  ?
  when MME aware the UE is from 5GC, locally set the RFSP Index to a value of “4G prioritized” (Sol.#8)
  MME select the RFSP index value according to the RFSP Index in use from HSS+UDM (Sol. #2, #4, #5, #7)
For N26/without N26 interworking: Should PCF keep AM Association and continue to update authorized RFSP Index? (Sol.#1, #6, #7)
The validity timer: can we agree on the following?
  MME set the "RFSPinUseExpiryTime“ according to
    The preconfigure value at MME locally. (Sol.#2, #8, #10)
    Or the value selected by PCF (Sol. #3,#4,#5)
    The value from PCF has higher priority than the preconfig. Value
MME selects an RFSP Index value using the enhancement solution from this SID before a RFSP Index value validity timer expires. When the timer expires, the MME re-selects an RFSP Index value according to current specification.

## Slide 7: Following Plan
2022-02 SA2#149E (0.5TU)
2022-04 SA2#150E (0.5TU)
2022-05 SA2#151E (0 TU)
2022-08 SA2#152E (0.5TU), to finish evaluation and conclusion; submit WID
2022-10 SA2#153E (0.25TU) Normative #1
2022-11 SA2#154E (0 TU)
2023-1 SA2#154AH(0.25TU) Normative #2