SA WG2 Meeting #152E e-meeting	S2-2205776

August 17th – 26th 2022, Elbonia	(revision of S2-220xxxx)

Source:	China Mobile

Title:	Cover sheet for presentation of TR 23.700-87 to TSG-SA#97

Document for:		Approval

Agenda Item:	10.2

Work Item / Release:	FS_NG_RTC/Rel-18

Abstract of the contribution: This contribution proposes the TR 23.700-87 to be sent to TSG-SA#96 for approval.

3GPP TSG-SA Meeting #97E	Tdoc <DocNumber>

Elbonia, Sep. 13th – 19th

Title:	Presentation of Report to TSG:
TR 23.700-87, Version 0.4.0

Source:	TSG SA WG2

Document for:	Approval

Abstract of document:

The Technical Report 23.700-87 studies the system architecture for the next generation real time communication services based on IMS enhancement requirements from SA1 and SA4.

- Enhancement to support Data Channel usage in IMS network;

- IMS enhancement to support AR telephony communication;

- IMS enhancement to support third party specific user identities;

- Study of Applicability of Service based principles to IMS media control interfaces.

Changes since last presentation to TSG SA:

This is the first presentation to TSG SA.

The TR is considered 81% complete.

Outstanding Issues:

The following issues are to be concluded:

- The interaction between DCSF and IMS AS for DC event report;

- How to ensure the same application is downloaded to UEs;

- Whether CRS based solution can be agreed as a solution for KI#3.

Contentious Issues:

No consensus could be reached to introduce a new optional function UMF for Rel-18..