## Slide 1
Xiaomi
Discussion about Terminology Alignment

## Slide 2: Terms defined in FS_Ranging_SL (TR 23.700-86)
Definitions
Ranging: refers to the determination of the distance between two UEs or more UEs and/or the direction and/or relative positioning of one UE (i.e. Target UE) from another UE (i.e. Reference UE) via PC5 interface.
Reference UE: A UE who determines a reference plane and reference direction in the Ranging based service and Sidelink positioning.
  NOTE 1: Reference UE is the same as Observer UE used in TR 22.855 [2].
Target UE: A UE whose distance, direction and/or position is measured comparing to the reference plane, reference direction and/or location of a Reference UE in the Ranging based service and Sidelink positioning.
  NOTE 2: Any UE participating in the Ranging/Sidelink Positioning can be both a Target UE and a Reference UE and can switch roles in the same Ranging/Sidelink Positioning session.
Assistant UE: A UE who provides assistance for Ranging/Sidelink Positioning when the direct ranging/Sidelink positioning between a Reference UE and a Target UE cannot be supported.
Located UE: A UE of which the location is known or is able to be known using Uu based positioning. A Located UE can be used to determine the location of a Target UE using Sidelink Positioning.
Location Server UE: A UE offering location server functionality in lieu of LMF, for Sidelink Positioning and Ranging over Sidelink. It interacts with a Target UE, Reference UEs, Assistant UE and Located UEs as necessary in order to calculate the location of the Target UE.
Sidelink Positioning: Positioning UE using PC5.
Positioning: A functionality, which detects a geographical location and optionally, velocity (of e.g. a mobile terminal).
Relative position: An estimate of the UE position relative to other network elements or relative to other UEs.
Open Issues
Concerning Reference UE and Target UE, whether new name will be defined to differentiate with the term Reference UE and Target UE used in eLCS is FFS.
Definition on the terminology of Ranging and Sidelink positioning will be aligned with RAN WGs, and will be revisited when there's any conclusion in RAN WGs.

## Slide 3: Terms defined in RAN1
Definitions
Target UE: UE to be positioned (in this context, using SL, i.e. PC5 interface).
Sidelink positioning: Positioning UE using reference signals transmitted over SL, i.e., PC5 interface, to obtain absolute position, relative position, or ranging information.
Ranging: determination of the distance and/or the direction between a UE and another entity, e.g., anchor UE.
Anchor UE: UE supporting positioning of target UE, e.g., by transmitting and/or receiving reference signals for positioning, providing positioning-related information, etc., over the SL interface.
Open Issues
Continue discussion on additional terminology clarification(s) such as: Initiator UE, Responder UE, Sidelink Positioning group, reference UE, etc, including whether such terminology
FFS: clarification of the knowledge of the location of the anchor UE

## Slide 4: Terms defined in FS_eLCS_Ph3 (TR 23.700-71)
Definitions
Positioning Reference Unit (PRU): As defined in TS 38.305 [6].
Reference UE: A UE with a location assumed known to the network that can obtain location related information of one or more target UE(s), which may assist the network to improve the positioning performance of target UE(s).
Open Issues
Editor's note: It is FFS whether a PRU and a Reference UE should be combined into a single entity that is able to function as either or both.
Within the FS_eLCS_ph3 study and this TR, the Reference UE has no relationship with other Studies, e.g. FS_Ranging_SL, unless clearly mentioned. If a terminology alignment between studies is required, it will be done before starting normative work.

## Slide 5: FS_Ranging_SL Scenarios
a) Between 2 UEs: UE1 and UE2 are peers
b) UE0 positioned by multiple UEs over PC5
c) UE1 and UE3 are peers, but no direct communication, UE3 providing assistance
Target UE
Reference UE/ Anchor UE
Target UE
Reference UE/ Anchor UE
Reference UE/ Anchor UE
Reference UE/ Anchor UE
Target UE
Reference UE/ Anchor UE
Assistant UE
d) UE0 to position multiple UEs over PC5
Target UE
Reference UE/ Anchor UE
Target UE
Target UE

## Slide 6: Role of Location Server UE
Target UE
Reference UE
LCS server UE
LMF
a) LMF and Target UE/Reference UE can directly communicate
b) LMF and Target UE/Reference UE communicate via LCS server UE
Target UE
Reference UE
LCS server UE
LMF

## Slide 7: Proposed Way Forward
Terminology alignments:
  Replace “Reference UE” with “Anchor UE”, using the terminology defined by RAN1
  Align the definition of “Ranging” and “Sidelink Positioning” between SA2 and RAN1
Clarify definition of Location Server UE
Update related texts throughout the TR
Send a LS to RAN WG about SA2 defined terminology to avoid further mis-alignment
[SA2] Ranging: refers to the determination of the distance between two UEs or more UEs and/or the direction and/or relative positioning of one UE (i.e. Target UE) from another UE (i.e. Reference UE) via PC5 interface.
[RAN1] Ranging: determination of the distance and/or the direction between a UE and another entity, e.g., anchor UE.
Proposal: Ranging: refers to the determination of the distance between two UEs or more UEs and/or the direction and/or relative positioning of one UE (i.e. Target UE) from another UE (i.e. Anchor UE) via PC5 interface.
[SA2] Sidelink Positioning: Positioning UE using PC5.
[RAN1] Sidelink positioning: Positioning UE using reference signals transmitted over SL, i.e., PC5 interface, to obtain absolute position, relative position, or ranging information.
Proposal: Sidelink Positioning: Positioning UE using PC5 to obtain absolute position, relative position, or ranging information.
[SA2] Reference UE: A UE who determines a reference plane and reference direction in the Ranging based service and Sidelink positioning.
[RAN1] Anchor UE: UE supporting positioning of target UE, e.g., by transmitting and/or receiving reference signals for positioning, providing positioning-related information, etc., over the SL interface.
Proposal: Adopt RAN1 definition of Anchor UE to replace Reference UE.