## Slide 1: FS_XRM status and plan for SA2#152e
Dan Wang, Hui Ni
China Mobile, Huawei

## Slide 2: Agenda
General status
KI related solutions analysis and potential conclusion

## Slide 3: General discussion (I)
Time Unit status
Proposal
  First version of WID is supposed to be approved in SA2#153(Oct meeting)
  In November meeting, the normative work start and CRs can be apporved (based on the first version WID), WID can be updated.
  In Dec SA plenary, TR23.700-60 and the WID will be sent for Approval
 |  |  |  | Feb, 22 | Apr, 22 | May, 22 | Aug, 22 | Oct, 22 | Nov, 22 | Jan, 23 | Feb, 23
SID/WID | Study TU | Normative TU | Total TU | #149 | #150 | #151 | #152 | #153 | #154 | #154AH | #155
FS_XRM | 9 | 5 | 14 | 1 | 2 | 2 | 2 | 2 | 1 | 2 | 2

## Slide 4: General discussion (II)
Progress at SA2#152e
  last chance for new solution , solution updates
  Start KI evaluations and conclusions
    Evaluation = summarise the solutions, how they answer the KI problem statement, identify advantages, point out limitations…
    Conclusion = make decision on how to resolve the KI problem statement, i.e. select an existing solution, or build a solution based on (a) proposed solution(s), or list principles.
  It is suggested the conclusion and evaluation papers can be merged before or during the emeeting.
    SA2#153e will focus on conclusions and WID
WT#1 update in SA#96 in June(SP-220705)

## Slide 5: Status of KI#1 (Policy control enhancements to support multi-modality flows coordinated transmission for single UE)
Number of solutions: 5(sol#1,36,38,39,40)
Key aspects:
  Minimize the delay difference beween two multi-modality flows
  Handling multi-modality flows together
  Related QoS requiremnent for the multi-modality flows
  Network exposure to support application assistance considering IMS/AF providing indication
  How to correlate the multi-modality flow together, i.e. based on AF indication or based on subscription
  Other aspects:
  Guarantee one PDU session for multiple multi-modality flows
  New solutions for KI1&2 will be discussed in 152e, the conclusion for KI1&2 can be submitted, but for information in 152e. It is expected to finish the conclusion in 153e.

## Slide 6: Status of KI#2 (Support the Application Synchronization and QoS Policy Coordination for Multi-modal Traffic among Multiple UEs)
Number of solutions: 6 (sol#2, 3, 4, 37, 38, 40)
Key aspects:
  AF provide group policy to UEs.
  Multiple PCFs vs single PCF
    Multiple PCFs, one PCF policy adjustment based on AF and other PCFs’ instruction.
      PCF discovery through BSF vs PCF using the same UDR
    Single PCF, guarantee the single PCF selection
  Handling multi-modality flows together
  Related QoS requiremnent for the multi-modality flows
  Network exposure to support application assistance considering IMS/AF providing indication
  How to correlated the multi-modality flow together, i.e. based on AF indication or based on subscription
  New solutions for KI1&2 will be discussed in 152e, the conclusion for KI1&2 can be submitted, but for information in 152e. It is expected to finish the conclusion in 153e.

## Slide 7: Status of KI#3 (5GS information exposure for XR/media Enhancements)
Number of solutions: 10 (sol. 5, 6, 41, 42, 43, 44, 45, 46, 47, 48)
No. | Exposure information | Solution description
#41 | congestion level | Use of ECN bits in NG-RAN for L4S
#46 | congestion infromation | For UL, UE/gNB can do congestion detection, and ECN marks, UE/gNB can do congestion detection, and set the information in IP header or GTP-U header, the UPF do the ECN marks. For DL, gNB sets ECN marks in the PDU IP header; gNB sets in the PDCP/RLC header, UE copies the ECN marks over to the IP PDU header. gNB transmits congestion information in the GTP-U header, sending to UPF. The UPF translates congestion into ECN marks, set finally in the IP PDU header of subsequent downlink packets.
#5 | UE data rate, normal data transmission interruption event, congestion information | subscribe:AF-NEF-PCF-SMF-RAN+UPF Notify: 1)RAN/UPF(-NEF)-AF;2)RAN/UPF-SMF-PCF(-NEF)-AF Exposure UE data rate, normal data transmission interruption event, congestion information to enable application codec/rate adaptation.
#43 | Congestion level information, QNC | Option1:without ECN; subscribe: AF-NEF-PCF-SMF-RAN/UPF; notification: RAN-UPF-AF Option2:with ECN; RAN-UPF(ECN marking)-UE XR application server could adjust media codec/traffic rate to adapt to network conditions
#6 | non-GBR QNC | there is available mean bitrate of non-GBR flow. RAN can report change of available mean bitrate when it is over a threashold. report: RAN-AMF-SMF-PCF(-NEF)-AF control: AF(-NEF)-PCF-SMF-AMF-RAN
#48 | QNC of GBR and non-GBR | As suggested in solution 6, a similar QoS Notification mechanism for GBR and non-GBR QoS Flows is needed. Therefore, in the case of XRM services the QoS Notification message may be used by the RAN to indirectly instruct the application to increase or reduce the codec rate or use a specific codec rate. notification: RAN-AMF-SMF-PCF-NEF-AF
#44 | QNC | the NG-RAN has its own logical to control the number of the QNC message to 5GC. The AF provided AW only control the latency from the GFBR measurement to generating the QNC message, it does not control/determine the number of QNC to be generated by the NG-RAN. subscribe:AF(-NEF)-PCF-SMF-RAN Notify: RAN-AMF-SMF-PCF(-NEF)-AF
#42 | round-trip delay | Subscribe:AF-NEF-BSF-PCF-SMF-UPF; Notify: RAN-UPF-NEF-AF There are two possible cases for round-trip delay monitoring. - The UL and DL traffic be within the same QoS flow. RTT can be measured; - The main UL and DL traffic are separated into two different QoS flows, e.g. RTT=RAN delay+(CNRTT1+CNRTT2)/2
#47 | delay difference, two way delay of data flows | subscribe: AF-NEF-PCF; exposure: PCF-NEF-AF Based on the notification and report of the delay status information, the AF can provide the coordinated service requirement to the 5GS for the tactile and multi-modal flows.
#45 | estimated QoS | request: AF-NEF-NWDAF-OAM; exposure: NWDAF-NEF-AF Estimated QoS: the estimated QoS parameters/characteristics (e.g. the bandwidth, packet error rate, etc.) in advance for a period of time and/or for a specific location area.
Key aspects:
  What to expose:
    Congestion indication / Congestion level
    UE data rate; normal data transmission interruption event;
    GBR/Non-GBR QNC
    Round trip delay/delay difference/two way delay
    Estimated QoS
  Methods:
    With ECN: which NF detect the congestion information, which NF do the ECN marking
    Without ECN: information exposure through CP/UP;
In SA2 152e:
Supporting ECN, make decision on which NF detects and which NF do ECN marking;
Supporting general information exposure procedure,
Make decision on which information are needed to be exposed.

## Slide 8: Status of KI#4&5 (PDU Set based handling)
Number of solutions: 10 for KI#4(PDU Set integrated handling), 2 for KI#5(Differentiated PDU Set handling), and 17 for both. 29 in total (sol #7-26, 49-57)
One consolidated solution (sol #52) was included in the TR with multiple ENs.
Key aspects:
  Enhancements on control plane:
    Assistance information from AF to 5GS
    New QoS parameters for PDU Set based QoS handling
  Enhancements on user plane:
    PDU Set related information to be identified by the UPF. And assumptions on N6 protocols.
    PDU Set related Information sending to RAN via GTP-U extension header
Observations:
  It’s not necessary to discuss and conclude KI#4 and #5 separately since most solutions are proposed to resolve both KIs.
  It’s not possible to evaluate all 29 solutions in details, compare their pros/cons considering the number and the overlapping between them.
  Sol #52 is a summary of majority views from all other solutions. It identified key aspects that could eventually act as a framework for normative work, but still open on many aspects.
  Most solutions are focusing on DL PDU Set handling. To support UL PDU Set handling, interaction between UE and RAN is the key.

## Slide 9: Status of KI#4&5 (PDU Set based handling)
Issues for discussion
  How to perform evaluation and conclusion
    Can we agree to evaluate and conclude KI#4 and KI#5 together?
    Two optional ways for make conclusion
      Option 1: Taking sol 52 as baseline to discuss the conclusion. Any content that cannot be agreed will be removed from sol 52. Complementary aspects from other solutions can also be proposed and agreed as part of conclusion separately.
      Option 2: Deriving agreeable principals as conclusions from all solutions, including sol 52.
  Consideration on N6 protocol(s), which option(s) should be considered:
    Use existing IETF RFCs and drafts of RTP protocol
    To define new RTP headers in 3GPP (SA4?)
    To extend GTP-U protocol
    No N6 protocol standardized (How PDU Set information is identified is based on UPF implementation)
  Support for uplink PDU Set handling
    Keep open and wait for RAN WG progress?
SA2 152:
Continue work on sol52(option 1) to resolve ENs, or start to derive agreeable principals(option 2) as interim conclusion.
Identify real controversial points
SA2 153: Resolve controversial points and conclude.

## Slide 10: Status of KI#6 (Uplink-downlink transmission coordination to meet Round-Trip latency requirements)
Number of solutions: 3 (sol. 27, 28, 29)
Key aspects:
  Current solution focus on how to control UL/DL PDB based on RT latency requirement.
    Sol 27, PCF control UL/DL PDB based on RT latency requirement.
    Sol 29/30, RAN control UL/DL PDB locally based on RT latency requirement.
SA2 152:
Evaluate solutions and determine which NF controls RT latency.
Conclude the KI.

## Slide 11: Status of KI#7 (Policy enhancements for jitter minimization)
Number of solutions: 4 (sol. 9, 30, 31, 32)
Key aspects:
  Sol 9 proposes PDU Set Delay budget can result to a jitter reduction. Since no jitter specific mechanism are proposed, it seems this solution need not be evaluated under KI#7.
  Other Sols (30,31,32) focus on jitter monitoring based existing QoS monitoring results, incl.
    Subscription and report of jitter
    PCC rule enhancements
    Jitter derivation
    Jitter usage for CN/AF
SA2#152e:
Focus on jitter monitoring based on existing QoS monitoring results, and corresponding subscription and reporting procedure/path.
Evaluate and conclude the KI.

## Slide 12: Status of KI#8 (Enhancements to power savings for XR services)
Number of solutions: 5 (sol. 33, 34, 58, 59, 60)
Key aspects:
  What information need to be sent to RAN for CDRX handling.
  How 5GC can achieve these information.
LS was sent to RAN1 and RAN2 in SA2 #151E. LS reply from RAN1 will be ready for SA2 #152E.
SA2#152e
Based on RAN1 feedback and evaluation of existing solutions, get interim conclusion on the basic set of information (e.g. Periodicity of burst, end indication of burst) and how 5GC obtain such information.
SA2#153e
Conclude the KI, further information can be added in SA2 #153e based on further inputs from RAN WGs.

## Slide 13: Status of KI#9 (Trade-off of QoE and Power Saving Requirements)
Number of solutions: 3 (sol. 34, 35, 61)
  Sol 34: UE power status impacts CDRX configuration.
  Sol 35: RAN get device power consumption and trigger QoS profile switch.
  Sol 61: PCF subscribe UE battery level change and adjust policy based on that.
Observation:
  Sol 35 and 61 are on UE battery based QoS adjustment. Which NF (RAN/PCF) get UE battery status and how to adjust QoS based on that should be evaluated.
  Sol 34 should be evaluated separately.
SA2 #152e
Check with RAN WG for feasibility of RAN obtaining UE battery status.
Evaluation of solutions from SA2 PoV while waiting for RAN feedback?
SA2 #153e
Determine whether NF should obtain UE battery status, and how to adjust policy.
Determine whether UE power status can impact CDRX configuration.
Evaluate solution and make conclusion.

## Slide 14: Thank you!