3GPP SA WG2 Meeting #152E	S2-220xxxx

17-26 August 2022, Electronic Meeting

Source:	Xiaomi

Title:	Discussion for TEI18 WID proposal on 5GC supporting Non-3GPP Satellite Access Network

Document for:	Discussion

Agenda Item:	10.5

Work Item / Release:	TEI18_5GN3SAT / Rel-18

Abstract of the contribution: This paper discusses TEI18 WID proposal on 5GC supporting Non-3GPP Satellite Access Network.

# Discussion

In the existing 3GPP defined satellite access in 5GS (before Rel-18), the UE shall support NR(Satellite) to access 3GPP network via satellite, and the satellite NG-RAN is a NG-RAN which uses NR(Satellite) in providing satellite access to UEs.

There is a service requirement in Stage1 TS22.261(v18.6.1) ‘Service requirements for the 5G system’:

“A 5G system with satellite access shall support different configurations where the radio access network is either a satellite NG-RAN or a non-3GPP satellite access network, or both.”

How to support satellite access as non-3GPP access network in 5GS needs to be specified in Rel-18 according to the Rel-18 stage1 service requirement.

3GPP has specified untrusted non-3GPP access to 5GC since Rel-15 and trusted non-3GPP access to 5GC since Rel-16, which can be the baseline for the statellite access as non-3GPP access network in 5GS.

Therefore, we would like to propose TEI18 work item on 5GC supporting Non-3GPP Satellite Access Network (TEI18_5GN3SAT).

The objective of the proposed TEI18 work item is to:

- [TS 23.501/502] the objective of this work item is to:

-	Add description and procedures related to support non-3GPP satellite access to 5GC including the satellite access as:

- Untrusted non-3GPP access

- Trusted non-3GPP access

# Proposal

Based on the discussion above, the following documents were submitted.

1) S2-220xxxx: New WID: 5GC supporting Non-3GPP Satellite Access Network (TEI18_5GN3SAT)

2) S2-220xxxx: Draft CR to TS 23.501

3) S2-220xxxx: Draft CR to TS 23.502