## Slide 1: Cross border mobility related to IMS calls and LI for home routed IMS
Ericsson
Ericsson/BCSS
2022-06-15

## Slide 2: Background
Currently if IMS signalling uses encryption in HPLMN, mobility without re-establishment of the IMS PDN connection/PDU session cannot be done in most cases. The main reasons are related to the regulatory requirement for Lawful intercept:
  LI in VPLMN uses tapping of traffic in SGW/UPF to be able to see all call related data, if traffic is encrypted this will not be possible.
  LI in HPLMN may be enabled but only allowed by the regulution when UE is in the county of HPLMN. In such a case, when moving out LI need to stop intercepting traffic.
LS S2-2203662 list LI requirements and some questions to SA2

## Slide 3: Questions and answers
What changes are needed so the IMS can make the required information available?
  IMS core to request UE re-register. VoLTE UE should support this already
What is the preferred mechanism to get the IMS-information provided to the VPLMN (e.g. as part of the registration process)?
  See above, for ongoing calls, the telephony AS sends re-INVITE to provide means for LI to intercept call related information such as called and calling party.
Are changes needed for the HPLMN to be able to deactivate or activate the IMS confidentiality protection during inter-PLMN handover?
  Yes, see above
Are changes needed for the VPLMN to detect if the correct configurations for roamers to allow lawful interception are in use at the VPLMN?
  No changes to 5GC/EPC Specification for VPLMN actions foreseen, LI is outside SA2 responsibility. NOTE: Inter PLMN mobility is mainly a deployment issue, and not a specification issue

## Slide 4: Way forward
Decide what release the needed IMS changes are to be made
Do not devide the needed changes in separate releases since the difference in between ongoing call and not ongoing call are minor, see next slide for proposed flow and also proposed CR
Our believe is that we can do this with a single CR under TEI18 with maximum of TU 0.5 which only has impact on IMS, i.e. EPC/5GC has no impact

## Slide 5: Small differences between in call or not in call
UE
P
-
CSCF
I/S-CSCF
H-PCRF/PCF
4. SIP NOTIFY (re-Authenticate)
2. NOTIFY (PLMN Change)
3. SIP MESSAGE (PLMN change, Re-authenticate request)
1. PLMN change detected
TAS
0. UE active in a voice call
6. SIP MESSAGE (Re-Invite request)
7. SIP Re-INVITE(called party, calling party, codec)
5. IMS Re-Registration procedure
Common procedure regardless of UE in or not in call
Extra procedure if UE in call

## Slide 6: Terminal side
Our understanding is that main chipset vendors and terminal vendors already should support the proposed solution, but to be verified.

## Slide 7: Some question raised during the joint C1, S2, S3, S3-LI call
How does TAS know the codecs and UDP endpoints of the UE and AGW, since those are needed?
  P-CSCF needs to translate. CR updated accordingly
How would LI system know if the concerned UE is calling or called party based on the header fields in the re-Invite.
  Information what info is needed is provided in the CR. Details to be sorted out in stage 3
How to handle SRTP?
  This is currently a short coming in existing text in Annex W of 23.228. Nothing is stated how the media plane should be handled. Two proposals are included in CR marked by comments as Alt1 and Alt2.