## Slide 1: Discussion for VoLTE GBR handling in roaming case
OPPO
SA WG2 Meeting #SA2-153E S2-2208606
10 - 27 Oct., 2022, Electronic meeting

## Slide 2: Background
In SA2#151E, a LS Out S2-2204724 is agreed with the following information:
SA2 has discussed the issue and believe that a GBR mismatch between HPLMN and RAN can lead to voice packets being dropped with no certainty that the voice coders will adapt to the lower data rate.
SA2 invite SA4 to provide further analysis of the impact of such a GBR mismatch.
One possibility might be to extend the reject message that e.g., carries the cause “QoS parameter mismatch” to include information on the maximum GBR that that MME/RAT can accept for that QCI.
SA2 invite CT4 and CT3 to comment on the appropriate reject causes and this possible extension.

## Slide 3: Summary of the discussion in last meeting
The following alternatives were raised by people
Alternative-1: The VPLMN downgrades the GBR itself
The VPLMN downgrades GBR parameter, and only sends the modified GBR parameter to the RAN in the VPLMN without informing the HPLMN.
Alternative-2: The VPLMN rejects with acceptable GBR value
S/P-CSCF may learn the supported GBR value in the VPLMN and may send a proper value next , the S/P-CSCF sends the information to UE and UE may trigger a new INVITE request as described in 24.229. time.
Alternative-3: Solve it as an implementation issue
The VPLMN and HPLMN should have an agreement on the VoLTE GBR value for inbound roaming. This can be done based on SLA. The GSMA NRG may help to have such recommended GBR value for the inbound roaming case.
Notes: Some changing is made based on a policy, the policy is related to UE’s resource, data privacy, network condition. And the network condition needs to be known by UE

## Slide 4: Evaluation
From OPPO side, we consider it as a problem needs to be revolved with the following evaluation:
Alternative-1 (The VPLMN downgrades the GBR itself):
it needs some UE impacts or enhancements to be aware of the downgrade of GBR and make some adaption work. It is not recommended since it will impact UEs in the market.
Alternative-2 (The VPLMN rejects with acceptable GBR value):
It can let the HPLMN knows the proper value and solve the problem, but it needs to impact both HPLMN and VPLMN’s BF. It is not expected the solution can be implemented very soon but it is a possible direction to resolve the problem.
Alternative-3 (Solve it as an implementation issue):
It is another possible way to resolve the problem, but it highly depends on the agreement between inter-PLMN. More GSMA work such as making recommendation for the GBR value in inbound roaming case is expected.

## Slide 5: Proposal
Proposal-1: consider trying to resolve it with an implementation way, such as sending an LS to GSMA to encourage them to standardize the VoLTE GBR value （e.g. an minimum GBR value for VoLTE QoS flow) in inbound roaming case as recommendation for inter-PLMN implementation.
Proposal-2: if majority agree, adding a solution in altenative-2 (i.e. the VPLMN rejects with acceptable GBR value) to resolve the problem as a technical method.
Note: This solution should consider both VoLTE/VoNR and EPS Fallback scenario.