## Slide 1: Discussion on the information exchange architecture between two PLMNs
Huawei, HiSilicon

## Slide 2: Background: Architecture principles for KI#3
For sure the analytics exchange between two PLMNs is allowed, however, whether the raw data exchange between two PLMNs is allowed or not is waiting for the feedback from SA3/GSMA.
This paper proposes a discussion on the architecture options on the information exchange between two PLMNs, no matter the information is analytics or the potential raw data.

## Slide 3: Architecture options
V-PLMN
H-PLMN
NWDAF
DCCF
XNF
NWDAF
DCCF
XNF
SEPP
SEPP
Option 1: Introduce a standalone XNF. The V-NWAF/V-DCCF discovers the H-GEF through the V-GEF, and the H-GEF sends the subscription information to the H-NWAF or H-DCCF.
NWDAF
DCCF
NEF
SEPP
NWDAF
DCCF
NEF
SEPP
V-PLMN
H-PLMN
XNF
XNF
SEPP
XNF
SEPP
XNF
V-PLMN
H-PLMN
NWDAF/DCCF
NWDAF/DCCF
SEPP
SEPP
NWDAF/DCCF
XNF
NWDAF/DCCF
XNF
V-PLMN
H-PLMN
Option 2: The NEF is enhanced to support the XNF's functionality. The V-NWAF/V-DCCF discovers the H-NEF through the V-NEF, and then the H-NEF sends the subscription information to the H-NWAF or H-DCCF.
Option 3: Enhance the SEPP to support the XNF's functionality and enable the V-NWAF/V-DCCF to interact with the H-NWAF/H-DCCF through SEPP.
Option 4: Enhance the NWDAF/DCCF to support the XNF's functionality, the V-NWDAF/V-DCCF can directly discovers H-NWDAF or H-DCCF or H-NF for information subscription through existing mechanisms.
Support to introduce a central NF (i.e. XNF)’s functionality such as user consent checking, data anonymization/filtering etc.
But there are 4 architecture options to implement the XNF as follows:

## Slide 4: Pros/Cons
Option# | Introduce a new NF | Pros | Cons
1 | YES |  | The functionality of the new NF is simple and single, and the introduce of the new NF will enhance the complexity of the network data analytics architecture.
2 | NO |  | The NEF is used for the information exposure to the application provider but not 5GC NF in another PLMN. So it is not suitable to enhance the NEF.
3 | NO |  | Though the SEPP enables the interconnect between 5G networks from different PLMNs. However, the SEPP is more security related. In addition to the security related requirement (e.g. user consent checking, data anonymization), others requirements (e.g. data/analytics type checking or filtering, minimization of signaling because of data/analytics exchange) are also needed, so it is also not suitable to enhance the SEEP.
4 | NO | Currently, NWDAF/DCCF has already supported to collect or provide information (including analytics, or raw data if SA3/GSMA is confirmed), so it is suitable to enhance the NWDAF/DCCF to support user consent checking, anonymization/filtering before the information exchange in roaming scenario. On the other hand, if only analytics exchange between two PLMNs is allowed, the analytics related signaling will be not massive, so only NWDAF’s enhancement is needed, no DCCF enhancement is needed. | The functionality of the NWDAF/DCCF becomes more complex.

## Slide 5: Proposal
It is proposed to select the Option 4 as baseline for the information exchange architecture in roaming scenario.