## Slide 1: Consolidated solution proposal for PIN
Zhenhua Xie (rapporteur)
vivo
S2-2209008

## Slide 2
Architecture
AF is optional to provision parameters without user privacy concern for dynamic 5G system resources management related to PIN
SMF is impacted to support PIN Communication and corresponding 5G system resources management
NEF is enhanced to expose capability for PIN
UDR is enhanced to store, return, and notify Application Data for PIN
PCF is enhanced to generate PIN UE policy and PIN SM policy according to information notified by UDR
PEGC is enhanced to send necessary information to SMF for supporting PIN communication configuration

## Slide 3
Concept of PIN session
Consisting of one or more PDU Sessions
At least one PDU Session of PEGC is included
Control of PDU Sessions is anchored at same SMF to enable network local switch
Transfer PIN traffic within or outside PIN
May transfer PIN signaling between PEMC and PEGC

## Slide 4
High level overall procedure
PIN policy provisioning:
  The user subscribes PIN service from operator with GPSIs of PEMCs and PEGCs, which result in policy pre-configuration
  The AF is only used to manage 5GS resources for PIN dynamically, the parameters are used for UE policy control and SM policy control without privacy concern
5GS resources management:
  The PEMC and PEGC establish PDU Sessions according to PIN UE policy.
  The SMF anchors PDU Sessions of PEGC and PEMC, and allows PEGC to allocate IP addresses for PINEs
PIN communication management:
  The SMF enables the network local switch for PIN signaling
  The PEGC sends PIN communication configuration (packet filters and requested QoS) to SMF according to PEMC’s command
  The SMF enables the network local switch for PIN traffic according to the received PIN communication configuration

## Slide 5
Data manipulation for PIN
AF provisioning PIN service data:
  NEF expose PIN service operation
  NEF stores PIN UE data and PIN session data in UDR for PIN UE policy control and PIN SM policy control according to PIN service parameters received from AF
PCF subscribes event from UDR:
  AM-PCF is pre-configured to subscribe UDR for PIN UE data notification for PEMC/PEGC according to user’s PIN service subscription.
  SM-PCF subscribes UDR for PIN session data notification for PEGC’s PDU Session related to a PIN