## Slide 1
Thales, FS_5GSAT_Ph2, 3gPP Call Conference 21th Sept. 2022
Rapporteur discussion slides
Objective: introduction for discussion on how to complete TR23.700-28

## Slide 2: TR23.700-28 v 0.4.0 after SA2#152: STATUS
23 solutions are described, no more new solutions are expected in SA2#153
Rel17 solution for support of discontinuous satellite coverage is documented in §7.1
A methodology to rank solutions and be and help for final choice is proposed in §7.2
  1/Refine the mapping between solution and Key Issues, by identifying for each aspect of the Key Issue, if the given solution addresses the aspect or not.
  2/ Agree on preferable system assumptions
  3/ Determining the final solutions or assembly of parts of solutions, based on 1/ and 2/
Initial list of 4 preferable system assumptions is presented in §7.3.
Coverage Information Provisioning (first system assumption determination) is discussed, to UE in §7.4.1, to CN in §7.4.2.
Traceability matrix between KI requirements, impacts and solutions is provided in §7.5.1
No solution ranking is proposed yet in §7.5.2
Limitations of solutions are discussed in §7.5.3
Conclusions, that should, for each Key Issue, select solutions (and/or part of solutions) to cover all requirements, are to be elaborated in §8 during SA2#153, with rational for choice (preferable system assumptions,…)
OK ?
To complete

## Slide 3: TR23.700-28 objective SA2#153
Initial list of 4 preferable system assumptions is presented in §7.3.
Coverage Information Provisioning (first system assumption determination) is discussed, to UE in §7.4.1, to CN in §7.4.2.
Traceability matrix between KI requirements, impacts and solutions is provided in §7.5.1
No solution ranking is proposed yet in §7.5.2
Limitations of solutions are discussed in §7.5.3
Conclusions, that should select solutions (and/or part of solutions) to cover all requirements, are to be elaborated in §8 during SA2#153, with rational for choice (preferable system assumptions,…)
Need to be completed with solutions 17 to 23
Need to be completed with solutions 17 to 23
To be completed - At least with preferable architecture for coverage map generation (NW side)
Preferably a single (or minimum) Tdoc(s) to be submitted as basis for discussion during meeting
§7.4.1 Needs to be completed with solutions 17, 19, 21, 22
§7.4.2 Needs to be completed to determine best system assumption for coverage map generation
! call for volunteers !
Solution ranking can be proposed according §7.3, §7.5.1 and §7.5.3

## Slide 4: (§7.4.2) Discussion on preferable architecture for coverage map generation (NW side)
Several contributions in the last SA2#152 propose different architectures for the coverage map information generation and transfer to AMF/MME
It’s seems good architectural design principal to keep AMF/MME « clean MM and RM state machine », and to consider it’s not AMF/MME job to interface with Satellite Network Center and compute coverage maps… So where is the best place to do it?
Note this is independant to the system assumption on where the decisions (RR/CM) are taken (UE or CN), just to determine that if CN needs the coverage info, what is the best place to elaborate it.
Solution(s) | Where to elaborate cov. map | Pro | Cons
1, 4, 5 | Received from RAN | R17 compatible | - Limited to coverage information available in RAN (4 sat) - RAN dependancy
2,15 | External server (not via SCEF/NEF) | Possibly single source RAN/CN | - No standard interface for AMF/MME - Security
2,17, 19 | External server (via SCEF/NEF) | - Standard interface for AMF/MME | - Need SCEF/NEF evolution
15 | Pre-configuration in AMF (option sol15) | Simple | No standardized interface
6, 21 | NWDAF analytics | Standard interface for AMF | - Which external NWDAF interface? - 5G only
17 | New dedicated NF (CMNF) | Stand alone dedicated NF, clear AMF interface | 5G only
22 | External server (via NEF) by utilizing existing UAV architecture | Existing architecture (No new EPC interface needed) | 5GC and 5GC/EPC interwokring CN (No EPC only)

## Slide 5
Thales, discussion slides for Call Conference 21th Sept. 2022
Legend
-> generation of coverage information for positions/times in relation with Satellite Network Center
-> transfer of coverage information on given interface
Different system assumptions for coverage map generation and transfer - over 5GS
UE
gNB
AMF
Dedicated
NF
NEF
SBA/SBI
N1
CP
N2
N3
NWDAF
Third Party
Ext.
Server
Ext.
Server
(AF)
UPF
N6
UP
DN
Ext.
Server
N33
Sol22
Sol22
N1
SIB
Sol22
Sol22
Sol21
Sol21
Sol21
Sol19
Sol21
Sol19
Sol19
Sol17
Sol17
Sol17
Sol17
Sol17
Sol17
Sol15
Sol15
Ext.
Server
Sol15
DCAF
Sol15
Sol15
Sol15
Sol1,4,5
Sol1
Sol1,4,5

## Slide 6
Legend
-> generation of coverage information for positions/times in relation with Satellite Network Center
-> transfer of coverage information on given interface
UE
eNB
MME
SCEF
CP
S1
Third Party
Ext.
Server
Ext.
Server
(AF)
PGW
SGi
UP
DN
Ext.
Server
Sol22
SIB
Sol22
SMF
(+PGW-C)
Sol22
Sol19
Sol19
Sol19
Ext.
Server
Sol17
Sol17
Sol15
Sol15
NEF
Different system assumptions for coverage map generation and transfer - over 4G
Thales, discussion slides for Call Conference 21th Sept. 2022
Sol1, 4, 5
Sol1
Sol1,4,5
Sol2
Sol2