## Slide 1: Discussion on MBS
LiMeng
Huawei

## Slide 2: Agenda
Merging proposals for Rel-18 (see other documents).
Rel-18 open issues.
  KI#1: Inactive reception;
  KI#2: MOCN sharing;
    How to identify the broadcast service in 5GC.
  KI#3: on-demand MBS reception;
    Use case and/or benefits and solutions.
Rel-17 open issues.
  MBS Session activation/deactivation
  MBS User service
WID proposal.
Click here to join the meeting

## Slide 3: Rel-18 open issues

## Slide 4: KI#1 (RRC Inactive reception)
Overview
S2-2208334 | 23.700-47: KI#1, Update to Evaluation and Interim Conclusion | Ericsson | Evaluation: clarify solution #26, and #27; Conclusion: add one sentence saying “AF provides preferable UE list” in session creation procedure.
S2-2208472 | 23.700-47: KI#1, Interim conclusion updates | Nokia | on which UEs to keep in RRC_CONNECTED, clarify it can be cross-MBS sessions. And other clarifications.
S2-2208473 | 23.700-47: KI#1, evaluation updates | Nokia | Add clarification for each solutions in a finer categories. (one small issue: 7.1.3 for solution #23 can be refined)
S2-2208853 | 23.700-47: KI#1 conclusions update | CATT | Clarifying the way of using Mobility registration to join/leave, and other clarification.
S2-2208904 | 23.700-47: KI#1, Further evaluation and conclusion update | Huawei | Clarification on the way of using assistant information.
S2-2208961 | 23.700-47: KI#1, update the evaluation of Key issue#1 | ZTE | Adding solution #27 and #28 to the table in clause 7.1.
S2-2208962 | 23.700-47: KI#1, update the conclusion of Key issue#1 | ZTE | Clarify that the CM-IDLE UEs can also make use of Service request to activate the associated PDU session and receive MBS data.
S2-2208288 | 23.700-47: KI#1 and KI#6, Sol#26 Update to address ENs | Nokia | 
S2-2208332 | 23.700-47: KI#1, Sol#18: update to resolve ENs | Ericsson | 
S2-2208333 | 23.700-47: KI#1, Sol#27: update to resolve ENs | Ericsson | 
S2-2208852 | 23.700-47: KI#1 Sol#20 update: resolving Editor's notes | CATT | 
S2-2208963 | 23.700-47: KI#1, update the solution 6 | ZTE | 
S2-2208964 | 23.700-47: KI#1, update the solution 28 | ZTE | 

## Slide 5: KI#1 (RRC Inactive reception), cont’d
UE
RAN
SMF
MB-SMF
PCF
AF
NEF
UDM
1a. MBS session creation (MBS session priority)
2a. Shared tunnel establishment (MBS session priority)
MBS session priority information
MBS UE priority information
2b. PDU session modification (Connected UE)
1b. Npcf_PolicyAuthorization_Update (Connected UE)
3b. RAN MAY keep this UE to inactive
1c. MBS session creation (list of Connected UE)
2c. UE join
3c. Context subscribe (list of Connected UE)
4c. PDU session modification (Connected UE)
2d. PDU session establishment (SMF gets prioritized info)
3d. UE join
4d. PDU session modification (Inactive UE)
1d. Authorized UE list + prioritized info
Overview of Assistance information provisioning
Alt#1
Alt#2
Alt#3
Issue #1 – the way to provide the assistant info for MBS

## Slide 6: KI#1 (RRC Inactive reception), cont’d
Issue #2 – What information will be provided to the RAN?
  Alt #1: For an MBS session, an indication if the UE is Privileged(or the UE is suggested to be kept in CM-CONNECTED mode);
  Alt #2: For an MBS session, an indication if the UE can be switched to RRC Inactive mode and receive MBS data.
  Alt #3: An indication if the UE is privileged (or suggested to be kept in CM-CONNECTED)
Issue #3 – How to include KI#1 in the WID objective?
  Proposal: add KI#1 in the WID objective from the perspective of “requirement”, e.g.,:
    Support of UEs within an MBS multicast session to receive MBS session data while in CM-CONNECTED with RRC Inactive state.

## Slide 7: KI#2 (MOCN sharing)
Issue #1 – Usage of TMGI and Backward compatibility?
Issue #2 – Resource efficiency?
Issue #3 – Flexibility of releasing?
Issue #4 – O&M Configuration to be standardized?
Issue #5 – Service layer enhancement?
Overview
S2-2208395 | 23.700-47: KI#2, Evaluation Update | Ericsson
S2-2208474 | 23.700-47: KI#2, Interim conclusion updates | Nokia
S2-2208725 | 23.700-47: KI#2: Update the conclusions | Huawei
S2-2208732 | 23.700-47: Conclusion update on KI #2(MOCN network sharing) | SAMSUNG
S2-2208844 | 23.700-47: Conclusions for KI#2 | Qualcomm
S2-2208967 | 23.700-47: KI#2, update the evaluation and conclusion for the Key issue#2 | ZTE

## Slide 8: KI#2 (MOCN sharing), cont’d
Issue #1 – Usage of TMGI and Backward compatibility?
Rel-17 NG-RAN
Message sent for Rel-18 MOCN
Rel-17 5GC NFs
Message sent for Rel-18 MOCN
Possibility to reject?
Possibility to reject?
x
y
5GC of PLMN a
5GC of PLMN b
5GC of PLMN c
AF
MOCN TMGI α
z
MOCN TMGI α
Broadcast for b
Broadcast for c
Broadcast for c
Issue #2 – Resource efficiency?
Issue #3 – Flexibility of releasing/update?
  Whether the release/update will affect other MBS sessions?
  E.g., when release one MBS session, will other MBS session for the same broadcast service needs to be updated? Will the TMGI be re-allocated?
Issue #4 – O&M Configuration to be standardized?
  Do we need to standardize the OAM in SA2?
Issue #5 – Service layer enhancement?
  E.g., when UE needs to receive more than 1 TMGIs for a certain MBS service.

## Slide 9: KI#3 (on demand MBS session)
Overview
S2-2208336 | 23.700-47: KI#3, Evaluation update | Ericsson | Evaluation
S2-2208660 | 23.700-47: FS_5MBS_Ph2 KI#3 Update to evaluation and conclusion | China Mobile | Evaluation and Conclusion
S2-2209190 | 23.700-47: KI#3, evaluation updates | Nokia | Evaluation
Solution update (2)
S2-2208287 | 23.700-47: KI#3, Sol#30 Update to address ENs | Nokia | 
S2-2208657 | 23.700-47: FS_5MBS_Ph2 KI#3 Sol#11 Update for making clarification | China Mobile | 
Evaluation and conclusion (3)(2)

## Slide 10: Rel-17 open issues

## Slide 11: MBS Session activation/deactivation
 | Nokia | HW | Ericsson
Q1 During the MBS session deactivation procedure, does the MB-SMF instruct the MB-UPF to stop the forwarding of DL MBS data towards the N3mb DL F-TEIDs configured in the MB-UPF for the MBS session? | If session activation is to be detected by the MB-UPF, the MB-SMF can request the MB-UPF to perform Buffered Downlink Traffic detection and thus to stop forwarding data. If session activation is to be based on an AF request, the MB-SMF does not request the MB-UPF to perform Buffered Downlink Traffic detection and to stop forwarding data. | SA2 confirms that for the MBS session deactivation, the MB-SMF instructs the MB-UPF to stop the DL MBS data forwarding towards the N3mb DL F-TEIDs for the MBS session. | The answer to Q1 is yes
Q2 If the answer to Q1 is yes, when the multicast traffic resumes (i.e. first packet arrives at MB-UPF), does the forwarding of MBS data towards the N3mb DL F-TEIDs resume only after the MB-SMF instructs the MB-UPF to forward the packets at step 15 of the MBS session activation call flow (Figure 7.2.5.2-1), i.e. after the MB-SMF activates the multicast MBS session towards the AMF(s) (and NG-RAN nodes) and receives a successful response from the AMF (and a first NG-RAN node)? | Step 15 only applies if session activation is detected by the MB-UPF via Buffered Downlink Traffic detection. It can be executed in parallel to the previous steps to avoid that the start of the transmission is unduly delayed until replies from all NG-RAN nodes and SMFs are received. Newly established tunnels toward NG RAN nodes are already activated in step 10a and newly established tunnels toward SMF are already activated in step 10b. | SA2 confirms that the DL MBS data forwarding towards the N3mb DL F-TEIDs is resumed only after the MB-SMF instructs the MB-UPF to forward the packets at step 15 of the MBS session activation call flow (Figure 7.2.5.2-1 of TS23.247). | For Q2, SA2 confirms that when MBS session is activated, MB-SMF instructs the MB-UPF to forward the packets towards the existing N3mb DL tunnels at step 15, after it receives the first successful response from the NG-RAN via the AMF.
Q3 Can SA2 confirm that during an MBS session deactivation procedure, the SMF need not and shall not request the UPF(s) to maintain the N19mb tunnels and that, after an N19m tunnel (of the MBS session) is removed in the UPF, the SMF shall not send a ContextUpdate request message towards the MB-SMF to report the removal of the N19mb tunnel in the UPF? | SA2 agreed that keeping the tunnel for data forwarding towards the NG-RAN nodes and SMFs established may speed up the activation procedure (also in case Buffered Downlink Traffic detection is applied). The MB-SMF only releases those tunnels for data forwarding when being requested by NG-RAN or SMF, respectively. The MBS session activation procedure is already designed in such a way that it assumes that tunnels may exist at this point. | ‐Option 1: the N19mb tunnel is released. In this case the SMF need send a ContextUpdate request message towards the MB-SMF to release the tunnel between UPF and MB-UPF. At the next time MBS session activation, the SMF notifies the MB-SMF to re-establish the N19mb tunnel if it is needed. ‐Option 2: the N19mb tunnel is maintained but the delivery of the data to the UE's PDU session is suspended. In this case the SMF notify UPF to drop the received MBS session data. At the next time MBS session activation, the SMF notifies the UPF to forward the MBS session data if it is needed. Per operator’s policy one of the above two options is selected by the SMF during the MBS session deactivation. Also if the N19mb tunnel (of the MBS session) is removed in the UPF, the SMF need send a ContextUpdate request message towards the MB-SMF to report the removal of the N19mb tunnel in the UPF. | For Q3, SA2 confirms that the MB-SMF requests the MB-UPF to remove N19mb DL tunnels in step 2 of clause 7.2.5.3, and thus there is no need for the SMF(s) to send ContextUpdate request message to remove the N19mb DL tunnel between the UPF and the MB-UPF again.

## Slide 12: MBS User service

## Slide 13: Thank you!