## Slide 1: FS_GMEC/GMEC: Way Forward for Open Issues
SA2#153e

## Slide 2: Multiple SMFs for VN group communication: background
Objective: Support of SMF redundancy for reliability of the 5G VN group communication and which architectural enhancements, if any, are needed to enable the support of multiple SMFs to serve a 5G VN group
There are 2 kind of solutions:
  Alt #1: Sol#3 and sol#16 (S2-2208283) Solutions not needing N19 links between UPF(s) and leveraging IETF based N6 VPN(s) between UPF(s)
    Reply on the deployed ETSUN, use N16a enhancements for local-switching at I-UPF
    Configure N6 VPN between all related UPFs that are deployed to support a specific 5G VN, and those UPFs need also to support PE functionality, new “usage of PSA UPF” event notification (AF->NEF->UDM->SMF, SMF->AF) is used for dynamic management of the N6 VPN connectivity
  Alt #2: subset of sol#5, sol#19 (S2-2208939): Solutions requiring inter SMF communications to establish N19 links between UPF(s)
    Define a new NF (super SMF = GSMF) to which SMF(s) serving group members need to register with the SMF ID, UPF ID, N19 tunnel information, UE addresses supported by these UPF(s)
    GSMF services are used to negotiate N19 links between UPF(s) as well as the UE addresses supported by the corresponding UPF(s).
UPF1
UE1
UPF2
UE2
N6 VPN
AF
Alt #1
UPF1
UE1
SMF1
UPF2
UE2
SMF2
N19
GSMF
Alt #2
PE
PE
ISMF-1
ISMF-2
L-PSA1
L-PSA2
SMF1
SMF1

## Slide 3: Multiple SMFs for VN group communication: way forward
Open Issue #1: N19-based and/or N6-based forwarding is used between UPFs controlled by different SMFs
  Alt #1 – only N6-based forwarding: Sol#3 and sol#16 (S2-2208283)
    Propose SoH on Alt#1: Yes() No()
  Alt #2- only N19-based forwarding: subset of sol#5, sol#19 (S2-2208939)
    Propose SoH on Alt#2: Yes() No()
  Alt #3: Specify both N19-based and N6-based forwarding as an option (S2-2208954)
    Propose SoH on Alt#3: Yes() No()

## Slide 4: group service area enforcement
Background: A group can be provisioned with the group service area, the service area is applicable to each UE within the group.
Open Issue #2: How to enforce the group service area, e.g. when the UE member moves in/out of the service area of the group
  Alt#1: only LADN-based approach (S2-2208524)
    Propose SoH on Alt#1: Yes() No()
  Alt#2: support both LADN-based approach and SMF-based approach (S2-2208607)
    Propose SoH on Alt#2: Yes() No()

## Slide 5: Reporting for group member changes
Background:
  Exposure of membership changes applies to both 5G VN group created via 5G VN PP API and any other groups configured by OAM. The AF can be notified about the membership changes via this exposure service.
  In previous GMEC conference call, the assumptions for membership change exposure is to use Parameter Provisioning service, however some companies offline show different views on this assumption.
  So the purpose here is to confirm formally the assumption
Open Issue#3: Whether to use Event Exposure service or Parameter Provisioning service for reporting of group member changes
  Alt #1: Enhance Parameter Provisioning service for support of group member changes reporting (S2-2208428/S2-2208432)
    Yes
  Alt #2: Enhance Event Exposure service for support of group member changes reporting (S2-2208595/S2-2208941)
    Yes

## Slide 6: Monitoring of CSA/CSR
Open Issue#4: How to support Monitoring of CSA/CSR (communication service availability, communication service reliability )
  Alt#1: NWDAF/NEF analytics service is enhanced for monitoring of CSA/CSR
    Yes No
  Alt#2: NEF exposure of CSA/CSR monitoring is not specified
    Yes No
Postponed