## Slide 1: GMEC CC: Next Steps
For SA2#153e

## Slide 2: Status
KI#2 and KI#5 are concluded completely
KI#1 and KI#3 are concluded with the ENs:
KI#4 conclusion is postponed
GMEC WID-SP-220989 is agreed at SA#97, WID scope contains conclusions for KI#2 and KI#5

## Slide 3: Outline
Contribution plan for normative work
  KI#2, KI#5
  Structure for Normative work
  Volunteers
ENs Discussion
  KI#1, KI#3
  Volunteers
KI#4 Evaluation & Conclusion
  Way forward Discussion
GMEC WID revision

## Slide 4: Contribution plan for normative work KI#2
Key Issue #2: Enhance group status event reporting
  23.501 structure to capture the clarifications/enhancements
    New section?
    Sub-section under 5.20 (External Exposure of Network Capability) or 5.29.2 (5G VN group management)
    Other ways?
  Volunteers: (NTT DoCoMo, Huawei, Ericsson)?
  23.502 structure to capture the clarifications/enhancements
    Updates for Monitoring Event (4.15.3.1, 4.15.3.2, Nudm_EventExposure/Nnef_EventExposure services)
    Or, Updates for Provisioning Service (4.15.6.1, 4.15.6.x, Nudm_ParameterProvisioning/Nnef_ParameterProvisioning services/new PP_Notify Service)
    Other ways?
  Volunteers: (NTT DoCoMo, Huawei, Ericsson)?

## Slide 5: Contribution plan for normative work KI#5
Key Issue #5: Allowing UE to simultaneously send data to different groups with different QoS policy
  23.501 structure to capture the clarifications
    New section in Annex?
    Sub-section under 5.29.3 (Support for 5G LAN-type service/PDU Session management)
    Placeholder for Reference to KI#1/#3 for QoS provisioning for each group?
    Other ways?
  Volunteers: (Samsung, Nokia, Huawei, China Telecom)?
  23.502 structure to capture the clarifications
    None

## Slide 6: ENs Discussion KI#1 (1)
Key Issue #1: Enhance group attribute management
  For enforcement of service area applicable to each UE within the group:
    Editor's note: Whether to support LADN area per DNN/S-NSSAI will be determined during normative phase.
    Editor's note: Whether to support SMF-based method will be determined during normative phase.
    Option #1: If UE indicates that it can support LADN area per DNN/S-NSSAI to the AMF, the AMF then can provide UE with the LADN area per DNN/S-NSSAI, then UE, AMF and SMF enforces LADN area per DNN/S-NSSAI. Otherwise the option #2 will be used.
    Option #1a: The AF provides indication that the group members support LADN area per DNN/S-NSSAI during group definition. The AMF can receive such indication from UDM and then can provide UE with the LADN area per DNN/S-NSSAI, then UE, AMF and SMF enforces LADN area per DNN/S-NSSAI. If such indication is not received, then the option #2 will be used.
    Option #2: SMF-based method will be used. In order to enable the UE to make aware of when to re-establish the rejected PDU session due to moving out of service area, the UE is pre-configured with service area for the group or dynamically configured with the service area from application (AF) via application signaling
    Option #3: UDM guarantees that the UE’s groups won’t share the same DNN, e.g. by rejecting the creation request for the second group on the same DNN, or by assigning different DNNs + same S-NSSAI for the UE’s groups. So later the LADN mechanism can be reused.
    Way Forward:

## Slide 7: ENs Discussion KI#1 (2)
Key Issue #1: Enhance group attribute management
  Support of Group-MBR using Slice-MBR.
    Editor's note: How to support reusing Slice-MBR for Group-MBR will be determined during normative phase.
    Options?
    Way Forward:
  Volunteers for PCR: (Huawei, Ericsson, China Mobile, ZTE, China Telecom, Samsung, Nokia, CATT)?
  Stable conclusion part:
    WID update.
    Draft CRs?
      23.501: Sub-section under 5.20 (External Exposure of Network Capability) or 5.29.2 (5G VN group management)? New sections? Or other ways?
      23.502: Updates for Provisioning Service (4.15.6.1, 4.15.6.x, Nudm_ParameterProvisioning/Nnef_ParameterProvisioning services)
      Volunteers: (Huawei, Ericsson, China Mobile, ZTE, China Telecom, Samsung, Nokia, CATT)？

## Slide 8: ENs Discussion KI#3 (1)
Key Issue #3: NEF exposure framework for provisioning of traffic characteristics and monitoring of performance characteristics
  Editor's note: Whether a new NEF service is to be defined or existing AF session with QoS is enhanced is FFS and can be determined during normative phase:
    Option #1: new NEF service?
    Option #2: Enhance existing AF session with QoS?
    Option #3: other existing service, e.g., Parameter Provisioning service in KI#1?
    Way Forward:
  QoS Parameter Notification Control or AQP is used for monitoring of specific performance characteristic.
    Editor's note: Whether QNC or QAP is more general to support monitoring of specific QoS can be determined during normative phase.
    Option #1: QNC mechanism is enhanced to monitor and report for a specific performance characteristic
      FS_XRM conclusion: 5G System also may support API based exposure of congestion level information towards AF. The following information may be exposed: QNC for GBR QoS Flow: data rate cannot be guaranteed
    Option #2: set multiple combinations of AQP (GBR, PDB, PER) values, those AQPs can be used by the AF to derive the unsatisfied QoS parameter using the reference to the highest-prioritized AQP that RAN currently matches
    Way Forward:

## Slide 9: ENs Discussion KI#3 (2)
Key Issue #3: NEF exposure framework for provisioning of traffic characteristics and monitoring of performance characteristics
  Editor's note: How to reuse existing QoS division mechanism or other SID conclusion for UE-to-UE traffic can be determined during normative phase.
    Way Forward: Update based on Other SID conclusion and existing mechanism.
  Editor's note: Whether and how to support monitoring of communication service availability, communication service reliability is FFS.
    NWDAF is responsible to monitor CSA/CSR?
    SA5 scope?
    Other ways?
    Way Forward:
  Volunteers for PCR: (Huawei, Ericsson)?

## Slide 10: ENs Discussion KI#3 (3)
Key Issue #3: NEF exposure framework for provisioning of traffic characteristics and monitoring of performance characteristics
  Stable conclusion part:
    WID update.
    Draft CRs?
      23.501: Sub-section under 5.29.3 (Support for 5G LAN-type service/PDU Session management)? New sections? Or other ways?
      23.502: New Service or Updates for existing services (AF SessionwithQoS or Parameter Provisioning service)
      Volunteers: (Huawei, Ericsson)?

## Slide 11: KI#4 Way Forward Discussion
Key Issue #4: Multiple SMFs for VN group communication
  Option#1, Introduce GSMF to support N19-based forwarding dynamically between UPFs controlled by different SMFs
  Option#2, Introduce NRF service enhancement and SMF-SMF interface to support N19-based forwarding dynamically between UPFs controlled by different SMFs
  Option#3, Introduce N16a enhancements (single SMF Set) and N6 pre-configuration to support N6-based between UPFs controlled by different SMFs
  Way Forward:
  Volunteers for PCR: (Samsung, Huawei, China Mobile, ZTE, CATT, Ericsson, Nokia, China Telecom)?

## Slide 12: GMEC WID revision
KI#1 and KI#3:
  Option #1: capture the stable conclusion part, add the other part after resolution of the ENs
  Option #2: add a reference to KI#1/#3 conclusion, update the description based on progress of ENs during the meeting
  Way Forward:
KI#4:
  Option #1: capture the agreeable part, add the other part after completing conclusion
  Option #2: add a reference to KI#4 conclusion, update the description based on conclusion of the progress
  Way Forward: