## Slide 1: GMEC CC: Next Steps
For SA2#153e

## Slide 2: Status
KI#4 conclusion is postponed
KI#2 and KI#5 are concluded completely
KI#1 and KI#3 are concluded with the ENs:
GMEC WID-SP-220989 is agreed at SA#97, WID scope contains conclusions for KI#2 and KI#5

## Slide 3: Outline
KI#4 Evaluation & Conclusion
  Way forward Discussion
Contribution plan for normative work
  KI#2, KI#5
  Structure for Normative work
  Volunteers
ENs Discussion
  KI#1, KI#3
  Volunteers
GMEC WID revision

## Slide 4: KI#4 Way Forward Discussion
Key Issue #4: Multiple SMFs for VN group communication
  Option#1, Introduce GSMF as a New NF to support N19-based forwarding dynamically between UPFs controlled by different SMFs (sol#5 without SMF-SMF interface)
  Option#2, Introduce NRF service enhancement and SMF-SMF interface to support N19-based forwarding dynamically between UPFs controlled by different SMFs (sol#4)
  Option#3, Introduce N16a enhancements (single SMF Set) and N6 VPN to support N6-based forwarding between UPFs controlled by different SMFs (sol#3, sol#16)
  Way Forward: Firstly, Work on options without new SMF-SMF interface
    Down-scope variants
    Sol#5 open issues (no SMF-SMF interface)
  FFS: Separate the GSMF from existing NF
  Volunteers for PCR: (Rapp (blank paper) + X company’s paper, Samsung, Huawei, China Mobile, ZTE, CATT, Ericsson, Nokia, China Telecom)?

## Slide 5: Contribution plan for normative work KI#2
Key Issue #2: Enhance group status event reporting
  23.501 structure to capture the clarifications/enhancements
    New section?
    Sub-section under 5.20 (External Exposure of Network Capability) or 5.29.2 (5G VN group management)
    New para under 5.20 (External Exposure of Network Capability)
    Other ways?
  Volunteers: (NTT DoCoMo, Huawei, Ericsson)?
  23.502 structure to capture the clarifications/enhancements
    Updates for Monitoring Event (4.15.3.1, 4.15.3.2, Nudm_EventExposure/Nnef_EventExposure services)
    Or, Updates for Provisioning Service (4.15.6.1, 4.15.6.x, Nudm_ParameterProvisioning/Nnef_ParameterProvisioning services/new PP_Notify Service)
    Other ways?
  Volunteers: (NTT DoCoMo, Huawei, Ericsson)?

## Slide 6: Contribution plan for normative work KI#5
Key Issue #5: Allowing UE to simultaneously send data to different groups with different QoS policy
  23.501 structure to capture the clarifications
    New section in Annex (informative, copy-paste of the TR conclusion?) QoS provisioning part need to Wait for KI#1/KI#3 conclusion
    Sub-section under 5.29.3 (Support for 5G LAN-type service/PDU Session management)
    Placeholder for Reference to KI#1/#3 for QoS provisioning for each group?
    Wait a bit for KI#1/KI#3 conclusion, then make CRs
    Other ways?
  Volunteers: (Samsung, Nokia, Huawei, China Telecom)?
  23.502 structure to capture the clarifications
    None
    Wait for KI#1/KI#3 conclusion

## Slide 7: ENs Discussion KI#1 (1)
Key Issue #1: Enhance group attribute management
  For enforcement of service area applicable to each UE within the group:
    Editor's note: Whether to support LADN area per DNN/S-NSSAI will be determined during normative phase.
    Editor's note: Whether to support SMF-based method will be determined during normative phase.
    Option #1: If UE indicates that it can support LADN area per DNN/S-NSSAI to the AMF, the AMF then can provide UE with the LADN area per DNN/S-NSSAI, then UE, AMF and SMF enforces LADN area per DNN/S-NSSAI. Otherwise the option #2 will be used.
    Option #1a: The AF provides indication that the group members support LADN area per DNN/S-NSSAI during group definition. The AMF can receive such indication from UDM and then can provide UE with the LADN area per DNN/S-NSSAI, then UE, AMF and SMF enforces LADN area per DNN/S-NSSAI. If such indication is not received, then the option #2 will be used.
    FFS: Option #2: SMF-based method will be used (from network PoV, it is not aware whether UE app is able to do this ). In order to enable the UE to make aware of when to re-establish the rejected PDU session due to moving out of service area, the UE is pre-configured with service area for the group or dynamically configured with the service area from application (AF) via application signaling
      Application is aware of the UE presence in the area of the group?
      Application is aware of the PDU session management?
      How to co-exist with LADN mechanism?
      LADN feature is not used in current marketing
      Inform the UE to stop NAS SM in some time?
    Option #3: UDM guarantees that the UE’s groups won’t share the same DNN, e.g. by rejecting the creation request for the second group on the same DNN, or by assigning different DNNs + same S-NSSAI for the UE’s groups. So later the LADN mechanism can be reused.
    Option #3a: for a given UE, the AMF checks if there is any existing LAND area for the same DNN/S-NSSAI of the group, AMF does some reactions
    Way Forward: Minimum: limitation that LADN DNN is only associated with only S-NSSAI. Keep door open for option#2, FFS for combination with option#2 or alternative option#2?

## Slide 8: ENs Discussion KI#1 (2)
Key Issue #1: Enhance group attribute management
  Support of Group-MBR using Slice-MBR.
    Editor's note: How to support reusing Slice-MBR for Group-MBR will be determined during normative phase.
    Options?
      Multiple DNNs for the same slice-MBR. Single PCF(?)/UDR for group-MBR control, restrict single PCF/UDR for a group
    Way Forward: share the solution updates and continue discuss offline
  Volunteers for PCR: (Huawei, Ericsson, China Mobile, ZTE, China Telecom, Samsung, Nokia, CATT)?
  Stable conclusion part:
    WID update.
    Draft CRs? (low priority, treat draft CRs as discussion paper(only for information))
      23.501: Sub-section under 5.20 (External Exposure of Network Capability) or 5.29.2 (5G VN group management)? New sections? Or other ways?
      23.502: Updates for Provisioning Service (4.15.6.1, 4.15.6.x, Nudm_ParameterProvisioning/Nnef_ParameterProvisioning services)
      Volunteers: (Huawei, Ericsson, China Mobile, ZTE, China Telecom, Samsung, Nokia, CATT)？

## Slide 9: ENs Discussion KI#3 (1)
Key Issue #3: NEF exposure framework for provisioning of traffic characteristics and monitoring of performance characteristics
  Editor's note: Whether a new NEF service is to be defined or existing AF session with QoS is enhanced is FFS and can be determined during normative phase:
    Option #1: new NEF service?
    Option #2: Enhance existing AF session with QoS?
    Option #3: other existing service, e.g., Parameter Provisioning service in KI#1, AF influence?
    Way Forward: check more on sol#2.
  QoS Parameter Notification Control or AQP is used for monitoring of specific performance characteristic.
    Editor's note: Whether QNC or QAP is more general to support monitoring of specific QoS can be determined during normative phase.
    Option #1: QNC mechanism is enhanced to monitor and report for a specific performance characteristic
      FS_XRM conclusion: 5G System also may support API based exposure of congestion level information towards AF. The following information may be exposed: QNC for GBR QoS Flow: data rate cannot be guaranteed
    Option #2: set multiple combinations of AQP (GBR, PDB, PER) values, those AQPs can be used by the AF to derive the unsatisfied QoS parameter using the reference to the highest-prioritized AQP that RAN currently matches
    Way Forward:

## Slide 10: ENs Discussion KI#3 (2)
Key Issue #3: NEF exposure framework for provisioning of traffic characteristics and monitoring of performance characteristics
  Editor's note: How to reuse existing QoS division mechanism or other SID conclusion for UE-to-UE traffic can be determined during normative phase.
    Way Forward: Update based on Other SID conclusion and existing mechanism.
  Editor's note: Whether and how to support monitoring of communication service availability, communication service reliability is FFS.
    NWDAF is responsible to monitor CSA/CSR?
    SA5 scope?
    Other ways?
    Way Forward:
  Volunteers for PCR: (Huawei, Ericsson)?

## Slide 11: ENs Discussion KI#3 (3)
Key Issue #3: NEF exposure framework for provisioning of traffic characteristics and monitoring of performance characteristics
  Stable conclusion part:
    WID update.
    Draft CRs?
      23.501: Sub-section under 5.29.3 (Support for 5G LAN-type service/PDU Session management)? New sections? Or other ways?
      23.502: New Service or Updates for existing services (AF SessionwithQoS or Parameter Provisioning service)
      Volunteers: (Huawei, Ericsson)?

## Slide 12: GMEC WID revision
KI#1 and KI#3:
  Option #1: capture the stable conclusion part, add the other part after resolution of the ENs
  Option #2: add a reference to KI#1/#3 conclusion, update the description based on progress of ENs during the meeting
  Way Forward:
KI#4:
  Option #1: capture the agreeable part, add the other part after completing conclusion
  Option #2: add a reference to KI#4 conclusion, update the description based on conclusion of the progress
  Way Forward: