## Slide 1: Discussion on PIN issues and corresponding proposals
Zhenhua Xie
vivo
S2-2209007

## Slide 2
Issue of whether 5GC is responsible for PIN management
Assumption:
  Meaning of PIN management and PINE management
    See the table in page 3
  NEF exposes APIs for (A), (B) and (C), and PCF/SMF handling the requests. The NEF APIs are, e.g.,
    A: Create/Delete PIN (PIN ID)
    B: Modify PIN (PIN ID, Service auth info)
    B: Modify PEGC (UE Address/DNN/S-NSSAI, Service auth info)
    C: Modify PIN (PIN ID, packet filters, QoS)
  SMF supports PEGC command for (C)
    UE (PEGC) initiates PDU Session Modification

## Slide 3
Issue of whether 5GC is responsible for PIN management
Type | Meaning | Companies’ view
PIN Mgmt. (A) | resources configuration/deconfiguration related to a PIN, including URSP/PIN Routing Selection Policy generation and provisioning for PDU Sessions related to PIN | i: with AF via NEF or not ii: possible without AF
PIN Mgmt. (B) | Service authorization related to a PIN, e.g., modify service authorization for a PIN PIN authorization: whether PEMC is allowed to do something to a PIN, whether AF is authorized to manipulate a PIN | With AF via NEF or not
PIN Mgmt. (C) | traffic QoS and routing control | With AF via NEF or not, and without AF
PIN Mgmt. (D) | resources status related to a PIN, including, activate/deactivate a PIN | i: with AF via NEF or not ii: With AF via NEF or not, and without AF
PIN Mgmt. (E) | Create/delete a PIN | Undiscussed
PINE Mgmt. | member management for a PIN (PEMC, PEGC, and PINE) | i: with AF ii: not needed

## Slide 4
Issue of whether 5GC is responsible for PIN management
Questions:
  Should it be possible for PEGC command SMF to do (B)? No KI#4
    preconfigured URSP/PIN Routing Selection Policy may be used when AF is not used
    E.g., over SM-NAS after PEGC getting URSP/PRSP to modify whole PIN Service auth info, modify Service auth info per PEGC, which eliminates exposure of everything to AF
  Whether does 5GC expose APIs, or SMF support PEGC propose, or both for (D)? E.g.,
    NEF API of managing PIN policy and 5GC resources activate/deactivate of a PIN with parameter of PIN ID (yes) KI#3
    PEMC to PEGC sends SM-NAS to SMF to indicate activate/deactivate a PIN with authorization information (both: no)
    SOH – (first we can have two revisions for two different way, and finally to determine whether SOH)
  Should it be possible for PEGC indicating PCF to do (A)？(possible:no)KI#4
    E.g., over AM-NAS sent to PCF via UE Policy Container (transparent to AMF) for generating URSP/PIN Routing Selection Policy
    SOH-(first we can have two revisions for two different way, and finally to determine whether)
  Whether does NEF expose APIs, or SMF support PEGC command, or both for PINE management? e.g., KI#3
    5GC allows AF to provision PEMC IDs, PEGC IDs, PINE IDs for a PIN (no:yes)
    PEGC sends SM-NAS to SMF including PEMC IDs, PEGC IDs, PINE IDs
    SOH if no consensus
Proposal:
  TBD

## Slide 5
Issue of identification
Questions:
  Whether PIN ID needs to be known by UDR/UDM/NEF? yes
    May internal PIN ID and external PIN ID discussed in normative phase
  Whether PIN ID is allocated by NEF/UDM/UDR or not?
    AF allocates, AF ID + PIN ID is unique (yes)
    PEMC allocates (yes)
    NEF/UDM allocates a unique ID (like NEF allocates Reference ID for some operations) (yes)
    Do it in normative phase
  Whether PINE ID needs to be known by UDR/UDM (no:yes) KI#3
    If UDR/UDM knows PINE ID, it implies 5GC support PINE management (storage) that related to above slide?
    What is the usage of the PINE ID by 5GC except storage?
    It is related first issue, can do SOH together.
Proposal:
  TBD

## Slide 6
Issue of non-3GPP QoS assistance information and proposal
Interim conclusions:
  5G QoS parameters (including QoS characteristics, GFBR/MFBR) may be sent to PEGC to assist the deriving of N3GPP QoS parameters
  5GC may take into account the delay budget between PINE and PEGC to guarantee the end to end delay for PINE traffic.
Issue:
  “5G_QOS_INFO” described in TS 24.502 is sent by N3IWF/TNGF to UE when initiating child SA creation, the Additional QoS Info in the 5G_QOS_INFO may include (table 9.3.1.1-2 of 24.502):
    QoS characteristics (resource type: GBR, Delayed critical GBR, non-GBR; priority level: 1-127; PDB; PER; AW; MDBV)
    Maximum Flow Bit Rate downlink (MFBR downlink);
    Maximum Flow Bit Rate uplink (MFBR uplink);
    Guaranteed Flow Bit Rate downlink (GFBR downlink);
    Guaranteed Flow Bit Rate uplink (GFBR uplink);
    Notification Control;
    Maximum Packet Loss Rate downlink; and
    Maximum Packet Loss Rate uplink.
  It is N3IWF/TNGF instead of 5GS that generates Additional QoS Info who takes into account the 5G QoS profile received via N2 instead of N1
  The “Additional QoS Info” is used for the access between UE and N3IWF, instead of the other side.
Proposal:
  Question1: 5G QoS parameters (including QoS characteristics, GFBR/MFBR) are sent from SMF to PEGC to assist the deriving of N3GPP QoS parameters? Yes
  Two revisions: one have one not have KI#4
  If no consensus, SOH.
  Question2: for deriving 5G delay budget, whether PEGC sends the non-3GPP delay budget to PCF via NAS? Yes:no
  If no consensus, SOH.

## Slide 7
Issue of URSP and proposal
Traffic descriptor (TD) of URSP rule:
Alternative solutions:
  Alt#1: Extend TD of URSP for PIN traffic mapping, e.g., using “source descriptors” or “gateway descriptors”
  Alt#2: Do not extend URSP, but provisioning mapping info with URSP, e.g., TD uses DNN, and mapping info is <PIN ID, DNN>
  Other possible ways
Proposal:
  TBD (e.g., both URSP and PIN Routing Selection Policy are delivered to PEGC)
  Two revisions: one have URSP, another don’t, and if no consensus, SOH KI#4
Information name | Description | Note
Application descriptors | It consists of OSId and OSAppId(s). | The information is used to identify the Application(s) that is(are) running on the UE's OS. The OSId does not include an OS version number. The OSAppId does not include a version number for the application
IP descriptors | Destination IP 3 tuple(s) (IP address or IPv6 network prefix, port number, protocol ID of the protocol above IP). | A URSP rule cannot contain the combination of the Traffic descriptor components IP descriptors and Non-IP descriptors
Non-IP descriptors | Descriptor(s) for destination information of non-IP traffic | 
Domain descriptors | Destination FQDN(s) or a regular expression as a domain name matching criteria. | 
DNN | This is matched against the DNN information provided by the application. | 
Connection Capabilities | This is matched against the information provided by a UE application when it requests a network connection with certain capabilities. (NOTE 4) | The format and some values of Connection Capabilities, e.g. "ims", "mms", "internet", etc., are defined in TS 24.526 [19]. More than one connection capabilities value can be provided

## Slide 8
Issue of PDU Session number per PIN and proposal
Interim conclusion:
  A PEGC may establish a Single or multiple PDU Sessions used for PIN communication. One PEGC may serve more than one PIN and in this case, there is at least one PDU session per PIN
Other proposal:
  Shared PIN session that a PEGC transfers traffic of multiple PINs and other APP
  Dedicated PIN session that PEGC transfers traffic of one or multiple PINs
  Dedicated PIN session that per PDU session per PINE
Issue:
  Not clear what is the purpose for a PIN to have more than one PDU Sessions per PEGC
  QoS differentiation is able to be done by QoS flows
  If one PIN at a PEGC has two PDU Sessions is allowed, it is same that divide the PIN into two, and one per PDU Session
  If multiple PINs at a PEGC share one PDU Session, it is same that combines those PINs as one big PIN and uses sub-networks by PEMC/AF for those original PINs
Proposal:
  TBD (e.g., only one PDU session per PIN per PEGC/PEMC)