## Slide 1: Discussion on PIN issues
Zhenhua Xie
vivo
S2-2206979

## Slide 2
Issue of architecture and proposal
Two architecture alternatives:
  AF based
    Enhance AF-NEF/PCF functionalities for providing PIN parameters
    PIN parameters for PIN management include membership information, PEGC-PINE association information, etc.
    PIN topology information are exposed to AF for PIN management
    PIN parameters for PIN communication configuration include traffic descriptions
  Non-AF based
    PIN management is done among PEGC, PEMC, and PINE
    PEGC initiates PDU Session Establishment/Modification procedure according to PEMC’s command for PIN communication configuration
Issue of “AF based”:
  AF is not a trust entity to user (although the operator can authenticate and authorize the AF)
  Complicated security requirement related to privacy concern: topology, authorization of PEGC manipulation by PEMC via AF, etc.
  More coordination with SA3, which may delay the study significantly
Issue of “non-AF based”:
  PEMC’s command to 5GC is via PEGC, but PEGC is a UE that is weaker than AF/NF in security aspect, and could be easily malfunctioned, e.g., hacked
  User is not aware whether the 5GC uses the correct PIN communication configuration to make sure the PEGC is not malfunctioned

## Slide 3
Issue of architecture and proposal
Proposal:
  “non-AF based” is mandate
    User subscribes PIN service with GPSIs of PEMCs and PEGCs, and pre-configuration is used for statically managing 5GC resources for PIN, i.e., PIN session, which consist of multiple PDU Sessions from PEMC(s) and PEGC(s) that control is anchored at same SMF
    PIN communication configuration sent by PEGC to 5GC needs to be informed to PEMC, in order for user detecting PEGC malfunction
  “AF based” is optional, only for provisioning parameters without privacy concern, i.e.,
    URSP generation information per PIN service subscription instead of per UE
    QoS authorization information per PIN session (i.e., what kinds of QoS are allowed for a PIN)
    Possible non-3GPP related QoS information per PEGC that is not associated with a PIN session
  In case dynamic PIN session management is deployed (AF based), user should subscribe max number of PINs in the PIN service subscription to make 5GC authorizes the number of PIN session established according to AF request
  Makes the user aware of the PIN communication configuration used by 5GC without PEMC impact
    The PEMC subscribes the notification of PIN communication configuration to SMF via PEGC, e.g., sends the IP address and UDP port of PEMC to SMF
    The SMF sends the PIN communication configuration to the PEMC via UPF over PDU Session of the PEMC
      SMF exposing PIN communication configuration to AF then forwarding to PEMC will expose the PIN communication configuration, which has user privacy concern
    If PEGC is malfunctioned that does not sends the subscription or with wrong information, the PEMC will not receive the notification, and user will notice the PEGC’s malfunction, then the user can kick off the PEGC for fixing it, the PIN communication configuration made by the PEGC will be removed then

## Slide 4
Concept of PIN session
Consisting of multiple PDU Sessions of PEGC(s) and PEMC(s)
Transferring traffic of a PIN, including within the PIN and outside the PIN
Control is anchored at same SMF
Enable network local switch among those PDU Sessions

## Slide 5
High level overall procedure proposal
The user subscribes PIN service from operator with GPSIs of PEMCs and PEGCs, which result in policy pre-configuration
The AF is only used to manage 5G resources for PIN dynamically, the parameters are used for AM policy control and SM policy control
The PIN management including PIN communication configuration is done by PEMC
The PIN signaling exchange between PEMC and PEGC is over direct connection or via UPF(s), but not via AF
The PEGC establishes PDU Session for the PIN session and sends PIN communication configuration to SMF according to PEMC’s command
The PIN communication configuration in 5GC needs to be informed to PEMC, for the sake of user detecting malfunction

## Slide 6
Issue of URSP and proposal
Traffic descriptor (TD) of URSP rule:
Issues:
  IP range of a PIN may be determined during/after PDU Session Establishment
  PIN session is not application related
  Domain/Non-IP/Connection are not suitable for PIN
Information name | Description | Note
Application descriptors | It consists of OSId and OSAppId(s). | The information is used to identify the Application(s) that is(are) running on the UE's OS. The OSId does not include an OS version number. The OSAppId does not include a version number for the application
IP descriptors | Destination IP 3 tuple(s) (IP address or IPv6 network prefix, port number, protocol ID of the protocol above IP). | A URSP rule cannot contain the combination of the Traffic descriptor components IP descriptors and Non-IP descriptors
Non-IP descriptors | Descriptor(s) for destination information of non-IP traffic | 
Domain descriptors | Destination FQDN(s) or a regular expression as a domain name matching criteria. | 
DNN | This is matched against the DNN information provided by the application. | 
Connection Capabilities | This is matched against the information provided by a UE application when it requests a network connection with certain capabilities. (NOTE 4) | The format and some values of Connection Capabilities, e.g. "ims", "mms", "internet", etc., are defined in TS 24.526 [19]. More than one connection capabilities value can be provided

## Slide 7
Issue of URSP and proposal
Proposals:
  Alt#1: Extend TD of URSP for PIN traffic mapping, e.g., using “source descriptors” or “gateway descriptors”
    Pros:
      Is able to be used for gateway UE other than PIN feature, i.e., it is a solution with a common framework for matching by gateway UE
    Cons:
      PEMC does not know the extension so different URSP may be needed
      Different feature still need to specify different value type of the field, e.g., PIN ID for PIN feature and MAC address/device ID for 5WWC feature
      Application descriptors also is a kind of source, “source descriptors” may cause confusion
  Alt#2: Do not extend URSP, but provisioning mapping info with URSP, e.g., <PIN ID, DNN>, i.e., PIN policy consist of URSP and mapping info
    Pros:
      Using DNN for TD, network does not need to distinguish PEMC and PEGC for providing AM policy before PDU Session Establishment
      Different feature can use different mapping info without URSP enhancement
    Cons:
      Additional IE needs to be provisioned with URSP

## Slide 8
Issue of PDU Session number per PIN and proposal
Interim conclusion:
  A PEGC may establish a Single or multiple PDU Sessions used for PIN communication. One PEGC may serve more than one PIN and in this case, there is at least one PDU session per PIN
Issue:
  Not clear what is the purpose for a PIN to have more than one PDU Sessions per PEGC
  QoS differentiation is able to be done by QoS flows
  If one PIN at a PEGC has two PDU Sessions is allowed, it is same that divide the PIN into two, and one per PDU Session
Proposal:
  Only one PDU session per PIN per PEGC/PEMC