## Slide 1: FS_PIN: Way Forward for Open Issues
SA2#153e

## Slide 2: AF based architecture or NF based architecture
There’re two different opinions on architecture: AF based (A) or NF based (B)
Different architecture has different way for operations of PIN service
The basic concept for AF based architecture:
  AF for PIN is optional for PIN service
  If AF for PIN is used, it can provision parameters to NEF (for 3rd party AF) or UDM (internal AF), which will influence the 5GC to perform PIN service accordingly, e.g., provision policy to PEGC/PEMC, manage 5GS resources, differentiate routing control and QoS control, etc.
The basic concept for NF based architecture:
  AF is not used for PIN service
  The PIN service is requested from PEGC/PEMC via NAS signalling to an 5GC NF (e.g., SMF, PCF), the 5GC NF will accordingly provision policy to PEGCs/PEMCs (not only the PEGC/PEMC sending the request), manage 5GS resources, differentiate routing control and QoS control, etc.
The basic concept for architecture without none of the above
  all features are based on static configuration in relevant
NF based
AF based

## Slide 3: AF based architecture or NF based architecture
Q1: Do you want an NF based architecture ?
  Propose SoH on Alt#1: Yes() No()
Q2: Do you want an AF based architecture ?
Propose SoH on Alt#2: Yes() No()
Q3: Do you want to none of the above)?
Propose SoH on Alt#3: Yes() No()

## Slide 4: AF based architecture or NF based architecture
Open Issue #1: The way for requesting policy update for PDU Session selection sent to all PEGCs/PEMCs
  Alt #1: only bullet x4) in revision Y of S2-2209013 (KI#4) result from NF based architecture
    Propose SoH on Alt#1: Yes() No()
  Alt #2: only bullet x5) in revision Y of S2-2209013 (KI#4) result from AF based architecture
    Propose SoH on Alt#2: Yes() No()
  Alt #3: bullet x4) and x5) in revision Y of S2-2209013 (KI#4)
    Propose SoH on Alt#3: Yes() No()
Not needed since covered by questions in slide 1.
Anaswer to Question in slide 1 automatically solve these questions

## Slide 5: AF based architecture or NF based architecture
Open Issue #2: The way for managing PIN policy to activate/deactivate 5GC resources for a PIN
  Alt #1: only bullet x2) in revision Y of S2-2209178 (KI#3) result from NF based architecture
    Propose SoH on Alt#1: Yes() No()
  Alt #2: only bullet x1) in revision Y of S2-2209178 (KI#3) result from AF based architecture
    Propose SoH on Alt#2: Yes() No()
  Alt #3: bullet x1) and x2) in revision Y of S2-2209178 (KI#3)
    Propose SoH on Alt#3: Yes() No()
Not needed since covered by questions in slide 1
In case of both we must support both.
Answer to Q1 aaumtomatically answer to this questions

## Slide 6: AF based architecture or NF based architecture
Open Issue #3: The way for managing PINE
  Alt #1: only bullet x?) in revision Y of S2-2209178 (KI#3) result from NF based architecture
    Propose SoH on Alt#1: Yes() No()
  Alt #2: only bullet x3) in revision Y of S2-2209178 (KI#3) result from AF based architecture
    Propose SoH on Alt#2: Yes() No()
  Alt #3: bullet x?) and x3) in revision Y of S2-2209178 (KI#3)
    Propose SoH on Alt#3: Yes() No()
  Alt #4: none of the bullet x?) and x3) in revision Y of S2-2209178 (KI#3)
    Propose SoH on Alt#3: Yes() No()
Question on why PINE ID needs to be added in UDR is unclear and the question is missing.
Not understand the questions

## Slide 7: Identification
Background: If PINE has 3GPP credential, 5GC will have the identification of PINE, but if the PINE does not have 3GPP credential, there’s argument on UDR stores the PINE ID.
Open Issue #4: Whether UDR knows PINE ID
  Alt#1: bullet x4) in revision Y of S2-2209178 (KI#3)
    Propose SoH on Alt#1: Yes() No()
  Alt#2: no bullet x4) in revision Y of S2-2209178 (KI#3)
    Propose SoH on Alt#2: Yes() No()
Question on why PINE need to be known? for what?
If managed by AF is probably not necessary

## Slide 8: N3GPP QoS assistance information
Open Issue #5: Does the N3GPP QoS assistance mechanism as described in sol X is supported?
    Propose SoH on Alt#1: Yes() No()
Background: The non-3GPP access is used between PINE and PEGC, in order to assist the QoS management for the non-3GPP access in case the PEGC has the capability, there is a proposal to extend the currently N3GPP QoS assistance for Trusted/untrusted to PIN. The N3GPP QoS assistance information is proposed to be used to assist the PEGC to determine the QoS to be applied in N3GPP access connection to PINE.

## Slide 9: Policy to PEGC for PDU Session selection
Do we support the addition of a PIN Routing Selection Policy based on "Source descriptor" as proposed in solution #7, clause 6.7.2.2.4 (KI#4) ?
    Propose SoH on Alt#1: Yes() No()
  Left to implementation in PEGC
    Propose SoH on Alt#2: Yes() No()
If it is agreed that this is the question, can we solved without SOH?
Background: The PEGC may support multiple PINs, and each PIN may be associated to one PDU Session (whether to use one PDU session for PIN or more PDU session is left to implementation). The PINE’s traffic needs to be mapped into one of the PDU Sessions associated to PIN. The legacy URSP is not suitable for this purpose since the traffic descriptor (TD) of the URSP rule is for destination mapping while in this case the traffic from different PINES needs to associated to different PDU session irrespectively from the destination (e.g. 2 PINEs send traffic to the same internet server).

## Slide 10: N3GPP delay budget
Open Issue #6: Does the N3GPP delay budget mechanism need to be supported ?
    Propose SoH : Yes() No()
Background: The non-3GPP access is used between PINE and PEGC, in order to consider the whole delay budget between UPF and PINE, companies propose PEGC sends the N3GPP delay budget per QoS flow to PCF via NAS, so that PCF can deduce the delay budget sent to NG-RAN, and the whole delay budget between PINE and UPF will fulfil the service requirement on delay budget.

## Slide 11: End