## Slide 1: FS_PIN: Way Forward for Open Issues
SA2#153e

## Slide 2: AF based architecture or NF based architecture
There’re two different opinions on architecture: AF based (A) or NF based (B)
Different architecture has different way for operations of PIN service
The basic concept for AF based architecture:
  AF for PIN is optional for PIN service
  If AF for PIN is used, it can provision parameters to NEF (for 3rd party AF) or UDM (internal AF), which will influence the 5GC to perform PIN service accordingly, e.g., provision policy to PEGC/PEMC, manage 5GS resources, differentiate routing control and QoS control, etc.
The basic concept for NF based architecture:
  AF is not used for PIN service
  The PIN service is requested from PEGC/PEMC via NAS signalling to an 5GC NF (e.g., SMF, PCF), the 5GC NF will accordingly provision policy to PEGCs/PEMCs (not only the PEGC/PEMC sending the request), manage 5GS resources, differentiate routing control and QoS control, etc.
The result of SOH on questions related to this aspect will be used to deduce whether AF based is used, or NF based is used, or both are used (maybe some purposes are based on arch (A) or (B), some/all purposes are based on both (A) and (B) depends on implementation), and consider whether corresponding text is added/kept in conclusion of KI#1
NF based
AF based

## Slide 3: AF based architecture or NF based architecture
Open Issue #1: The way for requesting policy update for PDU Session selection sent to all PEGCs/PEMCs
  Alt #1: only bullet x4) in revision Y of S2-2209013 (KI#4) result from NF based architecture
    Propose SoH on Alt#1: Yes() No()
  Alt #2: only bullet x5) in revision Y of S2-2209013 (KI#4) result from AF based architecture
    Propose SoH on Alt#2: Yes() No()
  Alt #3: bullet x4) and x5) in revision Y of S2-2209013 (KI#4)
    Propose SoH on Alt#3: Yes() No()

## Slide 4: AF based architecture or NF based architecture
Open Issue #2: The way for managing PIN policy to activate/deactivate 5GC resources for a PIN
  Alt #1: only bullet x2) in revision Y of S2-2209178 (KI#3) result from NF based architecture
    Propose SoH on Alt#1: Yes() No()
  Alt #2: only bullet x1) in revision Y of S2-2209178 (KI#3) result from AF based architecture
    Propose SoH on Alt#2: Yes() No()
  Alt #3: bullet x1) and x2) in revision Y of S2-2209178 (KI#3)
    Propose SoH on Alt#3: Yes() No()

## Slide 5: AF based architecture or NF based architecture
Open Issue #3: The way for managing PINE
  Alt #1: none of the bullet x?) and x3) in revision Y of S2-2209178 (KI#3)
    Propose SoH on Alt#3: Yes() No()
  If the way forward for Alt#1 is No, then the following
  Alt #2: only bullet x?) in revision Y of S2-2209178 (KI#3) result from NF based architecture
    Propose SoH on Alt#1: Yes() No()
  Alt #3: only bullet x3) in revision Y of S2-2209178 (KI#3) result from AF based architecture
    Propose SoH on Alt#2: Yes() No()
  Alt #4: bullet x?) and x3) in revision Y of S2-2209178 (KI#3)
    Propose SoH on Alt#3: Yes() No()

## Slide 6: Identification
Background: If PINE has 3GPP credential, 5GC will have the identification of PINE, but if the PINE does not have 3GPP credential, there’s argument on UDR stores the PINE ID.
Open Issue #4: Whether UDR knows PINE ID
  Alt#1: bullet x4) in revision Y of S2-2209178 (KI#3)
    Propose SoH on Alt#1: Yes() No()
  Alt#2: no bullet x4) in revision Y of S2-2209178 (KI#3)
    Propose SoH on Alt#2: Yes() No()

## Slide 7: N3GPP QoS assistance information
Background: It is non-3GPP access that is used between PINE and PEGC, in order to assist the QoS management for the non-3GPP access in case the PEGC has the capability, companies propose SMF sends the N3GPP QoS assistance information to PEGC via NAS, the parameters of N3GPP QoS assistance information is already used between N3IWF/TNGF and UE but sent by N3IWF/TNGF to UE not via NAS.
Open Issue #5: Whether N3GPP QoS assistance information is sent from SMF to PEGC via NAS
  Alt#1: bullet 1) and corresponding NOTE in revision Y of S2-2209013 (KI#4)
    Propose SoH on Alt#1: Yes() No()
  Alt#2: no bullet 1) and corresponding NOTE in revision Y of S2-2209013 (KI#4)
    Propose SoH on Alt#2: Yes() No()

## Slide 8: N3GPP delay budget
Background: It is non-3GPP access that is used between PINE and PEGC, in order to consider the whole delay budget between UPF and PINE, companies propose PEGC sends the N3GPP delay budget per QoS flow to PCF via NAS, so that PCF can deduce the delay budget sent to NG-RAN, and the whole delay budget between PINE and UPF will fulfil the service requirement on delay budget.
Open Issue #6: Whether N3GPP delay budget needs to be sent from PEGC to PCF via NAS
  Alt#1: bullet 11) in revision Y of S2-2209013 (KI#4)
    Propose SoH on Alt#1: Yes() No()
  Alt#2: no bullet 11) in revision Y of S2-2209013 (KI#4)
    Propose SoH on Alt#2: Yes() No()

## Slide 9: Policy to PEGC for PDU Session selection
Background: The PEGC may support multiple PINs, and one PIN will use only one PDU Session. The PINE’s traffic needs to be mapped into one of the PDU Sessions associated to PIN. The legacy URSP is not suitable for this purpose as the traffic descriptor (TD) of the URSP rule is for destination mapping and is used to mapping traffic from upper layer application.
Open Issue #7: Whether extended TD of URSP rule is used or a PIN Routing Selection Policy is used
  Alt#1: bullet 9) and 9b) in revision Y of S2-2209013 (KI#4)
    Propose SoH on Alt#1: Yes() No()
  Alt#2: bullet x6) in revision Y of S2-2209013 (KI#4)
    Propose SoH on Alt#2: Yes() No()

## Slide 10: End