## Slide 1: FS_PIN: Way Forward for Open Issues
SA2#153e

## Slide 2: AF based architecture or NF based architecture
There’re two different opinions on architecture: AF based (A) or NF based (B)
Different architecture has different way for operations of PIN service
The basic concept for AF based architecture:
  AF for PIN is optional for PIN service
  If AF for PIN is used, it can provision parameters to NEF (for 3rd party AF) or UDM/PCF (internal AF), which will influence the 5GC to perform PIN service accordingly, e.g., provision policy to PEGC/PEMC, manage 5GS resources, differentiate routing control and QoS control, etc.
  If AF for PIN is not used, all features are based on static configuration in relevant
The basic concept for NF based architecture:
  AF is not used for PIN service
  The PIN service is requested from PEGC/PEMC via NAS signalling to an 5GC NF (e.g., SMF, PCF, or a new 5GC NF), the 5GC NF will accordingly provision policy to PEGCs/PEMCs (not only the PEGC/PEMC sending the request), manage 5GS resources, differentiate routing control and QoS control, etc.
The basic concept for architecture without none of the above
  all features are based on static configuration in relevant
NF based
AF based

## Slide 3: AF based architecture or NF based architecture
Q1: Do you want an NF based architecture ?
  Propose SoH on Alt#1: Yes() No()
Q2: Do you want an AF based architecture ?
Propose SoH on Alt#2: Yes() No()

## Slide 4: Identification and PINE management
Background: If PINE has 3GPP credential, 5GC will have the identification of PINE, but if the PINE does not have 3GPP credential, there’s argument on whether PINE management needs to be support by 5GC, e.g., UDR stores the PINE ID for a PIN.
Q: Whether PINE management needs to be support by 5GC or not
    Propose SoH: Yes() No()

## Slide 5: N3GPP QoS assistance information
Background: It is non-3GPP access that is used between PINE and PEGC, in order to assist the QoS management for the non-3GPP access in case the PEGC has the capability, companies propose SMF sends the N3GPP QoS assistance information to PEGC via NAS, the parameters of N3GPP QoS assistance information is already used between N3IWF/TNGF and UE but sent by N3IWF/TNGF to UE not via NAS.
Q1: Whether N3GPP QoS assistance info is sent from SMF to PEGC or not
    Propose SoH: Yes() No()
Q2: If Q1 is Yes, whether other parameters (e.g., ARP, Periodicity) are required?
    Propose SoH: Yes() No()

## Slide 6: N3GPP delay budget
Background: It is non-3GPP access that is used between PINE and PEGC, in order to consider the whole delay budget between UPF and PINE, companies propose PEGC sends the N3GPP delay budget per QoS flow to PCF via NAS, so that PCF can deduce the delay budget sent to NG-RAN, and the whole delay budget between PINE and UPF will fulfil the service requirement on delay budget.
Q: Whether N3GPP delay budget for PINE’s traffic over a QoS flow needs to be sent from PEGC to PCF or not
    Propose SoH: Yes() No()

## Slide 7: Policy to PEGC for PDU Session selection
Background: The PEGC may support multiple PINs, and one PIN will use only one PDU Session. The PINE’s traffic needs to be mapped into one of the PDU Sessions associated to the PIN. The legacy URSP is not suitable for this purpose as the traffic descriptor (TD) of the URSP rule is for destination mapping, and companies comment that the URSP is used to mapping traffic from upper layer application.
Q: Whether TD of URSP rule for PIN is enhanced or not
    Propose SoH: Yes() No()

## Slide 8: End