## Slide 1: FS_PIN: Way Forward for Open Issues
SA2#153e

## Slide 2: AF based architecture or NF based architecture
There’re two different opinions on architecture: AF based (A) or NF based (B)
Different architecture has different way for operations of PIN service
The basic concept for AF based architecture:
  AF for PIN is optional for PIN service
  If AF for PIN is used, it can provision parameters to NEF (for 3rd party AF) or UDM/PCF (internal AF), which will influence the 5GC to perform PIN service accordingly, e.g., provision policy to PEGC/PEMC, manage 5GS resources, differentiate routing control and QoS control, etc.
  If AF for PIN is not used, all features are based on static configuration in relevant
The basic concept for NF based architecture:
  AF is not used for PIN service
  The PIN service is requested from PEGC/PEMC via NAS signalling to an 5GC NF (e.g., SMF, PCF, or a new 5GC NF), the 5GC NF will accordingly provision policy to PEGCs/PEMCs (not only the PEGC/PEMC sending the request), manage 5GS resources, differentiate routing control and QoS control, etc.
The basic concept for architecture without none of the above
  all features are based on static configuration in relevant
NF based
AF based

## Slide 3: AF based architecture or NF based architecture
Q1: Do you want an NF based architecture ?
  Propose SoH: Yes() No()
Q2: Do you want an AF based architecture ?
Propose SoH: Yes() No()
Q3: Do you want an both NF and AF based architecture ?
Propose SoH: Yes() No()
Q4: Do you want none of the above ?
Propose SoH: Yes() No()

## Slide 4: Identification and PINE management
Background: There’s argument on whether PINE management, e.g., add/remove a PINE for a PIN, needs to be support by 5GC, which may enhance UDR to store the PINE ID for a PIN.
Q: Whether PINE management needs to be support by 5GC or not
    Propose SoH: Yes() No()

## Slide 5: Policy to PEGC for PDU Session selection
Background: The PEGC may support multiple PINs, and one PIN will use only one PDU Session. The PINE’s traffic needs to be mapped into one of the PDU Sessions associated to the PIN. The legacy URSP is not suitable for this purpose as the traffic descriptor (TD) of the URSP rule is for destination mapping, and companies comment that the URSP is used to mapping traffic from upper layer application.
Q1: Whether TD of URSP rule is enhanced to support routing of PIN traffic by PEGC UE or not
    Propose SoH: Yes() No()
Q: Whether a new UE policy “PIN Routing Selection Policy” is introduced to support routing of PIN traffic by PEGC UE or not
    Propose SoH: Yes() No()

## Slide 6: End