## Slide 1: Summary and coordination between FS_eNA_Ph3 KI#9 and FS_eLCS_Ph3 KI#4
3GPP TSG-WG SA2 Meeting #154,
Toulouse, France, November 14-18, 2022
S2-2210596
NOTE: this is also proposed in FS_eLCS_Ph3, S2-2210597, For information

## Slide 2
FS_eNA_Ph3 KI#9 studies the enhancement of NWDAF with finer granularity of location information
  TR23.700-81 v1.1.0
  11 solutions for KI#9 (#25, #26, #27, #54, #55, #56, #57, #58, #59, #70, #71)
  In SA2#153e, KI#9 evaluation and KI#9 interim conclusions have been completed
  In SA2#154, the evaluation and conclusion will be updated.
  Planning normative work will start in SA2#154ad (January 2023)
  2 open issues have been identified and need confirmations from eLCS_Ph3;
FS_eLCS_Ph3 KI#4 studies the interaction between Location Service and NWDAF
  TR23.700-71 v1.1.0
  6 solutions for KI#4 (#10, #11, #12, #13, #20, #35)
  In SA2#153e, KI#4 evaluations and KI#4 conclusions have been completed
  In SA2#154, normative work will start.
  Information will be shared with FS_eNA_Ph3
3GPP TSG-WG SA2 Meeting #154,
Toulouse, France, November 14-18, 2022
General

## Slide 3
- From LCS, NWDAF retrieves location data from the GMLC.
NOTE 3: How the NWDAF retrieves location information from LCS needs coordination with LCS KI#4.
- From LCS, NWDAF can collect finer granularity location data from LCS including timestamp, age of location, UE location with requested granularity, velocity (speed and orientation), LCS QoS (e.g. LCS accuracy), the indication of motion event occurrence, environment indication;
NOTE 4: Whether all the data collected can be provided by LCS need to be confirmed in eLCS_Ph3.
- The NWDAF provides a new analytic ID with location accuracy estimates as required by the conclusions of the eLCS-Ph3 study.
NOTE 5: Coordination with the eLCS-Ph3 study is required, whether the NWDAF needs to provide this
3GPP TSG-WG SA2 Meeting #154,
Toulouse, France, November 14-18, 2022
How the NWDAF determines from where to obtain finer granularity location information?
From the legacy system
From the LCS
The interface with the LCS system
The enhancements needed for LCS
The benefit to LCS
- The enhancements needed for AF and 5GC NFs (AMF, OAM…) other than LCS
Supporting analytics IDs, existing analytics ID enhancement, or new analytics ID
Enhancement to Output analytics
Enhancement to Analytics Filter
FS_eNA_Ph3 KI#9 Conclusions and identified coordination issues
Notes: Timestamp,  Solution#25, 27, 55, 57, 58
Age of location  Solution#25, 71
Velocity (speed and orientation)  Solution#25, 27, 55, 71
UE location with required granularity  Solution#57
LCS QoS (LCS accuracy)  Solution#57
Indication of motion evet occurrence  Solution#58
Environment indication  Solution#71

## Slide 4: FS_eLCS_Ph3 KI#4 Conclusions for information
3GPP TSG-WG SA2 Meeting #154,
Toulouse, France, November 14-18, 2022
NWDAF
GMLC
LMF (NWDAF consumer)
NWDAF
Ngmlc
NWDAF provides new analytics for Location Estimation Accuracy. The location accuracy analytics include horizontal or vertical accuracy, indoor/outdoor indication
NWDAF
The NWDAF retrieves location data from the GMLC using the Ngmlc services
To support privacy check, new LCS Client Type and Service Type will be defined.
To support reporting of finer granularity UE location information in a target geographical area in form of any shape comparing with TA/cell to the NWDAF, the enhancements for LCS system include:
The NWDAF provides to LCS system a target geographical area and a new location event reporting condition, i.e. reporting only when the UE locates in the exact target geographical area;
By comparing UE location information with the target geographical area, the LCS system reports the UE location information to the NWDAF once UE locates in the target geographical area
The NWDAF can retrieve indoor/outdoor indication if it can be decided by LMF.
The NWDAF can provides as part of Location Estimation Accuracy a ratio of NLOS/LOS measurements, if the LMF receives the NLOS/LOS measurement indicator from UE in the measurement report
Aspect#1: how the location services can benefit from NWDAF
Aspect#2: how the NWDAF use cases can benefit from location service
Aspect#3: how to provide location information to NWDAF
LCS

## Slide 5
3GPP TSG-WG SA2 Meeting #154,
Toulouse, France, November 14-18, 2022
Open issues and proposals
In FS_eNA_Ph3 KI#9
  Open issue #1: The NWDAF provides a new analytic ID with location accuracy estimates as required by the conclusions of the eLCS-Ph3 study.
  FS_eLCS_Ph3 is expected to help confirm, whether such new analytics ID is needed.
  Open issue #2: KI#9 supporting use cases need LCS enhancement, especially the identified parameters, such as timestamp, age of location, UE location with requested granularity, velocity (speed and orientation), LCS QoS (e.g. LCS accuracy), the indication of motion event occurrence, environment indication are expected to be provided
  FS_eLCS_Ph3 is expected to help confirm, whether the LCS system can provide such parameters
    If yes, when FS_eNA_Ph3 can obtain the answers
    If no, can these parameters be provided in eLCS_Ph3 normative work?
In FS_eLCS_Ph3 KI#4
  No open issues for discussion.