## Slide 1: Observations for 5GC to support Member Selection Assistance Functionalities
Rapporteur:
OPPO, Oracle
AIMLsys
3GPP TSG-SA2 Meeting #154
Toulouse, France, Nov 14 - 18, 2022
S2-2210862

## Slide 2: Content Summary
What has been discussed about Member Selection Assistance Functionality?
What are the Member Selection Criteria (inputs from AF -> 5GC)?
What are the Candidate UE List, Time Windows & Member Policy (output from 5GC -> AF)?
Where should we host the Member Selection Assistance Functionality?
Way Forward

## Slide 3: What has been discussed about Member Selection Assistance Functionality?
candidate UE-list-c
and/or
Event Report /
Notification
Tentative UE-list-C
+
Member
Selection Criteria - Z
and/or
Event Subscription - O
candidate UE-list-b
and/or
Event Report /
Notification
Tentative UE-list-B
+
Member
Selection Criteria - Y
and/or
Event Subscription - N
candidate UE-list-a
and/or
Event Report /
Notification
Tentative UE-list-A
+
Member
Selection Criteria - X
and/or
Event Subscription - M
Application AI/ML AF
Latest definition from SA2#153E (subject to be further enhanced)
  Functionality offered by a 5GC NF which receives a request from Application AIML AF to provide a list of candidate UEs and additional information for the AF to perform FL. The 5GC NF then triggers the corresponding 5GC procedures to derive the set of candidate UE list as part of the assistance to be reported back to the AIML AF.
Process to support a particular round of Application AI/ML Member Selection
NF-i
NF-j
NF-k
candidate UE-list-c
and/or
Event Report /
Notification
Tentative UE-list-C
+
Member
Selection Criteria - Z
and/or
Event Subscription - O
candidate UE-list-b
and/or
Event Report /
Notification
Tentative UE-list-B
+
Member
Selection Criteria - Y
and/or
Event Subscription - N
candidate UE-list-a
and/or
Event Report /
Notification
Tentative UE-list-A
+
Member
Selection Criteria - X
+
Event Subscription - M
Application AI/ML AF
Process to support a particular round of Application AI/ML Member Selection
NF-i
NF-j
NF-k
Tentative UE-list-W + a list of
Selection Criteria – X+Y+Z
and/or
Event Subscription – M+N+K
candidate UE-list-w
and/or
Aggregated Event Report /
Notification
Member Selection
Assistance Functionality
Without
With
Member Selection
Assistance Functionality
Last SA2#153E
Working
Assumptions
1
2
3
4
1
2
3
3
3
4
1
2
3
4
1
2
3
4
3
4
1
2

## Slide 4: What are the key functionalities of Member Selection Assistance Functionality?
Enabling “Single” point of contact in 5GC to handle specific AF initiated group member selection service request and to provide the aggregated report to respond to the AF’s request.
  Opportunity to optimize the handling of the list of member selection criteria N MSAF_A(Criteria = X+Y+Z) vs. separated handling of multiple selection criteria Nx + Ny + Nz + …. for a single member selection operation.
  e.g. Solution#18, Solution#38, Solution#46 demonstrate the AF which requests 5GC assistance to identify the group of candidate UEs by providing a list of criteria
Intercepting a list of Member Selection Criteria (see next page for more details) requested by the AF to provide necessary service translation on the criteria before triggering the individual 5GC operation to fulfill the selection criteria.
Coordinating the individual 5GC NF to respond to the Member Selection Criteria in order to derive the target candidate member list.
  As part of the coordination support operation, Member Selection Assistance Functionality may assist different 5GC NFs such as PCF, NWDAF, SMF, AMF, UPF etc. to obtain the required input parameter(s) which may be come from the output of another 5GC NF after it responds to specific criterion
Deriving the candidate member list by aggregating the individual service responses from different 5GC NFs
Reporting back to the AF for the candidate UE list and/or corresponding Time Windows and/or corresponding Member policy for the upcoming group data transmissions
  See next page for more details on the Candidate UE list, Time Windows and Member policy

## Slide 5: What are the Member Selection Criteria (inputs from AF -> 5GC)?
Member Selection Criteria – AF specified requirements to 5GC for the assistance to select the UE according to the UE’s Identity, UE’s connection status (e.g. S-NSSAI, DNN, MA configuration, 3GPP vs. n3GPP access etc.), UE’s conditions (e.g. UE’s location), QoS performance and UE’s characteristics (e.g. UE’s mobility pattern, trajectory etc.).
The list of parameters for the criteria is as follows:
  UE Identity
    UE or UE List (GPSIs, SUPIs, External Group ID, or IP Addresses ) or any UE
  UE consent
  UE connection status
    S-NSSAI, DNN, MA configuration, UE’s access type (i.e. 3GPP vs. n3GPP access etc.), stationary/mobile, UE reachability, UE abnormal behavior
  UE condition
    UE’s location (current location, historical location, trajectory, direction, proximity to target etc.), loading condition,
  QoS performance
    QoS configuration in PCF, QoS monitoring results, QoS sustainability, throughput UL/DL etc.
  UE characteristics
    UE’s mobility pattern, trajectory etc.

## Slide 6: What are the Candidate UE List, Time Windows & Member Policy (output from 5GC -> AF)?
UEs in Candidate UE List
  UE IDs, number of UEs required to perform the requested Application AI/ML operation (e.g. for each federated learning cycle),
  Percentage of UEs that should take part in requested Application AI/ML operation from each sub-area, and/or a minimum number of UEs and /or a maximum number of UEs that should take part in requested Application AI/ML operation from each sub-area.
Time Window
  Time window for performing the specific Application AI/ML operation.
  Different candidate UE list could be provided for different time windows.
  NOTE: The granularity of the time window should be corresponding to the time window(s) which is/are requested by the AF. It could apply to the entire Application AI/ML operation or some cycles of the Application AI/ML operation.
Member Policy
  Member policy to be applied to each member in the target Application AI/ML operation (e.g. predicted QoS parameters for the UEs in the candidate list). If the time window is provided, the member policy is related to the corresponding time window.

## Slide 7: Where should we host the Member Selection Assistance Functionality?
NEF
  NEF needs to be supported even though it is a trusted AF
NWDAF
  Fundamental change to the internal logic of NWDAF and processing performance because NWDAF is intended to provide statistical/hysteresis information processing of which the life cycle of the date sets require long term derivation – the operation behavior is 100% opposite to support the data sets required for the run-time Application AI/ML operation
  Furthermore, scope of NWDAF is for Network operation and is NOT for application operation
new 5GC NF
  Clean slate approach to support new functionalities, new services for 5G system to support Applications
  new NF to be introduced to 5GC, require additional management overhead

## Slide 8: Way Forward
TBD …
Agree!
Oui!
Jawhol!
Si!
同意!

## Slide 9
Comments, AOB Anyone?