## Slide 1: FS_eNA_Ph3+eNA_Ph3: Way Forward for Open Issues
SA2#154
2022.11.15

## Slide 2: KI#1: How to improve correctness of NWDAF(1/2)
Background
  Regarding feedback information, one Editor’s Note is listed in KI#1 conclusion and quite a few papers submitted this meeting as well as in conf call before meeting:
  Editor's Note: The analytics consumer NF making some decision may change the trend indicated by the prediction output. The analytics consumer NF may provide a unified feedback related to the effect of an analytics on the changes in network status after the consumption of analytics. How to define such unified feedback and based on which logic is FFS.
Q1: It is proposed to first decide whether consumer NF provides feedback information to NWDAF, which is taken into account by NWDAF for better Accuracy Calculating:
  Yes
  No

## Slide 3: KI#1: How to improve correctness of NWDAF(2/2)
Q2: Regarding how to feedback information, if yes for the first question in previous slide, which solution(s) are to be chosen as baseline solution in R18:
  Option a: whether the consumer NFs do actions
  Yes No
  Option b: In addition to option a, if action is performed, further indicate whether the actions affect the network (based on the consumer NFs’ internal logic) The feedback info may also include service area/NF impacted.
  Yes No
  Option c: indicate whether the network performance or user experience are improved e.g. by comparing network KPIs without/with action taken by NF consuming data analytics (proposed by Huawei)
  Yes No

## Slide 4: KI#4: How to Enhance Data collection and Storage (1/2)
Background
  The conclusion in KI#4 documented so far only includes the storage of ML model in ADRF and there is no conclusion on which NF is allowed to retrieved a ML model from the ADRF. There are no related solutions in the TR so far.
Q1: Which NF is allowed to retrieve a ML model from the ADRF?
  Option A: an NWDAF containing MTLF that stores a ML model in ADRF should be the only NF allowed to retrieve the stored the ML model from the ADRF
  Yes: No:
  Option B: When an NWDAF containing MTLF (referred to as NWDAF 1) stores an ML model in ADRF, in addition to NWDAF 1, should other NWDAF containing MTLF in the network be allowed to retrieve the ML model stored in ADRF by NWDAF 1
  (NOTE: The model provided from the ADRF to other NWDAF containing MTLF is aligned with the conclusion of KI#5.)
  Yes: No:
  Option C: When an NWDAF containing MTLF (referred to as NWDAF 1) stores an ML model in ADRF, in addition to NWDAF 1, should other NWDAF containing AnLF in the network be allowed to retrieve the ML model stored in ADRF by NWDAF 1
  (NOTE: The model provided from the ADRF to other NWDAF containing AnLF is aligned with the conclusion of KI#5.)
  Yes: No:

## Slide 5: KI#4: How to Enhance Data collection and Storage (2/2)
Background
  The KI#4 conclusion agrees that the MTLF can sends the ML model address to ADRF by triggering ADRF's ML model storage service. So far there is no definition for ML model in SA2.
  Whether and how the MTLF send the ML model itself to ADRF using 3GPP defined service based interface is FFS.
Q1: How MTLF send the ML model to ADRF using 3GPP defined service based interface?
  Option A: The ML model itself will not be sent from the MTLF when triggering ADRF's ML model storage service. Only the ML model address is included.
  Yes No
  Option B: The ML model itself will not be sent from the MTLF when triggering ADRF's ML model storage service. Something with clear definitions (e.g., container for ML model, etc.) can be included
  Yes No
  Option C: The ML model itself can be sent from the MTLF when triggering ADRF's ML model storage service. The detail is left to stage-3 work
  Yes No