## Slide 1: Discussion about feedback information
vivo

## Slide 2: Background
One Editor’s Note is listed in KI#1 conclusion:
  Editor's Note: The analytics consumer NF making some decision may change the trend indicated by the prediction output. The analytics consumer NF may provide a unified feedback related to the effect of an analytics on the changes in network status after the consumption of analytics. How to define such unified feedback and based on which logic is FFS.
In general, it looks interesting and beneficial to discuss how NWDAF take into account the feedback information from the analytics consumer NF to better calculate Accuracy
One alternative could be that, based on the feedback information, NWDAF does not use the ground truth data (which may be affected by the actions taken by the consumer NF) to calculate Accuracy.
Notes: Discuss on whether and how to use / define this unified feedback information – consumer NF to NWDAF,
After the NF receive the analytic results, the NF could decide xxx
The consumer NFs must know if they do any action and may know if the actions affect the networks.
Sync – in sync – sync up

## Slide 3: Discussion
3 scenarios are listed in the table below
# scenarios | whether NF consumer do actions | whether ground truth data affected | Examples | 
1 | Does actions | No impact | 6.7.2 UE mobility analytics | Consumer AMF receives UE mobility analytics and decides to optimize paging strategy. The ground truth data (UE moving trajectory) will not be affected
2 | No action | No impact | 6.4: Observed Service Experience related network data analytics | Consumer PCF receives Service Experience analytics and decides to do not necessarily perform any actions as everything looks good. Therefore the ground truth data (Observed Service Experience ) will not be affected.
3 | Does actions | Has impacts | 6.4: Observed Service Experience related network data analytics | Consumer PCF receives Service Experience analytics and decides to increase authorised GBR as application Service Experience is not good . Therefore the ground truth data (Observed Service Experience ) will be affected.
Observation1: Consumer NF consuming data analytics may not take any action, which does not affect ground truth and not change the trend indicated by the prediction output
Observation2: Even consumer NF consuming data analytics does take any action, which could or could not affect ground truth and not change the trend indicated by the prediction output

## Slide 4: Proposal (1/2)
It is proposed consumer NF provides feedback information to NWDAF, which is taken into account by NWDAF for better Accuracy Calculating
Regarding how NWDAF utilize feedback information e.g. remove the affected data is vendor implementation and not standardized.
Notes: It is useful for the NWDAF to know these information and calculate the accuracy correctly.

## Slide 5: Proposal (2/2)
Regarding feedback information, threes alternative options are listed:
  Option a: whether the consumer NFs do actions.
  Option b: In addition to option a, if action is performed, further indicate whether the actions affect the network (based on the consumer NFs’ internal logic).
  Option c: indicate whether the network performance or user experience are improved e.g. by comparing network KPIs without/with action taken by NF consuming data analytics (proposed by Huawei).
It is proposed
  choose option a as baseline solution in R18
  discuss whether option b is clear enough to capture it in R18
  delay option c to future release as we need more time to study how to evaluate network performance improvement
Notes: It is useful for the NWDAF to know these information and calculate the accuracy correctly.

## Slide 6
Backup slides

## Slide 7: Do action and no impact (scenario 1)
For the example of scenario B, AMF (NF consumer) requests the UE mobility predictions as defined in clause 6.7.2 of 23.288. The NWDAF returns a location information to indicate that the TA or cells where the UE may move into. AMF changes the mobility pattern and optimize paging strategy, and it will not affect the UE behaviour and the TA or cells where the UE move into.
In this situation, the consumer NF do actions, but the actions cannot affect the networks. The UEs will move into the TA or cells as their wills, thus, the ground truth will not be affected and the NWDAF can calculate the correct accuracy.
PCF request and receives the prediction results of the the UE mobility predictions
Results is a TA or cell
AMF changes the mobility pattern and optimize paging strategy
cannot affect the UE behaviour and the TA or cells where the UE move into.
Notes: Change mobility pattern to optimize the paging and
optimized paging strategy

## Slide 8: No action and No impact (scenario 2)
For an example of scenario A, the PCF (consumer NF) requests the predictions of the Service Experience for an Application from NWDAF as defined in clause 6.4 of 23.288. If the results (e.g. Mean Opinion Score (MOS)) fulfil the requirements for this application, the PCF will do nothing.
In this situation, the consumer NF will not do any action and the values in network will not be affected. Thus, the ground truth will be same as it should be, and the accuracy will be calculated correctly.
PCF request and receives the prediction results of the the Service Experience for an Application
Results is a MOS and fulfil the requirements
PCF do nothing
QoS is same as it should be, and the accuracy will be calculated correctly
Notes: Accuracy 被影响，因为xxx，比如计算公式和哪个地方被影响了

## Slide 9: Do actions and has impact (scenario 3)
For an example of situation 1, the PCF (consumer NF) requests the predictions of the Service Experience for an Application from NWDAF as defined in clause 6.4 of 23.288. If the results (e.g. Mean Opinion Score (MOS)) does not meet the requirements for this application, the PCF will raise the QoS value to improve the MOS score.
This modification changes the QoS level, the MOS will be affected and not be the same as the value without the modification due to the raised QoS level will raise the MOS. In other words, the ground truth in the network is affected and the accuracy cannot be calculated correctly.
If the NWDAF can realize the data related to this actions has been affected, it can remove them and generate the correct accuracy. In order to identify if a network is affected, NWDAF may need to know if consumer NF do actions and if the actions affect the network.
PCF request and receives the prediction results of the the Service Experience for an Application
Results is a low MOS and cannot meet the requirements
PCF turn up the QoS level to improve the MOS
QoS is changed and MOS is affected to be not same as the prediction results
Notes: Accuracy 被影响，因为xxx，比如计算公式和哪个地方被影响了