## Slide 1: Discussion on device compliance to 3GPP specifications
CMCC, [Telecom Italia], ZTE, Xiaomi, [OPPO], CATT, Vivo
3GPP TSG SA WG2 Meeting #155 S2-2302428
Electronic Meeting, February 20 – 24, 2023

## Slide 2: A general solution to identify non-3GPP-compliant devices is needed
Observation 1:
  As indicated in [1] and [3], a general solution is expected by operators to identify the non-3GPP-compliant devices unknown to the network.
  As indicated in [2] and , as for the non-3GPP-compliant devices need to be rejected or allowed, this is preferred to be operator depended. Operators can reject the non-3GPP-compliant devices, and also may allow the non-3GPP-compliant devices.
  As summaried in [4], 3GPP companies acknowledge the non-3GPP-compliant UE issues. It is observed that there are non-3GPP-compliant UEs in the field, which do not support mandatory features defined in 3GPP RAN. TSG RAN has discussed how to handle this issue, and proposal on architecture enhancement is also provided and discussed. However, no consensus has been reached, and quite a few companies think SA2 may help RAN on this issue.
Proposal 1: 3GPP to work out a solution to identify the non-3GPP-compliant devices for the interested bodies.

## Slide 3: The testing/conformance/regulatory bodies can be involved
Observation 2:
  As company indicated in [2], the devices which originated this issue are not certified and cannot be certified and are unknown to the network. To identify the non-certified devices can help to resolove this issue.
  As company suggested in [2], the proponents should co-ordinate with the testing/conformance/regulatory authorities in terms of understanding the device’s abilities.
Proposal 2: 3GPP to co-operate with certification bodies (e.g. GCF) to work out a solution to enable networks to identify the non-certified devices or non-3GPP-compliant devices. The potential solution could be
  network to send UE-Certification Validation Information to the certification bodies (e.g. GCF)
  certification bodies to validate whether the UE has passed the certification and send success/failure results to network
The procedures above can be implemented after or before UE registration completed.

## Slide 4: An example solution for Proposal 2
UCV Server: UE-Certification Validation Server (e.g. GCF Server), used to store the UE certification information
UCV Function: UE-Certification Validation Function Unit, to help to route to the target UCV Server
Proposal 3: SA2 to evaluate the feasibility of Proposal 2, and to work out a solution accordingly.
UCV: UE-Certification Validation
UCV Information: UE-Certification Information, any information can help to identify the specific certification activities in certification body, e.g. REF in GCF, Marketing name, Model name, IMEI, etc.

## Slide 5: Reference
[1] RP-222163 On device compliance to 3GPP specifications; Telecom Italia, Telefonica, Orange, Bouygues Telecom; RAN#97e September 12-16, 2022.
[2] RP-222562 [97e-02-DevCompliance]; RAN#97e September 12-16, 2022.
[3] RP-223071 Discussion on device compliance to 3GPP specifications; CMCC, Telecom Italia, ZTE; RAN#98e December 12-16, 2022.
[4] RP-223443 [98e-03-DevCompliance]; RAN#98e December 12-16, 2022.
Notes: (2022-3)

## Slide 6: Thank you!