## Slide 1: AF interacting with VPLMN
EDGE_Ph2
KI#1/HR
Source: Huawei, HiSilicon

## Slide 2: Background
TR 23.700-48 v18.0.0
  NOTE 2: The baseline procedure for AF triggered EAS Re-discovery for an AF interacting with VPLMN will be determined in normative phase.
In Rel-17 EC procedures, AF needs to interact with 5GC in the following procedures:
  AF influence on traffic routing procedure to support
    N6 traffic routing requirement provisioning
    AF triggered EAS re-discovery
    AF triggered EAS IP replacement
    AF change during Edge relocation
    ……
  User plane management event exposure(e.g. exposure of DNAI change)
    UE mobility triggered Edge relocation
    AF change during Edge relocation
    …..
  EDI provisioning from AF
For HR-SBO case, if an AF can only interact with VPLMN, how to support the above procedures in VPLMN is not clear.
Especially, AF influence on traffic routing procedure goes through PCF, while it was concluded that “no V-PCF in VPLMN”, thus how the AF can perform “AF influenced traffic routing” needs to be investigated.

## Slide 3: Potential solutions to support AF influence procedure for HR-SBO
Alt#1: V-NEF interacts with V-SMF directly without V-PCF
Alt#2: V-NEF interacts with V-SMF via V-PCF
Alt#3: V-NEF interacts with V-SMF via HPLMN
Alt#4: If a V-AF can only interact with VPLMN, AF influenced traffic routing procedure will not be supported.
V-UDR
V-PCF
V-UPF
UE
V-SMF
AMF
H-UPF
H-SMF
RAN
H-PCF
UDM
AF
V-NEF
H-NEF
L-DN
L-PSA
Alt#2
Alt#3
Alt#1

## Slide 4: Pros vs. Cons of alternatives
Alternatives | Pros | Cons
#1 (AF-vNEF-vUDR/vUDR-vNEF-vSMF) | 1. AF influenced procedure can be supported 2. HPLMN is not involved. | 1. A new service operation is needed between vSMF and vNEF for AF influence data retrieval.
#2 (AF-vNEF-vUDR/vUDR-vPCF-vSMF) | 1. AF influenced procedure can be supported 2. HPLMN is not involved. | 1. vPCF is introduced, which may cause potential conflicting with hPCF on QoS control.
#3 (AF-vNEF-hNEF-hUDR/hUDR-hPCF-hSMF-vSMF) | 1. Existing AF influenced procedure in HPLMN can be reused. | 1. New interface between vNEF and hNEF is needed. 2. HPLMN is involved, which may not possible due to business reason (AF in vPLMN may not want to provide info via another PLMN to it’s own PLMN). 3. Potential long latency
#4 (no support for AF influenced.) | Less CR | Impossible to support some procedures critical for EC, including AF provisioning of N6 traffic routing, Edge relocation and EAS re-discovery.
Alt 1 is proposed as way forward. Corresponding CRs are submitted to SA2#155.

## Slide 5: Thanks!