## Slide 1: Discussion on Common API and Separate APIs Editor's note: API will be merged with common one (Nnef_AFSessionWithQoS …) at the next meeting
Huawei, HiSilicon

## Slide 2: Background
C3-230783 from CT3 would like to kindly ask SA2:
  Whether SA2 is planning to merge these two APIs into a single one?
  What is the common part and/or difference between the Nnef_AFRequestForQoS service API and the Nnef_MultiMemberAFsessionWithQoS service API?
In SA2#154AH, GMEC defines a new dedicated NEF service API, i.e. Nnef_AFRequestForQoS, to support the provisioning of traffic characteristics and the monitoring of performance characteristics for a UE or a group of UEs
  Introduction of a new dedicated NEF service API is a result from analysis of whether to use new NEF service or extend existing NEF service, the analysis lasts for several meetings.
In SA2#155, AIMLsys defines Nnef_MultiMemberAFsessionWithQoS service
  Originally, Nnef_MultiMemberAFsessionWithQoS targets for the Group ID, but change the target to a list of UE addresses
Observation: Adoption of new NEF service was preferred by GMEC group over extending the existing NEF service, and GMEC as well as CT3 doesn’t express any technical concerns to use the separate NEF API

## Slide 3: Situation
Certain similarity in functionality and commonality of some parameters but only wrt. the control over the QoS and the QoS monitoring for a service flow of an individual UE‘s PDU Session
Considerable differences in functionality and related control parameters (see also Annex for details):
  Existing API (AFSessionWithQoS) with Rel18 enhancements:
    single UE address
    TSC related parameters
    XRM related parameters, XRM multiple service flow concept
  GMEC API (MultiMemberAFSessionWithQoS):
    Group ID
    Maximum Group Data Rate monitoring/enforcement, Temporal invalidity conditions
  AIML API (AFRequestForQoS):
    list of UE addresses
    Maximum Consolidated Data Rate monitoring (with separate list of UE addresses)
Different procedures are necessary anyway
Observation: While some parameters are used in all APIs, many/most parameters are API specific

## Slide 4: Common API vs Separate API
Pros for common API:
  Re-use of specification and implementation related to those parameters that are common to all APIs
Cons for common API:
  Parameter profiling required (i.e. the specification of which parameters can be provided together and in which scenario)
  Criteria have to be defined for the NEF to determine which procedure to execute
    Perhaps individual UE address, group ID, list of UE addresses
  Finding an appropriate NEF which supports the required procedure/features becomes more complicated
  The future evolution of the API becomes more complicated
    More scenario specific functionality and parameters are likely to be added
    Parameters could be used differently depending on the scenario/procedure
Conclusion: There are certain risks and problems for a common API and the potential simplification on the service level is just shifting the complexity to the parameter level
Proposal: Keep AFSessionWithQoS, MultiMemberAFSessionWithQoS and AFRequestForQoS separate.

## Slide 5: A possibility to Optimize AFRequestForQoS
Other Proposal: Simplify the GMEC procedure
Alternative A, Use only UDM+UDR as NF for coordination of group context/state:
  1) Extend the PP service to support GMEC needs, considering the QoS provisioning is not so frequent, QoS provisioning can be stored as part of subscription data, see solution 2 in 23.700-74. Or 2) Extend the SP service to support GMEC needs, i.e. 5GC receive GMEC specific parameters and store it in the 5GC for the 5GC to enforce, see S2-2301193/ S2-2301194 at SA2#154AH
  AFRequestForQoS would then not be needed as separate service/API anymore
Alternative B, Use only NEF as NF for coordination of group context/state:
  1) Keep the current AFRequestForQoS NEF Service. 2) Move group context handling from TSCTSF/UDR to NEF, NEF resolves group members, subscribes for UE connectivity and interacts with PCF(s) in the same way as defined for the MultiMemberAFSessionWithQoS procedure.

## Slide 6: Simplification for GMEC Procedures (Alternative A)
Current procedures
Notification
per PCF
Retrieval of group data
Notification
per TSCTSF
NEF
UDM/UDR
SMF
TSCTSF
PCF
RAN
UE
UE
UE
UE
UE
PP Request for Group
PP Request for Group
Pre-processing
Connected UEs
Un-Connected UEs
UDM+UDR based Procedure
Optionally, move Pre-processing to NEF to avoid TSCTSF in Path
NEF
UDR
SMF
TSCTSF
PCF
RAN
UE
UE
UE
UE
UE
AFRequestForQoS Request for Group
a) Request for Group
Request per member
Request per member
Group Coordination
&Pre-processing
b) Request for Group
Notification
per PCF
Connected UEs
Un-Connected UEs
PP service is used for group data provisioning, e.g. default QoS, group data, service area
NEF
UDM/UDR
PP Request
for Group
PP Request
for Group
PP service is used for group data provisioning, e.g. default QoS, group data, service area and for dynamic QoS, QoS monitoring ..

## Slide 7: Annex

## Slide 8: Commonalities
AF Identifier, Flow description(s) or External Application Identifier, DNN if available, S-NSSAI if available
QoS Parameters to be provisioned
  QoS Reference or individual QoS parameters as described in clause 6.1.3.22 of TS 23.503 [20], Alternative Service Requirements (containing one or more QoS reference parameters or Requested Alternative QoS Parameter Sets in a prioritized order)
QoS to be Monitored
  QoS parameter(s) to be measured, Reporting frequency, Target of reporting and optional an indication of local event notification as described in clause 6.1.3.21 of TS 23.503 [20]
  Sponsored data connectivity information
  time period, traffic volume
OutPut: Transaction Reference ID
Observation: The above set of parameters are common between GMEC API and AIMLsys API

## Slide 9: Specifics for AFSessionWithQoS
AFSessionWithQoS
  Target: UE address, for a UE with established PDU Session (IP or Ethernet)
  TSC Traffic characteristics as described in clause 6.1.3.23 or 6.1.3.23a of TS 23.503 [20]
  XRM Parameters: Multi-Model Service ID, Multi-modal Service Requirements, RT Latency Indication as described in clause 6.1.3.22 of TS 23.503 [20], PDU Set QoS Parameters as described in clause 5.7.7 of TS 23.501 [2], Protocol Description (Indicates RTP/SRTP header type used by the flow)
  Output: result.
  Procedure: involvement of the TSCTSF based on operator configuration
  Functionalities: PCF for enforcement of XRM, TSCTSF for processing of TSC Parameters
  More, e.g. PIN?

## Slide 10: Specifics for MultiMemberAFSessionWithQoS
MultiMemberAFSessionWithQoS
  Target: a list of UE addresses (i.e. IP addresses), for UEs with established IP PDU Session
  QoS Monitoring event for Data Rate Monitoring for a list of QoS flows： Consolidated-MBR Threshold, a list of UE addresses subjected to Consolidated-MBR monitoring
  Output: result for the success or failure of the request corresponding to individual UE(s) in the list.
  Procedure: NA
  Functionalities: NEF functionality for enforcement of the Data Rate Monitoring for a list of QoS flows, NEF translation of the a list of UE addresses to request for each UE address and does aggregation
Observation: Compared to AFSessionWithQoS, MultiMemberAFSessionWithQoS is a combination of AFSessionWithQoS procedures executed for each UE address in the requested list, with additional NEF enforcement of Data Rate Monitoring for a list of QoS flows with collected monitoring reports. However, parameters, functionalities and procedures defined for XRM/TSC for AFSessionWithQoS is not applicable for MultiMemberAFSessionWithQoS.
Proposal: Keep MultiMemberAFSessionWithQoS Separate

## Slide 11: Specifics for AFRequestForQoS
AFRequestForQoS
  Target: GPSI or Group ID, for both UEs with established PDU Sessions and UEs with any future PDU Sessions
  Flow Descriptions: Only the server side information as Flow Description, e.g. 3-tuple(s) including protocol, server side IP address and port number
  TSC Traffic characteristics as described in clause 6.1.3.23 or 6.1.3.23a of TS 23.503 [20]
  Temporal invalidity condition (start-time, end-time)
  Monitoring of specific performance characteristic by requesting the Notification control with Alternative QoS Profiles
  Output: result.
  Procedure: involvement of the UDR or TSCTSF based on operator configuration
  Functionalities: Group coordination at PCF or TSCTSF, PCF can supplement the UE side information, e.g. UE IP address and port
  Observation: Compared to AFSessionWithQoS, the backend procedures, needed functionalities and specific parameters for AFRequestForQoS are distinctly different
  Proposal: Keep AFRequestForQoS Separate

## Slide 12: Extending other NEF services consideration
ParameterProvision
  Function: allowing external party to provision of information which can be used for the UE in 5GS
  Target: GPSI, UE address, Group ID
  Limitation for GMEC API: No support of provisioning of flow description, traffic characteristics, QoS parameters to be enforced, QoS parameters to be monitored etc. as part of the subscription data
  Proposal: Alternatively, Extend the PP service to support GMEC needs, considering the QoS provisioning is not so frequent, this limitation can be ignored.
ServiceParameter
  Function: allowing external party to provision of service specific parameters which can be used for the UE via UE policy
  Target: GPSI, UE address, Group ID
  Limitation for GMEC API: No need to impact UE policy after provisioning of flow description, traffic characteristics, QoS parameters to be enforced, QoS parameters to be monitored etc. as part of the subscription data
  Proposal: Alternatively, Extend the SP service to support GMEC needs, i.e. 5GC receive GMEC specific parameters and store it in the 5GC for the 5GC to enforce, see S2-2301193/ S2-2301194 at SA2#154AH.

## Slide 13: Extending other NEF services consideration
TrafficInfluence
  Function: request routing (forwarding) to actual NF Service Producer to influence traffic routing decisions
  Target: GPSI, UE address, Group ID, any UE
  Limitation for GMEC API:
    1) No support of provisioning of flow description, traffic characteristics, QoS parameters to be enforced, QoS parameters to be monitored etc. as part of the subscription data
    2) No support of TSC QoS/involvement of TSCTSF

## Slide 14: Possibilities to Optimize GMEC procedures following common/separate API
Keep current procedures
Use only UDM+UDR
Use only TSCTSF
Use only NEF
Full feature set only when TSCTSF is deployed
Simplified GBR QoS and QoS monitoring when UDR is used
Duplicated functionality standardized/ implemented
Restrictions are not understandable for AF
Most simple, as procedures can be re-used
Simplified GBR QoS and QoS monitoring when UDR is used
Restrictions are not understandable for AF
Full feature set
Requires deployed TSCTSF
Full feature set
NEF resolves group members, subscribes for UE connectivity
Move group context handling from TSCTSF/UDR/PCF to NEF
Either extention to AFSessionwithQoS procedure or keep the current new NEF Service
Replace current procedure by extension to Parameter/Service Provisioning procedure providing parameters to UDM (on group membership) and UDR (on group configuration)
Remove the UDR related interactions
Either extention to AFSessionwithQoS procedure or keep the current new NEF Service
Changes
Pros/Cons
A NF for coordination of group context/state exists to address further:
Problems for GBR handling: how to behave in case of failure to get resources?
Problems for QoS monitoring (when reporting period is in the order of minutes): how to coordinate so that reports are generated at similar points in time and aggregation is possible (as well as meaningful interpretation at AF)

## Slide 15: Comparison Summary
 | Separate NEF Service |  | Common NEF service |  |  | 
 | AFRequestForQoS | MultiMemberAFsessionWithQoS | AFSessionWithQoS | ParameterProvision | ServiceParameter | TrafficInfluence
Target UE | Group ID or GPSI | list of UE IP addresses | UE address | UE address, GPSI, Group ID | UE address, GPSI, Group ID | UE address, GPSI, Group ID, any UE
Support Future PDU Session | Yes | No | No | Yes | Yes | Yes
Multiple memberships? | Yes (one per PDU Session) | Yes (multiple per PDU Session) | No | Yes | Yes | Yes
Area/scope | Regional area/factory | Whole PLMN | Whole PLMN | Regional area/factory/Whole PLMN | Regional area/factory/Whole PLMN | Regional area/factory
Procedure dependency | TSCTSF required | None | TSCTSF required, depends | Yes, depends | UDR required | UDR required
Group control | TSCTSF or PCF | NEF | None | UDM | UDR | UDR
QoS type | Both GBR and non-GBR | Individual GBR QoS | Both GBR and non-GBR | None | None | None
Flow description | Communication between UEs or between UE and DN, 3 tuples | Communication only between UE and DN, 5 tuples | Communication only between UE and DN, 5 tuples | None | None | Communication only between UE and DN, 5 tuples
Update frequency | rare | Frequent (wrt. current members, QoS, monitoring) | Frequent (wrt. QoS, monitoring) | rare | rare | Frequent (wrt. Traffic routing)
commonalities | Certain similarity in functionality and commonality of some parameters (i.e. for an individual UE‘s PDU Session QoS and QoS monitoring is controlled) |  |  |  |  | 
Specifics | Traffic characteristics, Temporal invalidity, Group Data Rate | Consolidated bitrate monitoring | XRM support, TSC parameters etc. | UE related parameters | Service specific parameters | Traffic routing parameters
Summary | Straightforward for different area application developers, simple and clear specification |  | Integrated NEF functionalities applicable to all different applications, NEF needs validation of the correctness for parameter combos for a given application and invoke different backend procedures accordingly, every developer has to learn all the parameters or procedures even none of their interest, complex specification mixed of different features and use cases and this becomes worse in future evolution of the API when even more scenario specific functionality and parameters have to be supported |  |  |