## Slide 1: Study on DetNet Phase 2
Ericsson

## Slide 2: Rel-18 DetNet solution
UE
(R)AN
UPF
SMF
AMF
PCF
TSCTSF
CPF: DetNet controller
DetNet network
5GS logical DetNet Router
DetNet system
NW-TT
UDM
For industrial/critical communications
Realized DetNet forwarding sub-layer: 5GS acting as a transit router.
TSCTSF maps requirements (max. latency and max. loss) and traffic specification to 3GPP parameters
DetNet service sub-layer not specified in rel-18 due to lack of IETF support for IP user plane

## Slide 3: DetNet service sub-layer for IP
Redundant paths with packet replication and elimination
  Failure of one path does not affect e2e traffic
Redundancy e2e or for a segment
3GPP support for redundant paths:
  Mutiple UEs (23.501 Annex F)
  Dual connectivity (23.501 clause 5.33.2.1)
  Redundancy handling for replication and elimination not part of 3GPP spec.
IETF solution for DetNet IP user plane service sub-layer now mature
  draft-ietf-detnet-mpls-over-ip-preof expected to become RFC in rel-19 timeframe
  Uses MPLS headers for encapsulation without requiring MPLS support.
DetNet controller
PREOF
PREOF
Host1
Host2
PREOF: Packet Replication, Elimination and Ordering Function (DetNet)

## Slide 4: 5GS IP service layer support for DetNet - Example 1
UE2
UE1
RAN1
UPF1
DetNet controller
RAN2
UPF2
PREOF
PREOF
5GS
Redundant 5GS path using 2 UEs
DetNet controller provided in operator domain
Operator self-contained solution for redundancy as a service

## Slide 5: 5GS IP service layer support for DetNet - Example 2
Redundant 5GS path using dual connectivity (single UE)
DetNet controller provided in operator domain
Operator self-contained solution for redundancy as a service
UE
RAN1
UPF1
DetNet controller
RAN2
UPF2
PREOF
PREOF
5GS

## Slide 6: 5GS IP service layer support for DetNet - Example 3
Redundant 5GS path using 2 UEs
External DetNet controller
Redundancy can be extended e2e, PREOF possible outside of 5GS
UE2
UE1
RAN1
UPF1
DetNet controller
RAN2
UPF2
PREOF
PREOF
5GS

## Slide 7: DetNet_Ph2: Summary
Rel-18 DetNet limited to forwarding sub-layer
Rel-19 DetNet possible to extend to IP service sub-layer to provide redundancy
Flexible framework proposed to integrate with industrial/critical applications:
  DetNet controller may be outside of 5GS, or integrated into 5GS for operator self-contained solution
  PREOF functionality may reside within 5GS, or outside
  3GPP redundant paths possible with multiple UEs or using dual connectivity
Adds operator value to integrate 5GS to industrial deployments and provide 5GS redundancy as a service.