## Slide 1: Study on delegation of (re)selection of target NF across PLMNs
Magnus Olsson
Ericsson

## Slide 2: Outline
NF1
NF2
NFc3
SCPx
vSEPP
SCPy
NFp1
NFp2
NFp3
hSEPP
vPLMN
hPLMN
{ [sbi-target-apiroot] AND/OR
[sbi-discovery-nf-set]} OR
(sbi-discovery-*)
sbi-target-apiroot
3GPP has defined indirect communication via the SCP, allowing for different levels of delegation from the NF (acting as client) to the SCP, of the selection and reselection of the target destination logic.
However, indirect communication via the SCP is not defined across PLMNs, since the NF target is selected in the vPLMN

## Slide 3: Content
Delegation of (re)selection logic from NF to SCP provides some advantages as follows:
  It allows selection is performed closer to the target destination, what provides in some cases a more up to date information about target health and status.
  It allows reselection is performed closer to the target destination, what minimizes signaling path for the retry.
These advantages now are restricted for intra-PLMN interactions, not possible across PLMNs

## Slide 4: Summary
This SID proposes the following objectives
  Identify the implications of having different combinations of communication models between client PLMN and destination PLMN.
  Identify the element(s) in the destination PLMN that is responsible to perform the delegated logic and describe the required capabilities.
  Propose required procedure and interfaces update.