## Slide 1: ID Mapping: From IDs used in AF request to IDs used in V-SMF subscription
EDGE_Ph2
KI#1/HR
Source: Huawei, HiSilicon

## Slide 2: Background
As agreed in last meeting (S2-2306205, S2-2306206), for AF influence procedure in HR-SBO:
  AF can provide AF request using UE IP/GPSI/External Group ID as key.
  V-SMF can subscribe for AF request using SUPI/Internal Group ID as Key.
The problem is how the V-NEF can map the “IDs provided by AF” to “IDs used by V-SMF for subscription”, considering the V-NEF has no knowledge about the mapping between these IDs since it does not belongs to HPLMN. Issues include how the V-NEF can:
  Map UE IP to SUPI
  Map GPSI to SUPI
  Map External Group ID to Internal Group ID.
  Note: The mapping from GPSI/External Group ID to SUPI/ Internal Group ID also applies for EDI provisioning and ECAI provisioning procedures in VPLMN.
Our considerations for addressing the issue:
  Minimize the changes to the H/VPLMN by trying to reuse existing services.
  V-NEF can act as a 3rd AF to invoke H-NEF services for such ID mapping.

## Slide 3: Proposed solutions for UE IP to SUPI mapping
The V-NEF retrieves SUPI corresponding to the UE IP from BSF in HPLMN via H-NEF. (extending the Nnef_UEId_Get service to support mapping IP->SUPI)
  Further, if the UE IP provided by AF is a NATed IP, the V-NEF first retrieves the private UE IP and IP domain from the UPF which provides the NAT function (reusing the Nupf_GetPrivateUEIP_Get service), and differentiates the scenarios between non-roaming and HR-SBO.
H-NEF
AF
(V-)NEF
BSF
2. UE IP
3. UE ID
(SUPI)
1. UE IP
See CR4110(23.502) and CR0142(23.548) corresponding to this solution.
Public IP
NATed IP
V-NRF
AF
(V-)NEF
UPF
3. Get private UE IP and IP domain
1. NATed UE IP
H-NEF
BSF
4. Private UE IP
5. UE ID
(SUPI)
2. Get UPF address

## Slide 4: Proposed solutions for mapping GPSI/External Group ID to SUPI/ Internal Group ID
The V-NEF retrieves SUPI/Internal Group ID corresponding to the GPSI/External Group ID from UDM in HPLMN via H-NEF.(extending the Nnef_UEId_Get service to support inputs/outputs of these IDs)
The V-SMF retrieves the Internal Group ID(s) during PDU session establishment/modification, then use it as Data Key for subscription if needed.(extending the Nsmf_PDUSession_Create service operation)
See CR4110(23.502), CR0122(23.548) and CR0123(23.548) corresponding to this solution.
H-SMF
V-NEF
V-SMF
UDM
1. Internal Group Identifier(s)
2. Subscribe for AF request
AF
H-NEF
AF
(V-)NEF
UDM
2. External Identifiers
3. Internal Identifiers
1. External Identifiers
Mapping GPSI/External Group ID to SUPI/Internal Group ID
V-SMF retrieves Internal Group ID

## Slide 5: Thanks!