## Slide 1: New SID on 5G Architecture Enhancement for Ambient IOT Service
Huawei, HiSilicon

## Slide 2: Motivations
Ambient IoT: a New IoT Technology for Connections of Everything
Typical use case for Ambient IOT
Design target for Ambient IOT
Category 1: Pre-stored data report
Information (e.g., identity) is stored in a small size, ultra-low cost, and battery-less Ambient IoT device, mainly for production material, asset and goods inventory and tracking
Typical use cases include supply chain management in manufacturing, warehouse logistics, asset management in healthcare, etc.
Category 2: Sensing data report
Information (e.g., temperature) is generated and transmitted by wireless sensor without battery replacement during long lifetime
Typical use cases include wireless sensor for environment, equipment, and living things monitoring in industries such as electric power, chemical, livestock farming, manufacturing, etc.
Ambient IoT can reduce device cost and power consumption, by 10-100 times than existing mMTC technologies in Rel-19
Parcel volume is forecasted to reach 163.4 billion by 2025 in china and 220-262 billion by 2026 globally
Automatic inventory and tracking of parcels requires ultra-low cost and battery-less Ambient IoT devices

## Slide 3: Rel-19 ongoing progress
SA1 study on Ambient IOT will complete by June 2023, RAN work is ongoing
SA1:TR 22.840 completes 80% by 23Q1
SA1 overall progress
  30 use cases in the TR
  Ambient IoT communication patterns:
    Normal operation
    Device triggered operation
    On demand operation
Next step (May meeting): finalize the requirements
  Communication aspects
  Positioning
  Management of Ambient IoT devices
  Collected information and network capability exposure
  Charging
  Security and privacy
RAN plenary: TR 38.848 completes 50% by 23Q1
Consider three categories of Ambient IoT devices
  Device A: No energy storage, no independent signal generation/amplification, i.e. backscattering transmission.
  Device B: Has energy storage, no independent signal generation, i.e. backscattering transmission. Use of stored energy can include amplification for reflected signals.
  Device C: Has energy storage, has independent signal generation, i.e., active RF components for transmission.
  Consider four connectivity topologies
    Topology 1: BS ↔ Ambient IoT device
    Topology 2: BS ↔ intermediate node ↔ Ambient IoT device
    Topology 3: BS ↔ assisting node ↔ Ambient IoT device ↔ BS
    Topology 4: UE ↔ Ambient IoT device
Ambient IoT requirements are stable so that SA2 rel-19 study work can start soon
Topology 1 Diagram
Ambient IoT device directly and bidirectionally communicates with a base station.

## Slide 4: Potential architecture impacts
5G core needs to be enhanced to support Ambient IoT service
SA2 rel-19 needs to consider the following aspects
Ambient IoT device identification
Registration and Connection Management for Ambient IoT devices
Ambient IoT services and data transmission
Operator charging support
Ambient IOT Device
5G core
NG-RAN
AF (enterprise)
NG-RAN support：
Random access
Data transmission, etc
A-IoT essential functions：
Service operation(e.g. inventory)
Data transmission
Connection management
AF (enterprise IoT platform)
Initiate operation command，including operation type and area
Receiving device ID and data reporting
A-IoT management：
Security
Charging
End to End architecture to support Ambient IoT service, under RAN Topology 1: BS ↔Ambient IoT device
Architecture enhancement in rel-19 should focus on essential features