## Slide 1: Discussion on Network Slice Replacement in roaming
Huawei, HiSilicon
S2-2307100

## Slide 2: Network Slice Replacement for roaming
According to the following descriptions in clause 5.15.19 of TS 23.501, in roaming scenario the S-NSSAI to be replaced can be VPLMN S-NSSAI or HPLMN S-NSSAI.
For roaming, the S-NSSAI attributes of PDU session include VPLMN S-NSSAI and HPLMN S-NSSAI(which are provided to UE in the N1 SM container).
The HPLMN S-NSSAI is used to match the application (that is triggering the PDU Session Request) within the NSSP in the URSP rules. Therefore, it is necessary to update UE with the HPLMN Alternative S-NSSAI if the HPLMN S-NSSAI has to be replaced.
for roaming UEs when the VPLMN S-NSSAI has to be replaced by a VPLMN Alternative S-NSSAI, the AMF provides the mapping of the VPLMN S-NSSAI to the Alternative VPLMN S-NSSAI to the UE. for roaming UEs when the HPLMN S-NSSAI has to be replaced by an Alternative HPLMN S-NSSAI, the AMF provides the mapping of the HPLMN S-NSSAI to the Alternative HPLMN S-NSSAI to the UE.

## Slide 3: Network Slice Replacement for roaming
Slice Replacement for new PDU session
  Case#1: S-NSSAI to be replaced is VPLMN S-NSSAI
  Case#2: S-NSSAI to be replaced is HPLMN S-NSSAI
  Case#3: S-NSSAIs to be replaced are HPLMN S-NSSAI and VPLMN S-NSSAI
Slice Replacement for existing PDU session
  Case#1: S-NSSAI to be replaced is VPLMN S-NSSAI
  Case#2: S-NSSAI to be replaced is HPLMN S-NSSAI
  Case#3: S-NSSAIs to be replaced are HPLMN S-NSSAI and VPLMN S-NSSAI

## Slide 4: Slice Replacement for new PDU session
UE
AMF
V-UPF
RAN
1. UE to AMF:
VPLMN S-NSSAI, VPLMN Alternative S-NSSAI
HPLMN S-NSSAI,
H-SMF
H-UPF
2, AMF to V-SMF:
VPLMN S-NSSAI, VPLMN Alternative S-NSSAI,
HPLMN S-NSSAI
3. (in case of HR roaming)V-SMF to H-SMF:
HPLMN S-NSSAI,
V-SMF
4. N2 SM: VPLMN Alternative S-NSSAI
If the UE is provided with the mapping of the VPLMN S-NSSAI to VPLMN Alternative S-NSSAI then UE provides in the PDU Session Establishment message:
VPLMN S-NSSAI, VPLMN Alternative S-NSSAI,
HPLMN S-NSSAI,
5. N1 SM: VPLMN Alternative S-NSSAI, HPLMN S-NSSAI
Case#1: S-NSSAI to be replaced is VPLMN S-NSSAI
V-PLMN
H-PLMN
Observation 1:
Regardless of LBO or HR, the VPLMN proceeds with the PDU Session establishment using the VPLMN Alternative S-NSSAI.
This is similar to the slice replacement for non-roaming scenario.

## Slide 5: Slice Replacement for new PDU session
UE
AMF
V-UPF
RAN
1. UE to AMF:
VPLMN S-NSSAI,
HPLMN S-NSSAI, HPLMN Alternative S-NSSAI
H-SMF
H-UPF
2, AMF to V-SMF:
VPLMN S-NSSAI,
HPLMN S-NSSAI, HPLMN Alternative S-NSSAI
3. (in case of HR roaming)V-SMF to H-SMF:
HPLMN S-NSSAI,
HPLMN Alternative S-NSSAI
V-SMF
4. N2 SM: VPLMN S-NSSAI
5. N1 SM: VPLMN S-NSSAI, HPLMN Alternative S-NSSAI
If the UE is provided with the mapping of the HPLMN S-NSSAI to HPLMN Alternative S-NSSAI then UE provides in the PDU Session Establishment message:
VPLMN S-NSSAI,
HPLMN S-NSSAI, HPLMN Alternative S-NSSAI,
V-PLMN
H-PLMN
Case#2: S-NSSAI to be replaced is HPLMN S-NSSAI
Observation 2:
In case of LBO, the V-SMF proceeds with the PDU Session establishment using the VPLMN S-NSSAI. No impacts on the SMF selection. The V-SMF needs to provide UE with HPLMN Alternative S-NSSAI. No impacts on RAN and V-UPF.
In case of HR, the H-SMF proceeds with the PDU Session establishment using the HPLMN Alternative S-NSSAI. The V-SMF needs to provide UE and H-UPF with HPLMN Alternative S-NSSAI. No impacts on RAN.

## Slide 6: Slice Replacement for new PDU session
UE
AMF
V-UPF
RAN
1. UE to AMF:
VPLMN S-NSSAI, VPLMN Alternative S-NSSAI
HPLMN S-NSSAI, HPLMN Alternative S-NSSAI
V-SMF
H-UPF
2, AMF to V-SMF:
VPLMN S-NSSAI, VPLMN Alternative S-NSSAI
HPLMN S-NSSAI, HPLMN Alternative S-NSSAI
3. (in case of HR roaming)V-SMF to H-SMF:
HPLMN S-NSSAI,
HPLMN Alternative S-NSSAI
V-SMF
4. N2 SM: VPLMN Alternative S-NSSAI
If the UE is provided with the mapping of the VPLMN S-NSSAI to VPLMN Alternative S-NSSAI, and mapping of the HPLMN S-NSSAI to HPLMN Alternative S-NSSAI then UE provides in the PDU Session Establishment message:
VPLMN S-NSSAI, VPLMN Alternative S-NSSAI,
HPLMN S-NSSAI, HPLMN Alternative S-NSSAI,
5. N1 SM: VPLMN Alternative S-NSSAI, HPLMN Alternative S-NSSAI
V-PLMN
H-PLMN
Case#3: S-NSSAIs to be replaced are HPLMN S-NSSAI and VPLMN S-NSSAI
Observation 3:
In case of LBO, the V-SMF proceeds with the PDU Session establishment using the VPLMN Alternative S-NSSAI. The V-SMF needs to provide UE/RAN/V-UPF with VPLMN Alternative S-NSSAI. In addition, The V-SMF needs to provide UE with HPLMN Alternative S-NSSAI.
In case of HR, the V-SMF proceeds with the PDU Session establishment using the VPLMN Alternative S-NSSAI and the H-SMF proceeds with the PDU Session establishment using the HPLMN Alternative S-NSSAI. The V-SMF needs to provide UE with VPLMN Alternative S-NSSAI and HPLMN Alternative S-NSSAI.

## Slide 7: Slice Replacement for existing PDU session_LBO roaming
For Local Breakout roaming, the S-NSSAI to be replaced is:
  Case#1: VPLMN S-NSSAI only.
    The V-AMF notifies the V-SMF that the PDU Session is to be transferred to Alternative S-NSSAI(VPLMN S-NSSAI).
    The V-SMF determines whether the PDU session can be retained or not.
      If yes, the V-UPF/RAN/UE are impacted to receive the Alternative S-NSSAI.
      If not, the V-SMF trigger PDU session re-establishment.
  Case#2: HPLMN S-NSSAI only.
    The V-AMF notifies the V-SMF that the PDU Session is to be transferred to Alternative S-NSSAI(HPLMN S-NSSAI).
    Since the VPLMN S-NSSAI is not impacted, the PDU session can be retained. The UE is provided with Alternative S-NSSAI(HPLMN S-NSSAI) by the V-SMF via PDU Session Modification Command message so that the UE can further evaluate the URSP based on the new S-NSSAI attributes of PDU session.
    No impacts on RAN and V-UPF.
  Case#3: both VPLMN S-NSSAI and HPLMN S-NSSAI.
    The combination of case#1 and case#2.
V-AMF
UE
URSP
(H-S-NSSAI)
V-UPF
V-SMF
RAN
Case#1: it is similar with Non-roaming.
Case2: It is necessary to notify the V-SMF since N1 SM container is provided by the V-SMF to the UE.

## Slide 8: Slice Replacement for existing PDU session_HR roaming
For Home-routed roaming, the S-NSSAI to be replaced is:
  Case#1: VPLMN S-NSSAI only.
    The V-AMF notifies the V-SMF that the PDU Session is to be transferred to Alternative S-NSSAI(VPLMN S-NSSAI).
    The V-SMF determines whether the PDU session can be retained or not.
      If yes, the V-UPF/RAN/UE are impacted to receive the Alternative S-NSSAI.
      If not, the V-SMF trigger PDU session re-establishment.
  Case#2: HPLMN S-NSSAI only.
    The V-AMF notifies the H-SMF that the PDU Session is to be transferred to Alternative S-NSSAI(HPLMN S-NSSAI).
    The H-SMF determines whether the PDU session can be retained or not.
      If yes, the H-UPF/UE are impacted to receive the Alternative S-NSSAI. No RAN impacts.
      If not, the H-SMF trigger PDU session re-establishment.
  Case#3: both VPLMN S-NSSAI and HPLMN S-NSSAI.
    The combination of case#1 and case#2.
V-AMF
H-SMF
V-PLMN
H-PLMN
UE
V-SMF
V-UPF
H-UPF
RAN
URSP
(H-S-NSSAI)
Case#1: it is similar with Non-roaming.

## Slide 9: Conclusions of Slice Replacement for new PDU session
  Case#1: S-NSSAI to be replaced is VPLMN S-NSSAI
    For LBO and HR, the VPLMN proceeds with the PDU Session establishment using the VPLMN Alternative S-NSSAI.
    This is similar to the slice replacement for non-roaming scenario.
  Case#2: S-NSSAI to be replaced is HPLMN S-NSSAI
    LBO: No impacts on the SMF selection, RAN and V-UPF. The V-SMF needs to provide UE with HPLMN Alternative S-NSSAI.
    HR: the H-SMF proceeds with the PDU Session establishment using the HPLMN Alternative S-NSSAI. The V-SMF needs to provide UE and H-UPF with HPLMN Alternative S-NSSAI. No impacts on RAN.
  Case#3: S-NSSAIs to be replaced are HPLMN S-NSSAI and VPLMN S-NSSAI
    LBO: the V-SMF proceeds with the PDU Session establishment using the VPLMN Alternative S-NSSAI. The V-SMF needs to provide UE/RAN/V-UPF with VPLMN Alternative S-NSSAI. In addition, The V-SMF needs to provide UE with HPLMN Alternative S-NSSAI.
    HR: the V-SMF proceeds with the PDU Session establishment using the VPLMN Alternative S-NSSAI and the H-SMF proceeds with the PDU Session establishment using the HPLMN Alternative S-NSSAI. The V-SMF needs to provide UE with VPLMN Alternative S-NSSAI and HPLMN Alternative S-NSSAI.

## Slide 10: Conclusions of Slice Replacement for existing PDU session
  Case#1: S-NSSAI to be replaced is VPLMN S-NSSAI
    LBO: it is similar with Non-roaming.
    HR: it is similar with Non-roaming.
  Case#2: S-NSSAI to be replaced is HPLMN S-NSSAI
    LBO: No impacts on RAN and V-UPF. The V-AMF notifies the V-SMF that the PDU Session is to be transferred to HPLMN Alternative S-NSSAI.
    HR: The V-AMF notifies the H-SMF that the PDU Session is to be transferred to HPLMN Alternative S-NSSAI. The H-SMF determines whether the PDU session can be retained or not.
  Case#3: S-NSSAIs to be replaced are HPLMN S-NSSAI and VPLMN S-NSSAI
    LBO: The combination of case#1 and case#2.
    HR: The combination of case#1 and case#2.

## Slide 11: Proposals
It is proposed to update clause 5.15.19 of TS 23.501 by adding some descriptions of Network Slice Replacement in roaming including the following cases:
  VPLMN S-NSSAI has to be replaced by a VPLMN Alternative S-NSSAI
  HPLMN S-NSSAI has to be replaced by an Alternative HPLMN S-NSSAI
  Both VPLMN S-NSSAI and HPLMN S-NSSAI have to be replaced
It is proposed to update PDU Session establishment procedure in TS 23.502 to describe Network Slice Replacement in roaming.

## Slide 12
Thank you