## Slide 1: Timing as a service and timing resiliency enhancements for EPS
Qualcomm Incorporated
S2-2307214

## Slide 2: Background
Timing as a service refers to providing timing information to UEs​ as a monetizable operator service
  Rel-18 enabled
    subscription control for timing delivery to individual UEs​
    providing quality information about the 5GS clock to UEs
  Clock quality information enables UEs to
    determine if the 5G clock quality is sufficient,
    compare the 5G clock quality against other available time sources
    select the best available clock source​
Timing as a service enhances timing resiliency as it enables use of 5GS as another reliable time source.

## Slide 3: Motivation
Timing as a service is only supported for NR
NR coverage is still quite limited and may not be available in many areas for quite some time and cost of the UE can be problematic for certain use cases
Other RATs (terrestrial and non-terrestrial NB-IoT and eMTC) do not support timing as a service
  NB-IoT/eMTC do not support providing time selectively to UEs based on subscription information and
  NB-IoT/eMTC do not support providing clock quality information to UEs.​
  Note: For NB-IoT/eMTC over NTN, timing as a service is useful if GNSS is not supported or temporarily not available.​

## Slide 4: Proposal
Enable timing as a service for NB-IoT/eMTC (terrestrial and NTN) connected to EPC to maximize monetization potential for operators
  Enable selective reference time delivery for NB-IoT/eMTC based on subscription information
  Enable delivery of clock quality information to UEs for NB-IoT/eMTC (terrestrial and over NTN)​
  Support propagation delay compensation (specifically relevant for NB-IoT/eMTC over NTN for UEs without GNSS)

## Slide 5: Objectives
Study how to enable selective reference time and clock quality information delivery based on subscription for NB-IoT and eMTC (terrestrial and non-terrestrial)
  Subscription enhancements in HSS for control of reference time delivery and control of clock quality delivery to the UE
  MME enhancements to inform eNBs about need for reference time delivery and clock quality information delivery for individual UEs
  eNB support for delivery of reference time and clock quality information for individual UEs
Study how to support propagation delay compensation for NB-IoT and eMTC
NOTE: Cooperation with RAN2 and RAN3 is assumed for these objectives.