## Slide 1: Handling of the Allowed PDU session status IE in Non-allowed service area Source: Qualcomm
3GPP TSG SA WG2 Meeting #157
22 – 26 May, 2023, Berlin, DE
S2-2307221

## Slide 2: LS from CT1 (C1-227197)
CT1 would like to ask SA2 for guidance on an issue. The scenario is as follows:
The UE is registered to an AMF both via 3GPP and non-3GPP access. The UE is currently in a non-allowed area. The registration area (TAI list) for 3GPP access includes both TAs from the UE's non-allowed area and TAs from the allowed area. The UE is currently in a non-allowed area.
The UE has at least 1 PDU session activated via non-3GPP access which cannot be transferred to 3GPP access.
The UE is in IDLE mode both for 3GPP and non-3GPP access, when it receives a paging via 3GPP access indicating non-3GPP access and responds with a Service Request.
CT1 understands that if the UE responds to the paging when it is in a TA belonging to the allowed area, then the UE needs to include the Allowed PDU session status IE (in 23.502 terminology: "List Of Allowed PDU Sessions") indicating which of the PDU sessions associated with non-3GPP access can be transferred to 3GPP access and may include the Uplink data status IE if it has uplink data pending.
Question 1: Does the UE need to include the Allowed PDU session status IE also if it responds to the paging when it is in a non-allowed area?
Question 2: Is the UE allowed to include the Uplink data status IE if it has uplink data pending if it responds to the paging when it is in a non-allowed area?

## Slide 3: Issue #1: Does the UE include all PDU sessions in “List of Allowed PDU sessions” IE or none?
Q1) The UE as part of Allowed PDU session status IE (CT1 terminology) / List Of Allowed PDU Sessions (SA2 terminology) will indicate which PDU session(s) for the scenario described in CT1 LS:
  Opt1: The UE shall include empty PDU session list (*)
  Opt2: The UE is allowed to include any PDU session based on its policy ignoring service area restrictions. Same behaviour is applied for List Of PDU Sessions To Be Activated in the specific scenario described in CT1 LS .
SA2#156E Way forward: Option 1.
(*) there is disagreement on the exceptions for regulatory prioritised services (MPS/MCS) and emergency– see next slide

## Slide 4: Issue #2: What are the exceptions for PDU sessions that can be included in “List of Allowed PDU session” IE
Our view
  Rel.17: none.
    MPS/MCS over WLAN is not supported so UE will not know it is in MPS/MCS session and there are no MT emergency calls.
  Rel.18: MPS PDU session
    For MPS (UE can know based on MPS subscription indicated to N3IWF or TNGF with IKE_AUTH response)  this is proposed in S2-2307188
    Still no support for MCS over WLAN and no MT emergency calls

## Slide 5: Issue #2: What are the exceptions for PDU sessions that can be included in “List of Allowed PDU session” IE
S2-2305057: emergency call scenario
  UE establishes emergency PDU session over non-3GPP access. UE is NOT emergency registered
  UE loses non-3GPP coverage but cannot also find 3GPP coverage temporarily
  AMF moves the UE to CM-IDLE
  MT data for the emergency PDU session are sent/buffered in CN
  UE regains 3GPP coverage BUT does not transfer the emergency PDU session
  AMF pages the UE indicating non-3GPP access
Current TS 23.501 states:
  Emergency Services shall not be provided to a UE over 3GPP access and non-3GPP access concurrently, except for the following case:
    a UE may be Emergency Registered and have an emergency PDU session over non-3GPP access or may be attached for emergency session to ePDG over untrusted WLAN (as defined in TS 23.402 [43]) when 3GPP access becomes available. In which case the UE may have to register over 3GPP access and check first the support for Emergency Services over the 3GPP RAT it has selected (e.g. based on Emergency Services Support indication, Emergency Services Fallback, AS broadcast indicator). If there is native support for Emergency Services in the selected 3GPP RAT the UE will attempt to transfer the emergency PDU session from non-3GPP access to 3GPP access (see clause 4.9.2 or clause 4.9.3 of TS 23.502 [3]). If there is no native support for Emergency Services in the selected RAT, but Emergency Services Fallback to another RAT in 5GS or to another System where Emergency Services may be supported (based on the conditions defined in clause 5.16.4.11), the UE may trigger first Emergency Services Fallback (see clause 4.13.4.2 of TS 23.502 [3]) and then attempt to transfer the emergency PDU session from non-3GPP access to 3GPP access (see clause 4.9.2 of TS 23.502 [3]). In these cases the UE may thus briefly be emergency registered and receive emergency services over both 3GPP access and non-3GPP access concurrently.
  A UE may only attempt to use Emergency Services over non-3GPP access if it is unable to use Emergency Services over 3GPP access as specified in TS 23.167 [18].
But Samsung argument in SA2#156E was that the text only applies to Emergency Registered UE and a normally registered UE implementation is not mandated to transfer the PDU session when it regain 3GPP access
Our view is that there is clear indication in TS 23.501 and TS 23.167 that a) there is no MT emergency call, b) the UE only performs emergency call over non-3GPP access when 3GPP access is not available
Proposal: Clarify the text in TS 23.501 that UE needs to transfer the emergency PDU session if it is normally registered or emergency registered  this is proposed in S2-2307155

## Slide 6: Summary of QC papers in SA2#157
S2-2307188 (TS 23.502 CR): clarifies how the UE gets to know that N3IWF support MPS and therefore PDU session is for MPS
S2-2307155 (TS 23.501 CR): clarifies emergency session transfer from non-3GPP to 3GPP access
S2-2307153 (TS 23.502 CR): Non-Allowed areas clarifications related to MPS
S2-2307181: LS response to CT1