## Slide 1: XRM Rel-19 Topics
CableLabs

## Slide 2: Limitations with XRM R18
The study focused on using NR as access technology, specific enhancements to other access types were not studied
Rel-18 assumed XRM traffic over single-access PDU session only
As part of conclusions for KI#4 and KI#5, it was assumed that the RTP/SRTP header and/or payload necessary for the identification of PDU Set Information is not encrypted. However, if QUIC is used as transport, upper-layer headers & payload will get encrypted. Other media transport methods also not considered.

## Slide 3: Potential Key Issue #1: Other Access Types
XRM support via non-3GPP accesses (trusted, untrusted, wireline)
  Support current congestion level information exposure from non-3GPP access
    ECN marking for the purpose of L4S over non-3GPP access
    API-based exposure of congestion level information of non-3GPP access towards AF
    Support of PDU Set based QoS handling over non-3GPP access?
SA1 Rel-19 metaverse requirements
  Support means to expose additional network performance information (e.g., bitrate, latency) per UE for non-3GPP access to an authorized 3rd party application [SA1 TR 22.856 - Use case 5.25]

## Slide 4: Potential Key Issue #2: Multi-Access
Support synchronization of XRM traffic routed or steered over 3GPP and non-3GPP access networks [SA1 TR 22.856 - Use case 5.25]
  Support MA-PDU for a single XRM session
    Steer/switch from one access to other based on access performance
  Impact of multi-path protocols (MPTCP/MPQUIC) over end-to-end congestion control (L4S)

## Slide 5: Potential Key Issue #3: Various transport and media layers
 | PDU Set handling | L4S
RTP over UDP | Rel-18 | Rel-18
SRTP | Rel-18 | Rel-18
RTP over QUIC | Rel-19* | Rel-19*
QUIC (e.g. ,QUIC Prague) | N/A | Rel-18
TCP (e.g., TCP Prague) | N/A | Rel-18
MP-TCP | N/A | Rel-19*
MP-QUIC/MASQUE | Rel-19* | Rel-19*
HTTP/3 | Rel-19 | 
* - Associated IETF work not yet complete
Support of additional transport and media protocols for PDU Set handling and L4S

## Slide 6: Thank you!