## Slide 1: Mobile Virtual Private Network
Huawei, HiSilicon

## Slide 2
Mobile office and home office are becoming more and more popular, allowing the flexibility of the users to work remotely, including from a customer premise or other off-site location, and secure and reliable connection between the employees’ office equipment including UE or non-5GC capable device should be established no matter where the user is. It needs to study the system impact to support 5GC capable UE accessing office network by using cellular access anywhere, and non-5GC capable devices accessing via relay UE with different user identities.
In addition, employees’ office equipment may include the 5GC capable UE or non-5GC capable devices. When the user is in some place with only cellular coverage, his non-5GC capable device may access his working equipment via the 5GC capable UE which provides WLAN AP function for his non-5GC capable devices. What's more complicated but possible, more than one non 5GC capable devices belonging to the different employees may connect via the same relay UE. The enterprise wants to identify and manage these equipment (e.g. laptop) to allow only authorized equipment to access to his own office network and block access from non-company equipment (e.g., a visitor’s laptop). The enhancement of the 5G system is needed to allow for the creation and utilization of user-specific identities for the non-5GC capable device to offer services, independent of the subscription that is used by the relay UE to establish the connection.
Outline

## Slide 3
Case 2
Mobile office
Home office
Enterprise campus
UP
CP
5G Core
Use Case for mobile private network:
Case 1: Identify the User id for non-SIM device
Case 2: Remote UE accessing private network in everywhere
Remote UE
Employee
5G
CPE
Meeting room
Office building
Case 1
Mobile Virtual Private Network

## Slide 4
192.168.1.4
Employee User 1
Employee User 1
Employee User 2
NR
Wifi AP
UPF
DN-AAA
AMF
UDM
SMF
PCF
Campus A
N1
N2
N4
AUSF
In this case, there are the following requirements:
1) The employee’s different devices could access the office network via the relay UE or 5G CPE, no matter he is inside or outside the campus, with the same service experience. The office network needs to identify the device’s User ID.
2) As the device may belong to the different User, the different service or QoS control is necessary, and the relay UE should be authorized by the office network firstly.
3) Keep the service connectivity when the employee’s device is moving from one relay UE to another AP.
NR
Employee User 1
SIM
UPF
N4
N3
N2
Guest User
Employee User 2
NR
N3
N3
X
Wifi AP
Switch
AC
Employee User 2
staff office
①
②
③
In order to achieve the above requirements, it needs to study:
How the 5GC can authenticate/authorize the user identities of the device behind the UE. What information is needed to identify the device, whether this information are linked with the 3GPP subscriptions.
How to identify the device accessing 5GC through a relay UE. Whether and how to establish the relationship between the device and the relay UE. How the network limits the number of the devices connecting to the relay UE.
How the 5GC establishes separate PDU sessions for the different devices belonging to the different users. How the network control the traffic from the different devices/users, e.g. by using the different QoS or charging policy.
How to support the service connectivity for the device when it is moving from one relay UE to other access point or vice verse, e.g. from a relay UE to a WLAN AP.
①
②
Case 1:User id for non-SIM device

## Slide 5
In order to achieve the above requirement, it needs to study:
Whether and how to extend the 5G VN or PIN to support the per subscriber level group for personal network.
How to route the traffic between the remote UE and the devices belonging to the same personal network crossing different UPFs.
How to discover the devices behind the relay UE if there is NAT existing in the network.
UPF
AMF
UDM
SMF
Employee User 1
NR
PCF
NR
5G CPE/UE
User2 VPN
User1 VPN
User 1
staff office
UPF
SMF
AMF
N4
NR
N3
N3
N2
N4
N2
N3
In this case, there are the following requirement:
1) For the remote UE, i.e. the employee’ UE outside the office, it can communicate with the office equipment located in his private network no matter where the user is, in order to support mobile office or home office.
User 2
?
①
①
Employee User 1
User3 VPN
AUSF
Case 2: Remote UE accessing

## Slide 6
Summary
It is proposed to study how the 5G System can be enhanced to support the 5G mobile VPN in the 3GPP network.
How 5GC identifies the user identifier of the device accessing the 5GC via the relay UE which has the 3GPP subscriptions.
  How the 5GC can authenticate/authorize the user identities of the device behind the UE, what information is needed to identify the device, and whether this information is linked with the 3GPP subscriptions.
  How to control the relay UE, e.g. whether the NAT is allowed in the relay UE, and which devices and how many devices are allowed to access via this relay UE.
  Whether and how the 5GC establishes separate PDU sessions for the different devices, e.g. belonging to the different users. How to allocate the IP addresses for the devices, and how to control the traffic from the different devices, e.g. by using the different QoS or charging policy.
  How to establish the connection between the different devices via the different relay UE. Whether and how to support the device service to be isolated, controlled by the relay UE or 5GC.
Study how the remote UE, i.e. the UE outside the campus, can communicate with the devices behind the relay UE located in the campus via 5GC.
  Whether and how to extend the 5G VN or PIN to support the per subscriber level group for personal office network.
  How to route the traffic between the remote UE and the devices belonging to the same personal office network crossing different UPFs.
  How to discover the devices behind the relay UE if there is NAT existing in the network.