## Slide 1: Motivation on study to support ProSe direct/indirect communication for TSC communications and private networks
Lenovo, Siemens

## Slide 2: Introduction
Stage 1 requirements for Direct and Indirect communication for industrial automation are described in 3GPP TS 22.104 and accommodate for the following features
  Network performance requirements for periodic deterministic communication (both unicast and multicast) related to KPIs for corporate carrying use cases
  Requirements for clock synchronisation (working clock domain)
For Industrial IoT use cases, the following Stage 1 requirements described in 3GPP TS 22.104 clause 7 for supporting direct device communication are of importance in stage 2.
  Support direct device connection between a group of UEs for periodic deterministic communication (both unicast and multicast) with respective service performance requirements in Table 5.2-1 related to cooperative carrying
  Support clock synchronization (working clock domain) between the UEs within the group of UEs using ProSe direct device communication.
  NOTE: Similar requirements are also specified for ProSe indirect communication (clause 8, 3GPP TS 22.104).
  The use cases of multi-robots cooperation in factory automation, as depicted in TS 22.261 Annex D2, require the isochronous operation between robots using the direct device connection

## Slide 3: Study proposal
Propose to agree on a study to support ProSe Direct and Indirect Communication to support the Industrial IoT use cases and requirements described in 3GPP TS 22.104 and TS 22.261
Main focus of the study:
  Identify enhancements needed to support of ProSe Direct/Indirect Communication in private networks (SNPN and PNI-NPN) (including discovery, configuration of ProSe UEs to support ProSe in private networks)
    LS from 5G-ACIA (SP-221302) indicated that in most cases ProSe needs to be supported within private networks
  Identify enhancements needed in scenarios where 5GS is deployed as a layer-2 ethernet bridge when integrated with IEEE TSN network in order to support the stage 1 requirements:
    Clock synchronization of a common working clock between a group of UEs using ProSe Direct/Indirect Communication
    TSC communication via ProSe Direct/Indirect Communication

## Slide 4: Objectives – Work Tasks
  The following work tasks are identified for this study:
  WT 1: Identify enhancements needed to support ProSe Direct/Indirect communication in private networks (SNPN and PNI-NPN).
    For PNI-NPN network identify enhancement to support ProSe direct and indirect communication in conjunction with closed access groups.
  WT 2: Identify whether and how enhancements are needed (incl. e.g. configuration of UEs, PC5 QoS enhancements) to meet Industrial IOT requirements in 3GPP TS 22.104 by supporting periodic deterministic TSC communication via a ProSe Direct/Indirect Communication.
    Support of 5G-LAN/Ethernet/5G-VN in order to integrate the 5G ProSe communication with the IEEE 802.1-based subnetworks for use cases including mobile AGVs/mobile robots.
    Support of time synchronization protocols and profiles defined by IEEE 802.1AS for TSC communication via ProSe Direct/Indirect communication.
    Enhancements for the support of ProSe resource allocation and scheduling to ensure efficiency and continuity of industrial periodic deterministic communication.
    Support for URLLC requirements of low latencies and high reliabilities.
  WT 3: Identify whether and how enhancements are needed (incl. e.g. configuration of UEs, PC5 QoS enhancements) for supporting clock synchronization of a common working clock between a group of UEs using direct/indirect device connection ProSe communication.
  For all scenarios consider out-of-coverage, partial coverage and in-coverage cases.
  Coordination with RAN is expected (e.g. for QoS aspects)
  Expected TUs: 4 (3+1)

## Slide 5: Clock Synchronisation
Example case: Clock distribution via ProSe direct communication
  How UEs determine that 5GS clock or internal clock needs to be distributed over ProSe direct communication?
  Identify ProSe configuration enhancements to support clock distribution
  How is the 5GS clock (or internal clock) sent over ProSe direct communication (e.g. using a specific ProSe Identifier/Application ID?)
  Impacts on the ProSe layer (e.g. is there a need to define a layer above ProSe layer to provide clock reference information?)
  PC5 QoS parameters required to be supported for distributing clock information
  Whether a UE can use its internal clock for clock distribution (e.g. if UE(s) are out of coverage)

## Slide 6: TSC communication via ProSe direct connection
Example Case: ProSe direct communication is used to extend coverage to sent TSN stream to field devices
  When a ProSe UE (UE 1) supporting DS-TT receives TSN stream from CN how does the ProSe UE determine that the stream need to be send to a second UE (UE 2) supporting DS-TT over direct communication?
  Identify ProSe configuration enhancements to support TSC communication via ProSe direct communication
  How is the TSN stream sent over ProSe direct communication (e.g. using a specific ProSe Identifier/Application ID?)
  How ProSe UE determines PC5 QoS requirements over direct device connection for conveying TSN stream

## Slide 7
THANK YOU!