## Slide 1: Discussion on MBS service area update issue
Huawei, HiSilicon

## Slide 2
Background
In SA2 #158 meeting, SA2 reached some consensus and agreed to continue the work in SA2#159 meeting.
  Such information is reflected in S2-2309746 sent to SA6.
SA2 regards the scenario outlined by SA6 as an error scenario:
In 5MBS, an MBS service area in an MBS session create or update request is assumed to be within the same MB-SMF service area of a single MB-SMF.
If the AF requests an unacceptable service area (not entirely contained in a single MB-SMF service area), the session creation or update request may be rejected by the 5GC or may be accepted by the 5GC to handle only the acceptable part of the MBS service area (depending on further stage 2 discussion). It is expected that appropriate information about the acceptable or rejected parts of the service area will be defined and provided in the response to the AF in such situations.
SA2 intends to further refine the stage 2 TS 23.247 in future meetings to clarify this matter.
Highlights of the LS:
TBD in SA2 that whether the request is to be rejected or accepted.
Agreed that information containing service area (acceptable/rejected) provided to the AF.

## Slide 3
Problem statement
This scenario mainly happens for cross-domain case
MB-SMF 1
MB-SMF 2
MB-SMF 3
Same MB-SMF service area
MB-UPF 1
MB-UPF 2
MB-UPF 3
MB-UPF 3 is in the other domain
MB-SMF 4
MB-SMF 5
AF requested area
This case happens when the requested MBS service area from AF is crossing the domains.
  E.g., for the MBS Session, the serving MB-SMF is MB-SMF1, but AF requested MBS service area cannot be covered by MB-SMF1.
The issues to be further discussed:
  For TMGI allocation/Session Creation/Session Update, use reject or accept message in the response?
    Whether it should be NEF or MB-SMF to deal with the response?
    Whether the request session can be partially established if part of the request MBS service area can be supported by the MB-SMF?
    Should the returned MBS service area is the supported MBS service area, or non-supported one?

## Slide 4
Consideration
TMGI allocation
MBS session creation
MBS session update
NRF
NEF
2. Search MB-SMF
5. Find the request cannot be fulfilled
AF
1. TMGI allocation request (Service area)
3. Nnrf_NFDiscovery_Request request ()
4. Nnrf_NFDiscovery_Request response (Candidate MB-SMF, associated Service Area)
6. TMGI allocation response (error information, MBS service area can be fulfilled by one MB-SMF)
MB-SMF
NEF
AF
1. MBS session Creation (Case #1: MBS Session ID not included)
NRF
NEF
AF
See TMGI allocation part.
1. MBS session Creation (Case #2: MBS Session ID determined)
2. MBS session Creation request (MBS Session ID, MBS service area)
3. Find current MB-SMF cannot fulfill the request
4. MBS session Creation response (error information, MBS service area can be fulfilled by the MB-SMF)
1. MBS session Update (Case #2: MBS Session ID determined)
2. MBS session Update (MBS Session ID, MBS service area)
3. Find current MB-SMF cannot fulfill the request
4. MBS session Update response (error information, MBS service area can be fulfilled by the MB-SMF)
5. For the MBS service area can be covered, start

## Slide 5
Proposal
For the case when MBS session ID has not been determined:
  AF/NEF based on NRF’s feedback (including Candidate MB-SMFs and their associating service areas), to judge whether the request can be satisfied or not,
    No TMGI is allocated (i.e. procedure failed);
    Returned information include error information, MBS service area is fulfilled by one MB-SMF;
For the case when MBS session ID has been determined:
  MB-SMF based on its service area and the requested MBS service area, to justify whether the request can be satisfied or not.
    Procedure should be successful, and partial broadcast session established (i.e., established within the area can be supported);
    Error information would be provided;
    Supported area from MB-SMF will be provided.

## Slide 6
Thanks!